## Slide 1
S2E Design Plan
  Start with Matt’s layout
  Consider Cave1 + Cave2 constraints
  Use Elegant for initial spatial layout (X,Y,Z) and transverse optics (beam sizes in X, Y)
  Address longitudinal dynamics with GPT and Elegant
  Iterate
Cave 1
  POISSON to model gun and generate 350kV (Er,Ez)
  GPT to transform initial conditions to Elegant input at S=20cm
  Solenoids set waists at apertures (15 bend, Wien, Apertures, Cryounit)
  Chopper optics/layout constrained to 10mrad deflection
  Wien filter, chopper cavities, buncher and cryounit will get special component attention
  Beam exiting cryounit TBD : GPT, Elegant, Measurement, FEL model ?
  Quads set launch from Cave1 to Cave2
Cave 2
  Vertical chicane from cryounit CL 42” to HDIce CL 85-3/8”
  Quads compensate chicane dipoles and set size at HDIce
  Raster specs set distance range to target
  Limited space means good idea to thin about diagnostic + target + dump
UITC Optics Model Status as of July 28, 2014 (Grames/Wang)

## Slide 2
(Horizontal Bend)
(Vertical Bends)
Matt’s Layout

## Slide 3
As-found reference for Cave1 +Wall + Cave2

## Slide 4
Cave1 - 1497 MHz Chopper Cavity Conditions
300W
200W

## Slide 5
 | y [in] | y [cm] |  | 
Cryounit Height | 42.0000 | 106.6800 |  | 
HDIce Target Height | 85.3750 | 216.8525 |  | 
Difference | 43.3750 | 110.1725 |  | 
Beam Momentum [MeV/c] | 10.0000 |  |  | 
Vertical Bend Angle [deg] | [Rad] | delta-Z [cm] | BL[G-cm] | delta-S [cm]
30.0000 | 0.5236 | 190.8246 | 17266.3219 | 220.3452
35.0000 | 0.6109 | 157.3428 | 20060.6689 | 192.0800
40.0000 | 0.6981 | 131.2986 | 22816.8293 | 171.3981
45.0000 | 0.7854 | 110.1726 | 25529.5567 | 155.8075
50.0000 | 0.8727 | 92.4458 | 28193.6872 | 143.8201
55.0000 | 0.9599 | 77.1437 | 30804.1495 | 134.4959
60.0000 | 1.0472 | 63.6083 | 33355.9744 | 127.2163
Magnet Types | Function | Current Max [A] | Hyst Max [G-cm] | 
MBV | Existing 5MeV dipole | 3.5000 | 14833.0000 | 
MDL | New 5 MeV dipole | 10.0000 | ? | 
MBF | 123 MeV spectrometer | 60.0000 | 229144.0000 | 
MBL | 123 MeV chicance | 14.0000 | 50850.0000 | 
Cave2 - Vertical Chicane Geometry
delta-S
delta-Z
42”
85-3/8”
Maybe serves as the momentum spectrometer.
Thus, chose longer arm (smaller angle). 1mm/2203mm is 4.5E-4 (dp/p<0.05%)

## Slide 6
DS
Wien=0
Buncher
A1
A2
SRF1
SRF2
BL1
BL2
IBC_S
IBC_E
CAVE1
CAVE2
+5 QUADS (SOLID=OFF, DASHED=ON)
First pass Elegant layout – 350keV Gun to Dump
ex=ey=4E-8 (probably 2-3x too small)
dp/p = 1E-5 (OK at gun, not later…)

## Slide 7
Acceleration from 350 keV (0.69 MeV/c) to 10 MeV (10.5 MeV/c) ideally reduces transverse emittance by a factor of about 15. It is doubtful we’ll benefit this amount.
Normalized emittance should be constant. Measurement at CEBAF shows it isn’t and no measurement at 10 MeV (yet)
Options: use measurement; or simulation or model (if agrees with measurement). FEL … !?
P | bx (m) | ax | by (m) | ay | ex (norm) (mm-mrad) | ey (norm) (mm-mrad)
3.1 | 22.79 | -7.42 | 10.20 | -0.67 | 0.42 | 0.16
4.0 | 22.91 | -6.52 | 19.37 | -1.42 | 0.43 | 0.18
6.3 | 9.11 | -2.53 | 30.13 | -8.34 | 0.42 | 0.30
7.2 | 8.68 | -2.41 | 35.13 | -9.53 | 0.47 | 0.33
S2E probably means: S2E Cave1 + S2E Cave2, at least initially

## Slide 8
Importance of reasonable dp/p after cryounit
Increasing dp/p from Gun value (1e-5) to more typical – arguably challenging (0.5% = 5E-4)
(Vertical Bends)

## Slide 9
Floor coordinates of model can be generated and used to generate mechanical layout and answer questions related to construction of both caves.
If we want we can choose (X0, Y0, Z0) to be survey coordinates.
Keep in mind (X,Y,Z) are physical locations and (S) is distance beam travels, i.e S and Z are not the same.
Using Elegant model to generate/address mechanical layout

## Slide 10
Cave 1
  Add gun Twiss output from GPT
  Add generic hardware layout for better idea of layout and optical strengths needed
  Calculate options for existing Wien and upgrade Wien operating w/ 350keV beam
  Benchmark model of chopping optics with calculation
  Define input conditions to cryounit, i.e. final solution from Gun to Cryounit
  Update baseline optics in Elegant, make sure this makes sense
  Fold into GPT for longitudinal study => entering at 350keV vs. 550keV @ CEBAF
Cave 2
  Choose (extrapolate from measurement) reasonable cryounit output Twiss
  Optimize optics to reach 50-100 um spot size (do we speak 1-sigma, 4-sigma, 90% ?)
  Fold raster spec into layout
  Geant4 model to assess beam from HDIce to dump?
  Define BPM resolution to determine how far from target
  Define minimum “keep out” after HDIce for possible asymmetry detectors
  Fold into Elegant for transverse study
Proposed next steps…