## Slide 1
2015-LDRD-1a: Generation and Characterization of Magnetized Bunched Electron Beam from DC Photogun for JLEIC Cooler
JLEIC bunched magnetized electron cooler is part of Collider Ring and aims to maintain ion beam emittance and extend luminosity lifetime. Because the cooling rate is estimated to increase by two orders of magnitude in a solenoidal field, generating a magnetized electron beam (to avoid emittance growth when injecting into the solenoid) is desired.
LDRD Scientific Goals:
  Generate magnetized electron beam and measure its properties
  Explore impact of cathode magnet on photogun operation
LDRD Benefits:
  Simulations and measurements will provide insights on ways to optimize JLEIC electron cooler and help design appropriate electron source
  JLab will have direct experience magnetizing high current electron beam
PIs: Riad Suleiman and Matt Poelker

## Slide 2: Milestones
Year 1: Generate non-magnetized beam. Design, procure and install cathode magnet, pucks and slits. (nearing completion)
Year 2: Generate magnetized beam. Measure mechanical angular momentum and benchmark simulation.
Year 3: Measure photocathode lifetime vs magnetization up to 32 mA.

## Slide 3
Anode
K2CsSb
Photocathode
Cathode
Solenoid
(Bz=2kG)
Diagnostic Cross 1
(Slit + YAG Screen)
Three Skew Quads
(Round-to-Flat Beam Transformer)
Diagnostic Cross 2
(Slit + YAG Screen)
Diagnostic Cross 3
(YAG Screen)
Beamline
Focusing
Solenoid
Experimental Overview: Gun Test Stand
Generate magnetized beam:
  Laser size:1 – 5 mm, Bz = 0 – 2 kG
  Bunch charge: 1 – 500 pC
  Frequency: 15 Hz – 476.3 MHz
  Bunch length: 10 – 100 ps
  Average beam currents up to 32 mA
  Gun high voltage: 200 – 350 kV
Green
Laser

## Slide 4
K2CsSb Photocathode Preparation Chamber, Gun and Beamline: delivered 1 mA to dump (non-magnetized)
  Simulation (Fay Hannon):
  Used ASTRA and GPT simulation to design beamline and to locate magnets and diagnostics at optimum positions
  Simulated magnetized electron beam properties along beamline for various starting conditions
  Simulated a round to flat transformer
FY16 Accomplishments to date

## Slide 5
Cathode Solenoid Magnet
Magnet is now at JLab Magnet Measurement Facility to be mapped
New Pucks
  Designed to enhance magnetic field at cathode to 2.0 kG
Molybdenum
Steel
FY16 Accomplishments to date