## Slide 1: Description of Hardware of UITF 200 keV Mott DAQ
Riad Suleiman

## Slide 2: Upgraded Injector Test Facility – Mott data acquisition
BU-013-050-500
TID
Right (50˚)
Detector
Left (50˚)
Detector
142B
Preamp
VXS crate
SBC
E Out
570 Amp
Amp
Out
Fanout
SCA Out
OR
Mott
fADC
Amp
Out
Mott Trigger
INT
fADC
4 Helicity Signals
Helicity
Trigger
BU-013-050-1000-S
Right (120˚)
Detector
Left (120˚)
Detector
E Out
590A
Amp/Disc
142A
Preamp
4 Helicity Signals,
1 FC, 2 BPMs (X±, Y±)

## Slide 3: DAQ Hardware
Cable NIM Crate and VXS Crate
Cables from detectors to NIM Crate
Helicity signals from Helicity Board to VXS Crate

## Slide 4
Mott DAQ
Hardware | Rack
itfmdaq0 | ITF 07
Mott VXS Crate | 
Mott NIM Crate | 

## Slide 5
Mott DAQ crates
Slot | Board
1 | Linux SBC
2 | Empty
3 | TID
4 | Empty
5 | Empty
6 | Empty
7 | Mott FADC
8 | Empty
9 | Empty
10 | Empty
11 | Empty
12 | Empty
13 | Distribution Board
14 | Empty
15 | Empty
16 | INT FADC
17 | Empty
18 | Empty
19 | Empty
20 | Empty
21 | FT
Slot | Board
1 | 570 Amplifier
2 | 570 Amplifier
3-4 | ORTEC QUAD BIAS SUPPLY
5 | 590A Amplifier
6 | 590A Amplifier
7 | Empty
8 | Empty
9 | Empty
10 | QUAD GATE/DELAY GENERATOR PS794
11 | LEVEL TRANSLATOR
12 | LOGIC FAN IN/OUT LeCroy 429A
VXS Crate
Mott NIM Crate

## Slide 6: VXS CRATE
Itfsbcmdaq0 |  | TID |  |  |  | Mott FADC |  |  |  |  |  | Distribution Board |  |  | INT FADC |  |  |  |  | FT
itfmdaq0
TRG OUTPUTS
1
LN1
Delayed Helicity
T_Settle
Pattern Sync
Pair Sync
TM1
TRG
INPUTS
dECL-2
T_Settle

## Slide 7: Mott NIM Crate
570 Amp (50°) LEFT | 570 Amp (50°) RIGHT | ORTEC QUAD BIAS SUPPLY | 590A Amp (120°) LEFT | 590A Amp (120°) RIGHT |  |  |  |  | QD 794 | FAN 429A
→ IN E ← OUT E | → IN E ← OUT E | 142A Preamp (120°) LEFT +115 V | → IN E ← OUT E | → IN E ← OUT E |  |  |  |  | → nT_Settle ← 428 ns nT_Settle Trigger | → Delayed Helicity
 |  | 142A Preamp (120°) RIGHT +115 V |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | → T_Settle
 |  | 142B Preamp (50°) LEFT +115 V |  |  |  |  |  |  |  | → Pattern Sync
 |  | 142B Preamp (50°) RIGHT +115 V |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  | → Pair Sync

## Slide 8: CHANNEL ASSIGNMENT – TRIGGER INTERFACE (TID)
TID Chan | INPUTS
7 | 
6 | 
5 | 
4 | 
3 | TS#3 (DB MT1)
2 | 
1 | TS#1 (Mott DetTr)
0 | TRG ( Delayed nT_Settle)
INH | 
TID Chan | OUTPUTS
7 | 
6 | 
5 | 
4 | 
3 | 
2 | Distribution Board MT1
1 | 
0 | 

## Slide 9: CHANNEL ASSIGNMENT – PREAMPLIFIERS
OUTPUTS | 142A Preamp (120°) LEFT
E | 570 Amp E IN
T OUT | TID
OUTPUTS | 142A Preamp (120°) RIGHT
E | 570 Amp E IN
T OUT | TID
OUTPUTS | 142B Preamp (50°) LEFT
E | 590A Amp E IN
T OUT | -
OUTPUTS | 142B Preamp (50°) RIGHT
E | 590A Amp E IN
T OUT | -

## Slide 10: CHANNEL ASSIGNMENT – AMPLIFIERS
Channel | 570 Amp (120°) LEFT
E IN | 142A Preamp E
E OUT | Mott FADC CH0
Channel | 570 Amp (120°) RIGHT
E IN | 142A Preamp E
E OUT | Mott FADC CH1
Channel | 590A Amp (50°) LEFT
E IN | 142B Preamp E
E OUT | INT FADC CH0
SCA OUT | 
Channel | 590A Amp (50°) RIGHT
E IN | 142B Preamp E
E OUT | INTFADC CH1
SCA OUT | 

## Slide 11: FADC
FADC Chan | Signal
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | 
11 | Mott DetTr
12 | 
13 | Delayed Helicity
14 | T_Settle
15 | Pattern–Sync
16 | Pair–Sync
FADC Chan | Signal
1 | 
2 | 
3 | 
4 | 
5 | 
6 | 
7 | 
8 | 
9 | 
10 | Battery
11 | 
12 | 
13 | Delayed Helicity
14 | T_Settle
15 | Pattern–Sync
16 | Pair–Sync
Mott
INT