## Slide 1: Accelerator Parity Quality Beam
PQB To-do List

## Slide 2: Schedule
  PREx is tentatively scheduled for Hall A in May 2016.
  C-REx is tentatively scheduled for Hall A in Fall 2016.
  Møller is planned for Hall A in 2019.
  4-Hall operation and/or multiple A/B/C 5th pass requires 249.5 MHz bunch rep rate, and 2x charge density; approaches QWeak levels at injector.

## Slide 3: Upcoming Parity Violation Experiments
Experiment | Energy (GeV) | Pol (%) | I (µA) | Target | Apv (ppb) | Maximum Charge Asym (ppb) | Maximum Position Diff (nm) | Maximum Angle Diff (nrad) | Maximum Size Diff (δσ/σ)
PREx-II | 1.0 | 90 | 70 | 208Pb (0.5mm) | 500±15 | 100±10 | 1±1 | 0.3±0.1 | 10-4
C-REx | 2.2 | 90 | 150 | 48Ca (5mm) | 2000±42 | 100±10 | 1±1 | 0.3±0.1 | 10-4
Møller | 11.0 | 90 | 60 | 1H (150 cm) | 35.6±0.74 | 10±10 | 0.5±0.5 | 0.05±0.05 | 10-4

## Slide 4: Laser Table
Task | Sub Tasks | Date | Task Description
2 kHz Helicity Reversal |  | PREx | Requires 10 µs settle time – No ringing
 | RTP Pockels Cell |  | 
 | KD*P re-design |  | Model E-field to maximize PC uniformity, buy a properly engineered, one with the correct cell-diameter-to-laser-beam-diameter aspect ratio
Pockels Cell Stewart Platform |  | Fall 2015 | For remote optimization using e-beam

## Slide 5: Injector
Task | Sub Tasks | Date | Task Description
Improve 2-Wien Flip Optics |  | PREx | 
Injector Matching |  | PREx | Maximize damping
Helicity-correlated Beam Size Monitor |  | PREx | 
Upgrade Helicity Magnet controls |  | PREx | 
Locate Helicity Magnets to span (x,x') and (y,y') to minimize both position and angle |  | Fall 2015 | 
Augment helicity steering dipoles with helicity size quads |  | PREx | 
Share Injector apertures' current read-back with parity DAQ |  | Fall 2015 | 
Feedback to minimize transverse polarization |  |  | 

## Slide 6: Accelerator
Task | Sub Tasks | Date | Task Description
Study Depolarization at Higher Passes |  |  | 
 | Energy stability and precession to Hall |  | 
Synchrotron Radiation |  |  | 
 | Depolarization |  | 
 | Energy spread and energy tails |  | Clipping might be spin dependent
 | Polarization dependence |  | 
 | Adiabatic damping |  | 

## Slide 7: Hall A
Task | Sub Tasks | Date | Task Description
BCM Resolution |  |  | 
 | BCM Digital Receiver Bench studies |  | 
Beamline Instrumentation |  |  | 
Beam Polarimetry |  |  | 
Beam Matching and Optics |  |  | 
Phase Trombone |  |  | 

## Slide 8: PQB Beam Studies
Task | Sub Tasks | Date | Task Description
Injector |  |  | 
Accelerator |  |  | 
 | Energy spread in Hall A arc |  | 
 | Spin dance |  |