## Slide 1: Radiation Level at Positron Target Area
Distributions of positrons, electrons and photons at target in forward and backward directions (Geant4)
Energy spectra, phase-space and time distributions
Radiation levels near the target (FLUKA)
Comparison 60 MeV e+ with 10 MeV e+
A. Ushakov

## Slide 2: Primary Electron Beam and Target
Beam Energy: 120 MeV
Beam Current: 1 mA
Beam Size: σx = σy = 1 mm
No Energy Spread
No Beam Divergence
Beam Start at 10 mm from Target Exit Side
Target Material: Pure Tungsten
Target Thickness: 4 mm
Target Radius: 30 mm
Target Exit Side at Z = 0

## Slide 3: Yield, Energy and Power of Particles at Target (Geant4)
Forward Direction |  | 
Photon Yield | 7.5 | ph/e-
Average Energy of Photons | 7.9 | MeV
Average Power of Photons | 59.2 | kW
Electron Yield | 1.12 | e-/e-
Average Energy of Electrons | 35.2 | MeV
Average Power of Electrons | 39.3 | kW
Positron Yield | 0.24 | e+/e-
Average Energy of Positrons | 16.9 | MeV
Average Power of Positrons | 4.0 | kW
Total Power | 102.5 | kW
Backward Direction |  | 
Photon Yield | 0.39 | ph/e-
Average Energy of Photons | 1.03 | MeV
Average Power of Photons | 0.40 | kW
Electron Yield | 0.014 | e-/e-
Average Energy of Electrons | 2.18 | MeV
Average Power of Electrons | 0.03 | kW
Positron Yield | 0.001 | e+/e-
Average Energy of Positrons | 4.21 | MeV
Average Power of Positrons | 0.005 | kW
Total Power | 0.44 | kW
Power Deposition in Target | 16.84 | kW

## Slide 4: Positrons at Exit Side of Target: Phase Space and Y vs X
Phase Space
Number of primary electrons: 105
Y vs X
σx = 1.2 mm
Ye+ = 0.24 e+/e-
σx’ = 0.365
εnorm x = 14.7 mm·rad
Mean Ee+ = 16.9 MeV
εx = 0.43 mm·rad

## Slide 5: Positrons at Exit Side of Target: Energy vs Time
All Positrons
With 2 ps Time Cut
Ne+ = 22039
σE = 16.2 MeV
σt = 2 ps
Ne+ = 23769
σE = 16 MeV

## Slide 6: Positrons at Exit Side of Target: X vs Time
All Positrons
With 2 ps Time Cut
Ne+ = 22039
σx = 1.08 mm
σt = 2 ps
Ne+ = 23769
σx = 1.2 mm

## Slide 7: Positrons at Target Exit: Distribution of Energy
All Positrons
Mean Ee+ = 17.73 MeV with 2 ps time cut
2 ps Time Cut
Mean Ee+ = 16.89 MeV

## Slide 8: Electrons at Exit Side of Target: Phase Space and Energy Distribution
Phase Space
σx = 1.2 mm
Ye- = 1.12 e+/e-
σx’ = 0.334
Energy Distribution
Mean E = 31.2 MeV
σE = 28.3 MeV
εnorm x = 27.5 mm·rad
εx = 0.39 mm·rad

## Slide 9: Electrons at Exit Side of Target: X vs Time
All Electrons
With 2 ps Time Cut
Ne+ = 105181
σx = 1.1 mm
σt = 2 ps
Ne- = 111782
σx = 1.2 mm

## Slide 10: Photons at Exit Side of Target: Phase Space and Energy Distribution
Phase Space
σx = 1.5 mm
Nph = 745726
σx’ = 0.274
Energy Distribution
Mean E = 7.9 MeV

## Slide 11: Back-Scattered Photons: Phase Space and Energy Distribution
Phase Space
σx = 4.8 mm
Nph = 39061
σx’ = 0.52
Energy Distribution
Mean E = 1.0 MeV

## Slide 12: Distributions of Electrons and Positrons (FLUKA)

## Slide 13: Distributions of Photons and Neutrons (FLUKA)

## Slide 14: X vs Time for 603 MeV e+ and 103 MeV e+
Number of primary electrons: 107
60 MeV e+
10 MeV e+
σt = 0.14 ps
Ne+ = 26093
σx = 1.04 mm
σt = 0.4 ps
Ne+ = 481098
σx = 1.09 mm

## Slide 15: X’ vs Time for 603 MeV e+ and 103 MeV e+
60 MeV e+
10 MeV e+
σt = 0.14 ps
Ne+ = 26093
σx’ = 0.14
σt = 0.4 ps
Ne+ = 481098
σx' = 0.39

## Slide 16: Next Steps
Add magnetic field(s)
Track positrons and electrons
Find optimal field distribution(s) for 60 MeV and 10 MeV positrons
Calculate energy deposited by beams in magnet