## Slide 1: DAQ Speed and Run2 Estimates
April 3, 2015

## Slide 3: Estimates Assumptions
DAQ Rate limit = 2 kHz, Deadtime = 15%
Dump rate = 100 Hz/µA per detector:
  Measured during Run1 5 MeV data at
  Discriminator Threshold was 25 mV (or energy of about 1.25 MeV)
  Dump Dipole Magnet was at +5A

## Slide 4
3 MeV
5 MeV
8 MeV

## Slide 5: Dump Event Suppression
Increase Discriminator Threshold – Tested in Run1
Study Dump dipole (+5A, 0A, +5A) – Tested in Run1 (for thinner foils, 0A or -5A may yield lower dump rate)
Laser timing veto – Tested on February 9, 2015
Note: Dump rate depends on electron energy ( ̴1/E)

## Slide 6: Run2 Strategy
At 3 MeV:
  Dump events will be higher due to energy
  Increase Discriminator Threshold
  Thick foils will benefit from faster DAQ but very little reduction in overall time required for Run2. Here DAQ speed will help with systematic studies, e.g., many short runs with very high statistics for stability study.
At 8 MeV:
  Dump events will be lower due to energy
  Elastic rate is too low to benefit from faster DAQ
  Suppress dump events will reduce deadtime
  Will run at about 5 µA (31 MHz) for all foils (current limited)
What is a reasonable current limit? Run1 was 5 µA

## Slide 7: summary of FADC development for faster performance

## Slide 9: remaining challenges & plans