## Slide 1
300 kV DC High Voltage Gun with Inverted Insulator Geometry & CsK2Sb Photocathode
Y. Wang, P. Adderley, B. Bullard, J. Benesch, J. Grames, F. Hannon, C. Hernandez-Garcia, J. Hansknecht,
G. Krafft, R. Kazimi, M. Poelker, M. A. Mamun, G. Palacios, R. Suleiman, M. Tiefenback, S. Wijethunga, S. Zhang
Thomas Jefferson National Accelerator Facility
Acknowledgement: This work is supported by the Department of Energy under contract DE-AC05-06OR23177. Additional support comes from Laboratory Directed Research and Development program.
Designed & built compact DC gun with inverted insulator geometry; HV conditioned gun using Kr gas; operated reliably at 300 kV.
Conducted beam emittance studies.
Low normalized emittances:
~0.1 mm mrad at 0.2 mm laser
rms size and 18 fC bunch charge;
warrants more study
CsK2Sb photocathode is robust: less sensitive to ion bombardment
but expected longer lifetime
Make CsK2Sb photocathodes with different thickness Sb layers
Quantify how surface roughness
of the photocathode affects beam
emittance.
Summary & Plan
Compact DC Gun / Inverted Insulator
Insulator / Shed
Insulator is 97% purity alumina, ~7- inch long. Electric field strength at triple point junction is very
high, up to 100 MV/m, when gun biased to 300 kV
Shed lowers the field and protects triple point junction, also linearizes potential along insulator
Five-Meter Beamline
Gun chamber
Lenses & correctors
Harp & viewers
Vacuum pumps & dump
Low Field Emission after HV Conditioning
Required 150 hours to condition gun
Conditioned with krypton to 350 kV
Operated at 300 kV with minimal field emission
Beam Profile
Beam profiles were measured using YAG viewer
and wire scanner with low duty factor tune beam.
Photocathode Lifetime
Photocathode lifetime was measured using 4.5 mA
CW beam for several hours, Lifetime 164 C
CsK2Sb Photocathode
Photocathodes were made in-house: first deposit Sb layer on substrate, then co-deposit Cs and K while monitoring QE. Mask is used to control active photocathode area. Transfer photocathode to gun chamber prior to use
Introduction
The goal of this project is to develop a reliable, compact 300 kV DC high voltage photogun that operates with alkali-antimonide photocathodes, and to characterize beam quality. Inverted insulator and spherical cathode electrode with shed are the key design features. Preliminary studies show very promising results: gun operates reliably at 300 kV; shed protects triple point junction; alkali-antimonide photocathodes are less sensitive to ion bombardment than GaAs; beam emittance is low compared to published data.
Beam Operations
Operates at 300 kV
14-month period
1400 hrs beam time
New design employs inverted-insulator
geometry, which reduces interior surface area
Beam Emittance Studies
Beam emittance was calculated by varying lens strength and measuring corresponding beam sizes. Studies were conducted under different conditions: varying gun high voltage, laser size, laser position on photocathode, electron beam current. Emittance near damaged spot was also studied.
Prep chamber / Puck / Active area / damaged spots / QE map
Old gun design
New Design
Insulator
Simulation
Poisson & COMSOL are used to simulate electric field and potential
Triple point junction
Shed
<10 MV/m
> 100 MV/m
Chart: Potential along Insulator Surface
Linear_line | -300 | 0
Chart: Normalized Emittance vs Gun HV
| 50 | 100 | 150 | 200 | 230 | 250 | 300
X | 0.2139 | 0.1671 | 0.0996 | 0.1451 | 0.1232 | 0.1432 | 0.1412
y | 0.1746 | 0.1305 | 0.1134 | 0.1281 | 0.1171 | 0.1357 | 0.1311
Chart: Normalized Emittance vs Bunch Charge
| 8.9067022934758402 | 17.81340458695168 | 26.720106880427519 | 35.626809173903361 | 53.440213760855038 | 71.253618347806722
x | 0.1089 | 0.1009 | 0.1057 | 0.1209 | 0.1504 | 0.1626
y | 0.0877 | 0.0851 | 0.0889 | 0.0992 | 0.1185 | 0.1535
Chart: Normalized Emittance vs Beam Current
| 3 | 6 | 9 | 12 | 15 | 20
x | 0.1089 | 0.1009 | 0.1057 | 0.1209 | 0.1504 | 0.1626
y | 0.0877 | 0.0851 | 0.0889 | 0.0992 | 0.1185 | 0.1535
Chart: Normalized emittance vs Laser Position along Y Axis
| -4 | -2 | -0.5 | 0 | 0.5 | 2 | 3.5 | 5
x | 0.144 | 0.0861 | 0.1009 | 0.0717 | 0.094 | 0.0824 | 0.1021 | 0.1647
y | 0.134 | 0.0882 | 0.0851 | 0.0838 | 0.094 | 0.0859 | 0.108 | 0.1938
x_GPT | 0.07611 | 0.07673 | 0.0777 | 0.07658 | 0.07387 | 0.07251 | 0.07227 | 0.07234 | 0.07248 | 0.07249 | 0.07248 | 0.0723 | 0.07222 | 0.07216 | 0.07214 | 0.07209 | 0.07212 | 0.0721 | 0.07212 | 0.07208 | 0.07204 | 0.07207 | 0.07207 | 0.07208 | 0.07215 | 0.07213 | 0.07209 | 0.07205 | 0.07211 | 0.07211 | 0.07206 | 0.07204 | 0.07204 | 0.07204 | 0.07208 | 0.07215 | 0.07227 | 0.07234 | 0.07225 | 0.07211 | 0.07219 | 0.07223 | 0.07229 | 0.07246 | 0.07218 | 0.07299 | 0.07468 | 0.07653 | 0.07597 | 0.07495 | 0.0757
y_GPT | 0.1504 | 0.1048 | 0.09865 | 0.1084 | 0.09824 | 0.0866 | 0.08483 | 0.08504 | 0.08543 | 0.08597 | 0.0855 | 0.08459 | 0.08417 | 0.08397 | 0.08379 | 0.08428 | 0.08424 | 0.08448 | 0.08426 | 0.08422 | 0.08407 | 0.08411 | 0.08409 | 0.08419 | 0.08423 | 0.08419 | 0.08414 | 0.08395 | 0.08414 | 0.08413 | 0.08404 | 0.08411 | 0.08393 | 0.08393 | 0.08416 | 0.0842 | 0.08364 | 0.08464 | 0.08446 | 0.08417 | 0.08493 | 0.08548 | 0.08475 | 0.08485 | 0.07521 | 0.08758 | 0.09376 | 0.09889 | 0.09331 | 0.1052 | 0.1544
Chart: Normalized Emittance vs Laser Size
| 0.157 | 0.2 | 0.24299999999999999 | 0.3 | 0.34399999999999997
x | 0.0596 | 0.1009 | 0.1064 | 0.1444 | 0.165
y | 0.072 | 0.0851 | 0.0965 | 0.135 | 0.1629
Chart: Normalized Emittance vs Laser Position along X Axis
| -5 | -3.5 | -2 | -0.5 | 0 | 0.5 | 2 | 3.5 | 5
x | 0.0696 | 0.0768 | 0.08 | 0.0759 | 0.0717 | 0.0835 | 0.0811 | 0.0911 | 0.1058
y | 0.0882 | 0.0898 | 0.0831 | 0.0828 | 0.0838 | 0.0777 | 0.0766 | 0.0921 | 0.1079
x_GPT | 0.1099 | 0.0815 | 0.08829 | 0.09953 | 0.08966 | 0.07636 | 0.07305 | 0.0729 | 0.07302 | 0.07383 | 0.07319 | 0.07242 | 0.07216 | 0.07284 | 0.07239 | 0.07205 | 0.07196 | 0.0722 | 0.07199 | 0.07192 | 0.07217 | 0.07198 | 0.07217 | 0.07207 | 0.07213 | 0.07213 | 0.07208 | 0.07207 | 0.07203 | 0.07213 | 0.07238 | 0.0724 | 0.07205 | 0.07212 | 0.07212 | 0.07273 | 0.07267 | 0.07303 | 0.07268 | 0.07233 | 0.07255 | 0.07478 | 0.0769 | 0.07476 | 0.07356 | 0.0733 | 0.08089 | 0.09913 | 0.09704 | 0.08928 | 0.1179
y_GPT | 0.08799 | 0.08628 | 0.08554 | 0.0851 | 0.0849 | 0.08474 | 0.08459 | 0.08444 | 0.08427 | 0.08427 | 0.08432 | 0.08441 | 0.08436 | 0.08419 | 0.08401 | 0.08406 | 0.08399 | 0.08397 | 0.08403 | 0.08405 | 0.08408 | 0.08412 | 0.08416 | 0.08416 | 0.08421 | 0.08419 | 0.08414 | 0.08415 | 0.0841 | 0.08417 | 0.0842 | 0.08424 | 0.08421 | 0.08404 | 0.08404 | 0.08413 | 0.0842 | 0.08423 | 0.08417 | 0.0842 | 0.08417 | 0.0843 | 0.08459 | 0.08476 | 0.08449 | 0.08434 | 0.08457 | 0.08552 | 0.08766 | 0.08947 | 0.0897