## Slide 1
Polarized Positron Beam
R&D at Jefferson Lab
Larry Cardman1, Joe Grames1, Michael Tiefenback1, E. Voutier2
1 Thomas Jefferson National Accelerator Facility
2 Institut de Physique Nucléaire d’Orsay
Polarized positron production
The PEPPo experiment
PEPPo based Positron Source
Positrons at CEBAF
Notes: INJECTOR SCIENTIST AT JEFFERSON LAB
WOULD LIKE TO TELL YOU ABOUT A SMALL EXPERIMENT WE PERFORMED TO PRODUCE POLARIZED POSITRONS AT LOW ENERGY
WILL GET TO THIS COMMENT AT THE END

## Slide 2
2
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
Polarized Bremmstrahlung and Pair Creation
Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)
Notes: THE PEPPO METHOD IS PRETTY STRAIGHT-FORWARD
FIRST STAGE IS POLARIZED BREMMSTRHALUNG
SECOND STAGE IS POLARIZED PAIR CREATION
THIS COULD BE DONE IN SEPARATE TARGETS, BUT CONVENIENTLY ALSO IN ONE SINGLE TARGET
WE LEARNED EARLY ON THE CALCULATIONS OF OLSON/MAXIMON WERE NOT CORRECT AT LOW ENERGY, ESPECIALLY PAIR CREATION
NEW CALCULATIONS WERE DONE, THAT AGREE W/ OM AT HIGHER ENERGIES
WE WERE NOT FIRST TO PROPOSE THIS IDEA, SO WHY NOT BEFORE…

## Slide 3
J. Grames, E. Voutier et al., JLab Experiment E12-11-105 (2011)
The purpose of the PEPPo (Polarized Electrons for Polarized Positrons) experiment at the CEBAF Injector was to demonstrate the feasibility of using bremsstrahlung radiation of MeV energy Polarized Electrons for the efficient production of Polarized Positrons.
Polarized Electrons for Polarized Positrons

## Slide 4
BREMSSTRAHLUNG
Longitudinal e- (Pe-) produce elliptical g whose circular (Pg) component is proportional to Pe-
COMPTON TRANSMISSION
Polarized e+ convert into polarized g (Pg) whose transmission through a polarized iron target (PT) depends on Pg.PT
PAIR PRODUCTION
In the same target, g produce e+e- pairs and transfer Pg into longitudinal (Pe+) and transverse polarization averages to zero
Pe-
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
S1
D
D
S2
Pe+
Positron Transverse and Momentum Phase Space Selection
e+
T2
PT
Calorimeter
Compton Transmission Polarimeter
Ee = 6.3 MeV
Ie = 1 µA
T1 = 1 mm W
Geant4
PEPPo
J. Dumas, PhD Thesis (2011)
PEPPo measured the longitudinal polarization transfer from 8.25 MeV/c e- to e+ in the 3.07-6.25 MeV/c momentum range.
PEPPo Principle of Operation

## Slide 5
Two NaI detectors measured coincidence of back-to-back photons emitted by annihilation of positrons in a viewscreen.
4 MeV/c e+
Positron ID and Yield
T1
T2
S1
S2
D
D
e+
e-
pe-= 8.2 MeV/c
e+
10-5 e+/e-

## Slide 6
Compton Polarimeter Energy & Timing Spectra
The location of the 511 keV peak is an in-situ monitor of the gain of the detection chain and provides a link to radioactive source calibration data.
Compton physics asymmetries are obtained from the polarization sensitive energy deposition in the central crystal.
The coincidence time between the central crystal and a charge sensitive trigger scintillator allow for accidental subtraction.

## Slide 7
The experimental Compton asymmetry for a known polarized electron beam provides a measurement of the electron analyzing power (Ae) of the polarimeter.
A comparison between the experimental and the GEANT4 simulated response of the polarimeter establishes a calibrated model of the polarimeter.
The positron analyzing power (Ap) is then determined by simulation using the calibrated model.
Target polarization
Electron beam polarization
Electron-to-positron
polarization transfer
PT = 7.06% ±0.05%Sta.± 0.07%Sys.
A. Adeyemi (Hampton University)
Compton Transmission Analyzing Power

## Slide 8
PEPPo Result
PEPPo demonstrated efficient polarization transfer from 8.2 MeV/c electrons to positrons, expanding polarized positron production to MeV electron beam energies.
(PEPPo Collaboration) D. Abbott et al. , Phys. Rev. Lett. 116 (2016) 214801
electron beam polarization
85.2 ± 0.6 ± 0.7 %
Whenever producing e+ from e-, polarization is coming for free
if initial electrons are polarized.

## Slide 9
P. Adderley1, A. Adeyemi4, P. Aguilera1, M. Ali1, H. Areti1, M. Baylac2, J. Benesch1,
G. Bosson2, B. Cade1, A. Camsonne1, L. Cardman1, J. Clark1, P. Cole5, S. Covert1,
C. Cuevas1, O. Dadoun3, D. Dale5, J. Dumas1,2, E. Fanchini2, T. Forest5, E. Forman1,
Freyberger1, E. Froidefond2, S. Golge6, J. Grames1, P. Guèye4, J. Hansknecht1,
P. Harrell1, J. Hoskins8, C. Hyde7, R. Kazimi1, Y. Kim1,5, D. Machie1, K. Mahoney1,
R. Mammei1, M. Marton2, J. McCarter9, M. McCaughan1, M. McHugh10, D. McNulty5, T. Michaelides1, R. Michaels1, C. Muñoz Camacho11, J.-F. Muraz2, K. Myers12,
Opper10, M. Poelker1, J.-S. Réal2, L. Richardson1, S. Setiniyazi5, M. Stutzman1,
R. Suleiman1, C. Tennant1, C.-Y. Tsai13, D. Turner1, A. Variola3, E. Voutier2,11,
Y. Wang1, Y. Zhang12
1 Jefferson Lab, Newport News, VA, US 2 LPSC, Grenoble, France 3 LAL, Orsay, France
4 Hampton University, Hampton, VA, USA 5 Idaho State University & IAC, Pocatello, ID, USA
6 North Carolina University, Durham, NC, USA 7 Old Dominion University, Norfolk, VA, US
8 The College of William & Mary, Williamsburg, VA, USA 9 University of Virginia, Charlottesville, VA, USA 10 George Washington University, Washington, DC, USA 11 IPN, Orsay, France
12 Rutgers University, Piscataway, NJ, USA 13 Virginia Tech, Blacksburg, VA, USA
Many thanks for support from SLAC E166, DESY, Princeton, Cornell, International Linear Collider Project and Jefferson Science Associates
PEPPo Collaboration

## Slide 10
R. Dollan, K. Laihem, A. Schälicke, NIM A 559 (2006) 185, J. Dumas, J. Grames, E. Voutier, JPos09, AIP 1160 (2009) 120, J. Dumas, Doctorate Thesis (2011)
Optimum energy
Optimum
FoM
The polarization distribution of generated positrons is typical of bremsstrahlung induced pair creation with a production rate dominated by low-energy particles.
The positron energy at optimum FoM is about half of the electron beam energy.
Figure of Merit

## Slide 11
J. Dumas, Doctorate Thesis (2011)
Simplistic, but reasonable, collection cuts on momentum dp/p<10% and emission angle<10° mimic the acceptance and define source performance.
In the 10-100 MeV energy range one can estimate at the optimum FoM
  conversion efficiency e of about 10-5 - 10-3 e+/e-
  electron polarization transfer at optimum FoM is approx flat at 75%
FoM vs. CEBAF Injector Beam Energy

## Slide 12
The JPos17 International Workshop, to be held mid-september at the Jefferson Laboratory, intends to review the scientific and technological bases for polarized and unpolarized positron beams in the context of CEBAF 12 GeV, JLEIC, and low energy applications.
The JPos17 and JLab Positron Working Group efforts will serve as a basis for the a White Paper on Positron Physics at JLab.
wiki.jlab.org/pwg pwg@jlab.org
www.jlab.org/conferences/JPos2017
Please Join Us !!
JPos17 Sep 12-15 @ Jefferson Lab

## Slide 13
A Polarized Positron Source at CEBAF
Many factors can drive the solution (I challenge you … put three people in a room for 30 min and you’ll come up with 4 or 5 approaches!)
  Positron yield goes like the beam power
  A lower energy electron drive beam will require higher beam current, however, offers greater access selecting a compromise between positron polarization and beam intensity than a ‘hotter’ positron beam produced by high energy e- beam.
One possible solution would employ the CEBAF Full Energy Injector ~123 MeV to produce positrons.
  Collecting ~60 MeV e+ (optimum FoM) with ~few 10-4 e+/e- efficiency suggests that 100’s of microAmp or perhaps 1 milliAmp polarized e- beam and a high power converter (>100’s kW beam power) is required to produce a positron beam intensity Ie+ > 100 nA with a positron polarization Pe+ > 65%.

## Slide 14
QE ~ 5%, 30 mA/W
Pol ~ 35% @ 780 nm
Bulk GaAs
QE ~ 0.2%, 1 mA/W
Pol ~ 75% @ 850 nm
Strained GaAs:
GaAs on GaAsP
100 nm
Superlattice GaAs:
Layers of GaAs on GaAsP
QE ~ 1%, 6 mA/W
Pol ~ 85% @ 780 nm
100 nm
14 Layers
2 μm
350 μm
625 μm
CEBAF GaAs Photocathode Evolution
Spin Polarized Electron programs (particularly PV Users) have
driven the need for improved performance over last 20+ years
Pe- 35% 35% 75% 75% 85% 89%
Ie- 30mA 100mA 50mA 100mA 150mA 200mA
1995 1998 1999 2000 2004 2012 2016
Notes: FOR US AT JLAB, HOWEVER, SAW THIS AS AN OPPORTUNITY TO EXPLOIT WHAT WE’VE BEEN DOING W/ POLARIZED E- BEAMS FOR TWO DECADES
OVER THAT TIME THE SPIN PROGRAM HAS DRIVEN IMPROVEMENT
GAAS PHOTOCATHODES THAT BREAK DEGENERACY, YET RETAIN HIGH QUANTUM EFFICIENCY
THIS MEANS HIGH SPIN POLARIZATION (85%) AND HIGH QE (>1%)
LEARNING HOW TO SUSTAIN THIS FOR LONG PERIODS MAKES THIS VIABLE

## Slide 15
High current (1-10 mA) studies with low-P photocathodes demonstrated that charge lifetime is improved by increasing laser spot size (spreading out ion damage).
Measurements are underway using the CEBAF polarized source to characterize lifetime vs. spot size with high-P (>85%) photocathodes.
CEBAF Polarized Inverted Load Lock Gun
1mA
Slope is proportional to QE Decay
Increasing laser size reduces QE decay proportionally
Phys. Rev. ST Accel. Beams 14, 043501 (2011)
Lifetime studies at mA Beam Current

## Slide 16
Polarization Studies at mA Beam Current
Chart: Polarization (%)
| 1.67 | 10.4 | 50.5 | 100.5 | 250.5 | 504.0 | 755.0 | 1011.0 | 1.06
 | 85.6704 | 84.5218 | 84.3896 | 85.3479 | 84.9536 | 86.116 | 84.7714 | 85.9647 | 87.1486
For the first time, the spin polarization of a high-P superlattice photocathode is measured directly from low to milliAmpere intensity.
CEBAF Mott Polarimeter
The spin polarization of a high current (mA) beam is measured at CEBAF by extracting and accelerating a small fraction of the beam to a sub-percent accuracy Mott polarimeter.

## Slide 17: High Polarization Photocathode R&D
GaAs/GaAsP superlattice photocathode with GaAsP/AlAsP Distributed Bragg Reflector (DBR)
The highest QE & FOM of any reported high polarization photocathode
Paper ready for APL submission: W. Liu, S. Zhang, M. Stutzman, M. Poelker, Y. Chen, W. Lu, and A. Moy
DBR Stack
Substrate
SLSP
Photocathode
CEBAF
DBR (R&D)

## Slide 18
High Power Target R&D
Stainless Steel Windows (0.25mm)
LBE (2mm)
Input (e-)
Output (e-,e+,γ)
Liquid Metal Target – lead-bismuth eutectic (LBE)
  High Z = 82, 83
  Low melting point: 124°C
  High boiling point: 1670°C
Multiple LBE targets tested on various accelerators
  Natural Circulation
  Mechanical Pumping
  Electromagnetic Pumping
Approaching 10 kW power level, CW
Slide courtesy of James McCarter

## Slide 19
Summary
The PEPPo technique provides access to highly spin-polarized positrons in a reliable, radioactive-less, and low-cost method, opening access to a wide community.
A high-energy polarized positron beam program in the context of CEBAF 12 GeV (and JLEIC) based on the PEPPo technique is being explored.
Your attendance and input at JPos17 is welcomed, please visit: https://www.jlab.org/conferences/JPos2017/
If you would like to participate in the newly formed Jefferson Lab Positron Working Group please visit: wiki.jlab.org/pwg

## Slide 20
Back Up Slides

## Slide 21
P(e+) = 73 ± 15(stat) ± 19(syst) %
Compton Backscattering (KEK)
T. Omori et al, PRL 96 (2006) 114801
Helical Undulator (SLAC E166)
G. Alexander et al, PRL 100 (2008) 210801
P(e+) = 80 ± 7(stat) ± 9(syst) %
47.7GeV
Polarized b+ Decay
L.A. Page & M. Heinberg. Phys. Rev.
106(6):1220-1224 (1957)
Polarized due to parity non-conservation in the weak interaction
P(e+) ~ 40 %
Sokolov-Ternov Effect
D. Barber , AIP Conf. Proc. 588, 338 (2001)
HERA 27.5 GeV e+/e-
P(e+) ~ 70 %
Collecting Polarized Positrons
Notes: TO PROVIDE SOME CONTEXT, POLARIZED POSITRONS CAN BE COLLECTED IN A NUMBER OF WAYS
BETA DECAY – WEAK INTERACTION (NOT EFFICIENT FOR RF ACCEL)
ST – QUANTUM EMISSION OF SYNC. RAD. (NOT COMPATIBLE W/ CW BEAM)
PAIR PRODUCTION BY POLARIZED GAMMAS (PLAUSIBLE, BUT HIGH TECHNICAL CHALLENGE – INTENSE LASERS, HIGH ENERGY BEAMS)
WE WONDERED IF WE COULD SIMPLY USE OUR POLARIZED ELECTRON BEAM

## Slide 22
PEPPo ran at the CEBAF injector, taking advantage of the existing beam diagnostics that determine with precision the properties of the polarized electron beam entering the PEPPo apparatus.
Polarization controls
    30 Hz fast heilicity reversal (delayed)
    Slow laser polarization reversal (half-wave plate)
    4p spin rotator
Variable energy
3.1-8.2 MeV/c
Polarization measurement
dP/P < 2%
Energy measurement
dp/p < 0.5%
PEPPo
Laser
Intensity controls
10 pA – 1 µA
CEBAF Polarized Electron 10 MeV Injector

## Slide 23
Positron Yield using 10 MeV Electrons
>100nA e+ at IP2 for CEBAF => >1.0 milliAmp e- beam
Electro-magnetic Shower
e+ yield ~ e- beam power (E*I)
High Z-target increases yield
Operate at low energy below photo-neutron threshold to mitigate radioactivity
10 MeV e- shower
e+/e- yield ~ 0.1 % (optimized)
Collection efficiency ~ 1-10 %

## Slide 24: Polarized Positrons at JLEIC
A pulsed positron beam with low average current (>10 nA) is required for injection into JLEIC with a reasonably short injection time (minutes) and reasonably high equilibrium polarization (>40%).
A group (J. Grames, J. Guo, F. Lin, V. Morozov, E. Voutier, Y. Zhang) is exploring a polarized positron injector suitable for Jefferson Lab Electron Ion Collider (JLEIC).
L ≥1033cm-2s-1 Pe+≥40%
(An Early Career Award proposal will be submitted.)
35 s
68.1 MHz bunch train, 1.6 us
110 bunches (I = 4.6 uA)
67 fC
1.05 ms
20 ms
~ 50 Hz, Iave= 10.5 nA
…
×30
Bunch structure from an e+ injector:
J. Grames, SPIN 2016 @ UIUC, Sep 26-30 2016
24
e+

## Slide 25: JLEIC/CEBAF Positron Injector
10 MeV polarized e-
1.33 pC @ 1500 MHz
10 MeV pol e-
0.67 nC bunches
@ 1500 MHz
500-Turn
Accumulator Ring
(22m)
Bunch
Management
10 MeV polarized e-
0.67 nC @ 68.1 MHz
Positron Conversion/Collection Efficiency ~ 10-4
5-7 MeV Polarized e+
67 fC @ 68.1 MHz
to CEBAF/JLEIC
Harmonic
Extraction Ring
(22m)
 | Polarized Electron Source | Accumulator/ Extractor Rings | Electrons at Converter | Polarized Positron Source | R&D Challenge
JLEIC | Ave = 100 mA 1.33 pC @ 1500 MHz 2 mA w/ DF=5% | Ave = 1 A 1500 MHz | Ave = 100 uA 68.1 MHz 44 mA @ DF=0.23% | Ave = 10 nA 68.1 MHz 4.4 uA @ DF = 0.23% | Electron accumulator Harmonic extraction Target: 440 kW peak
CEBAF | Ave = 1-10 mA 4-40 pc @ 250 MHz (cw) | Not Necessary | Ave = 1-10 mA 250 MHz (cw) | Ave = 100 nA - 1 mA 250 MHz (cw) | High-QE photocathode High voltage gun Target: 10-100 kW ave
Polarized
Electron
10 MeV Injector
J. Grames, SPIN 2016 @ UIUC, Sep 26-30 2016
25
Slide courtesy of Fanglei Lin