## Slide 1: Parity Quality Beam (PQB) Working Group Report
OPS StayTreat
Riad Suleiman
Friday July 17, 2015

## Slide 2: Upcoming Parity Violation Experiments
Experiment | Energy (GeV) | Pol (%) | I (µA) | Target | Apv (ppb) | Maximum Charge Asym (ppb) | Maximum Position Diff (nm) | Maximum Angle Diff (nrad) | Maximum Size Diff (δσ/σ)
QWeak (Achieved) | 1.155 | 89.0 | 180 | 1H (35 cm) | 281±46 | 8±15 | 5±1 | 0.1±0.02 | 10-4
PREx-II | 1.0 | 90 | 70 | 208Pb (0.5mm) | 500±15 | 100±10 | 1±1 | 0.3±0.1 | 10-4
C-REx | 2.2 | 90 | 150 | 48Ca (5mm) | 2000±42 | 100±10 | 1±1 | 0.3±0.1 | 10-4
MOLLER | 11.0 | 90 | 60 | 1H (150 cm) | 35.6±0.74 | 10±10 | 0.5±0.5 | 0.05±0.05 | 10-4
  PREx-II is tentatively scheduled for Hall A in 2017
  C-REx is tentatively scheduled for Hall A in 2017
  MOLLER is planned for Hall A in 2022

## Slide 3: Issues from QWeak
  Beam Halo: there was beam halo that could develop a large helicity-correlated charge asymmetry
    Beam halo charge asymmetry was found to depend on:
    Beam loss at Injector Apertures
    Laser phase
    Machine tuning
    What can we do to help?
  BCM Resolution is not suitable for MOLLER:
    QWeak achieved 65 ppm but MOLLER requires 10 ppm
    BCM digital receiver bench studies found that local oscillator phase and amplitude noise is a likely cause of 65 ppm noise floor
    Try new digital receivers
    Improve phase/amplitude noise of local oscillator

## Slide 4: Hall A 2015/2016 Beamline Plan for PQB
  Install QWeak halo monitor in Hall A beamline
  Equip two BCMs with new-style digital receivers
  Install QQQ cavity triplet in Hall A beamline
  Reinstate Hall A beam modulation system (air-core coils and associated control/drive electronics)
    Beam modulation and accelerator Fast Feedback: is there a need to pause FFB when modulation is ON? does FFB implement a digital notch filter to attenuate modulation frequency (QWeak: 125 Hz for 20 s every 320 s) while passing all other frequencies?
    Need software support
To be ready for beam studies this Fall

## Slide 5: Synchrotron Radiation @ 11 GeV
  Total synchrotron radiation (SR)
  power (integrated over solid angle):
  Energy loss per electron per Arc:
  Eloss [MeV] = 0.04423 E4 [GeV] / ρ[m]
Area | ρ (m) | Energy Loss (MeV)
Arc 1 | 5.09 | 0.019
Arc 2 | 10.2 | 0.122
Arc 3 | 10.2 | 0.576
Arc 4 | 20.4 | 0.878
Arc 5 | 20.4 | 2.095
Arc 6 | 30.6 | 2.851
Arc 7 | 30.6 | 5.220
Arc 8 | 30.6 | 8.818
Arc 9 | 30.6 | 14.000
Hall A Arc | 40.1 | 3.070
Total |  | 38 MeV
Energy gain per
Linac is 1090 MeV

## Slide 6
106 electrons at 10 GeV, Arc 9: ρ=30.6 m
Average of n=647 photons per electron, each =22.33 keV
Energy spread due to SR in Arc 9
No non-gaussian tails since number of photons per electron per Arc is large ( [GeV])
  Simple GEANT4 Model:

## Slide 7
  Transverse Geometric Emittance and Energy Spread:
Area | Δp/p (10-3) | g,x (nm) | g,y (nm)
Inj Chicane | 0.5 | 4.00 | 4.00
Arc 1 | 0.05 | 0.41 | 0.41
Arc 2 | 0.03 | 0.26 | 0.23
Arc 3 | 0.035 | 0.22 | 0.21
Arc 4 | 0.044 | 0.21 | 0.24
Arc 5 | 0.060 | 0.33 | 0.25
Arc 6 | 0.090 | 0.58 | 0.31
Arc 7 | 0.104 | 0.79 | 0.44
Arc 8 | 0.133 | 1.21 | 0.57
Arc 9 | 0.167 | 2.09 | 0.64
Arc 10 | 0.194 | 2.97 | 0.95
Hall D | 0.18 | 2.70 | 1.03
Damping
Synchrotron
Radiation
Values are calculated at start of each Arc
Energy spread in Hall A is
Provided by Yves

## Slide 8
  What are the issues? Any polarization dependencies?
    Yves to implement an ELEGANT model to calculate spin precision with SR included – standard 6 GeV formula will not work
    Adiabatic Damping: amplitude of betatron oscillations (e.g., helicity-correlated position and angle differences etc.) is still damped by square root of ratio of momenta
    Polarization Dependencies (?):
      Total SR power depends on transverse polarization,
      Spin-flip SR (Sokolov–Ternov self-polarization effect) of about
      Total SR power for longitudinal polarized electrons is spin independent but power radiated into space above and below orbital plane is different and thus spin dependent () – principle of Spin-Light Polarimeter
        Helicity-correlated SR → Helicity-correlated emittance growth
Both cancel with helicity reversal
Notes: References:
1. A Spin-Light Polarimeter for Multi-GeV Longitudinally Polarized Electron Beams.
P. Mohanmurthy and D. Dutta, IEEE TRANSACTIONS ON NUCLEAR SCIENCE 61, 528 (2014).
http://dx.doi.org/10.1109/TNS.2013.2291114
2. An observation of the spin dependence of synchrotron radiation intensity.
S. A. Belomesthnykh et al., Nucl. Instrum. Methods, 227, 173 (1984).
http://dx.doi.org/10.1016/0168-9002(84)90119-0
3. https://wiki.jlab.org/ciswiki/index.php/PQB_Meeting_April_30,_2015

## Slide 9
  Beam Studies:
    Measure helicity-correlated beam properties in Hall A:
      Energy difference at 1C12 in middle of Hall A Arc
      Position and angle differences
      Charge asymmetry
    Measure beam halo
      Measure at 1 GeV and confirm QWeak results
      Measure at 11 GeV to study SR effects

## Slide 10: Tasks Summary

## Slide 11: Laser Table Tasks
Task | Sub Tasks | Date | Description
2 kHz Helicity Reversal |  | MOLLER | Requires 10 µs settle time – No ringing (not required for PREX-II, but hoped to test at this time). No Kerr Cell.
 | RTP Pockels Cell |  | Buy test crystals to characterize, design RTP quarter-wave system.
 | KD*P re-design |  | Model E-field to maximize Pockels Cell uniformity, buy a properly engineered, one with the correct cell-diameter-to-laser-beam-diameter aspect ratio
Pockels Cell Stewart Platform |  | 2016 | For remote optimization using e-beam. Assemble, build control software, qualify

## Slide 12: Injector Tasks
Task | Sub Tasks | Date | Description
Reinstate Injector Parity DAQ |  |  | 
Improve 2-Wien Flip Optics |  | PREx-II | 
Injector Matching |  | PREx-II | Maximize damping
Helicity-correlated Beam Size Monitor |  | PREx-II | Looking for ideas!
Upgrade Helicity Magnet controls |  | PREx-II | 
Locate Helicity Magnets to span (x,x') and (y,y') to minimize both position and angle |  | Fall 2015 | 
Augment helicity steering dipoles with helicity size quads |  | PREx-II | 
Share Injector apertures' current read-back with parity DAQ |  | Fall 2015 | 
MOLLER Feedback to minimize transverse polarization |  |  | Once a shift, adjust Wien angle

## Slide 13: Accelerator Tasks
Task | Sub Tasks | Date | Description
Study Depolarization at Higher Passes |  |  | 
 | Energy stability and precession to Hall |  | 
Synchrotron Radiation |  | MOLLER | 
 | Spin precession |  | 
 | Adiabatic damping |  | 
 | Polarization dependence |  | 
 | Helicity-correlated emittance growth |  | 
MOLLER (g-2) Spin Flip |  |  | Change beam energy by 100 MeV (few reversals)

## Slide 14: Hall A Tasks
Task | Sub Tasks | Date | Description
Reinstate Hall A Parity DAQ |  |  | 
Beam Halo |  |  | 
 | Install QWeak halo monitors in Hall A | Fall 2015 | 
BCM Resolution |  |  | 
 | New cavities and receivers | Fall 2015 | 
 | BCM receiver bench studies and beam studies | Fall 2015 | 
Beam Modulation |  | Fall 2015 | 
Beam Polarimetry |  |  | 
Spin Dance |  |  | 
Beam Matching and Optics |  |  | 
Phase Trombone |  |  |