## Slide 1: MOLLER Accelerator Tasks
Hall A
2025 – 2028
Riad Suleiman
November 15, 2022

## Slide 2: MOLLER Requirements
Beam energy GeV
65 µA with 90% polarization (max 70 µA for target studies)
Fast helicity reversal:
  1920 Hz, 10 µsec settle time, 64-window pattern, 128-window delay
Slow helicity reversals:
  Insertable half-wave plate (IHWP)
  Wien Filters
  ge-2 (93 MeV)
Feedbacks on:
  Helicity-correlated beam charge
  Helicity-correlated position and angle
  Polarization orientation
Adequate adiabatic damping of transverse phase-space
Small helicity-correlated beam asymmetries
Acceptable beam halo

## Slide 3: MOLLER Accelerator Tasks
CIS Tasks (Suleiman):
  New settings for Helicity Generator Board (with I&C and Fast Electronics)
  Helicity Decoder Boards (with Ohio Univ and Fast Electronics)
  New RTP HV Drive (with Indiana Univ and I&C)
  Upgrade IA system (with I&C)
  Upgrade Helicity Magnets Control (with I&C, Injector and CASA)
  Feedback on Horizontal Polarization Orientation (with Injector and CASA)
  Wien Filters slow reversal (with Injector and CASA)
CASA Tasks (Roblin):
  Adiabatic damping from 200 keV to Hall A
  Fast Feedback (FFB) System re-design (with I&C)
  Compton Polarimeter Setup
  Beam Dithering (with MOLLER and I&C)

## Slide 4: MOLLER Accelerator Tasks
OPS:
  Study co-operation of MOLLER with KL experiment in Hall D – 0.64 pC @ 7.8 MHz (128 ns, 5 µA average current) to Hall D and 0.26 pC @ 249.5 MHz (4 ns, 65 µA average current) to MOLLER:
    Beam loading in Bunchers or RF power in SRF Linacs? Digital RF?
    Any photocathode issues? (CIS)
  Any conflicts with other Halls? Need Experimental Schedule for 2025-2028
  Complete Injector Upgrade and commission (with CIS and CASA)
  Robust Ion Chambers inside MOLLER Spectrometer
  New BPM receivers in Hall A line (instead of S/H cards)
  New BCMs/Electronics in Hall A line
  Halo Monitors in Hall A