## Slide 1: Accelerator Physics
Alicia Hofler
Accelerator Physicist Experimental Liaison

## Slide 2: Notes from Riad
Message: We know how to set up energy and measure it
  3-4 slides (max 5)
Bubble beamline
Beam sizer?
Errors
Beam energy
  error bars
    Magnet current
    Field map
    angle
GPT modeling

## Slide 3: Energy Measurement
Procedure:
A priori, center beam in quadrupole closest to BPM and note positions (except 2D—no quads).
Turn OFF and cycle all unnecessary magnets around hysteresis loop.
Degauss dipole.
Establish straight ahead orbit with restricted corrector magnet set.
Adjust dipole setting (and cycle) for zero orbit in each dump BPM.
  Note dipole setpoint
    < 0 for beam in 2D line
    > 0 for beam in 5D line
For fixed incoming momentum, = ,
  From dipole setting fits, determine
  p
  errors in angle and field.
BPM=Beam Position Monitor
Dipole
2D
-30o
5D
25o
BPM
BPM
BPM
BPM
Accelerator coordinate system is LH

## Slide 4: Measured Energies
The measured values include errors/offsets in
  angle: -0.05o
    -30o ⇒ -30.05o
    25o ⇒ 24.95o
  field integral: 115.90 G cm
    Unshielded portion of beamline and deflected by earth’s field?
Minor Issues and possible mitigations:
  straight ahead orbit
    improve set up procedure (to eliminate/reduce unnecessary magnetic fields)
  stray fields
    more shielding
  how well know beam orbit angles
    fiducialize 2D and 5D harps
    add quads to 2D line for quad centering/establish orbit reference
  beam position on the radiator
    Target flag at radiator for steering
Design p (MeV/c) | Design K.E. (MeV) | 2D line dipole setting (G cm) | 5D (Bubble) line dipole setting (G cm) | Measured p (MeV/c) | Measured K.E. (MeV)
5.84 | 5.35 | -9937.637 | 8168.800 | 5.88 | 5.39
5.74 | 5.25 | -9865.500 | 8099.000 | 5.84 | 5.35
5.64 | 5.15 | -9632.300 | 7909.200 | 5.70 | 5.21
5.54 | 5.05 | -9468.500 | 7771.400 | 5.60 | 5.11
5.44 | 4.95 | -9320.700 | 7646.800 | 5.51 | 5.02
5.34 | 4.85 | -9135.993 | 7490.000 | 5.40 | 4.91
5.24 | 4.75 | -8957.675 | 7338.900 | 5.30 | 4.81