## Slide 1
Polarized Positron Beam
R&D at Jefferson Lab
Joe Grames
Center for Injectors and Sources, Jefferson Lab
The PEPPo experiment
Positron Beams at CEBAF
JPos17 and JLab PWG
Notes: INJECTOR SCIENTIST AT JEFFERSON LAB
WOULD LIKE TO TELL YOU ABOUT A SMALL EXPERIMENT WE PERFORMED TO PRODUCE POLARIZED POSITRONS AT LOW ENERGY
WILL GET TO THIS COMMENT AT THE END

## Slide 2
2
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
Polarized Bremmstrahlung and Pair Creation
Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)
Notes: THE PEPPO METHOD IS PRETTY STRAIGHT-FORWARD
FIRST STAGE IS POLARIZED BREMMSTRHALUNG
SECOND STAGE IS POLARIZED PAIR CREATION
THIS COULD BE DONE IN SEPARATE TARGETS, BUT CONVENIENTLY ALSO IN ONE SINGLE TARGET
WE LEARNED EARLY ON THE CALCULATIONS OF OLSON/MAXIMON WERE NOT CORRECT AT LOW ENERGY, ESPECIALLY PAIR CREATION
NEW CALCULATIONS WERE DONE, THAT AGREE W/ OM AT HIGHER ENERGIES
WE WERE NOT FIRST TO PROPOSE THIS IDEA, SO WHY NOT BEFORE…

## Slide 3
J. Grames, E. Voutier et al., JLab Experiment E12-11-105 (2011)
The purpose of the PEPPo (Polarized Electrons for Polarized Positrons) experiment at the CEBAF Injector was to demonstrate the feasibility of using bremsstrahlung radiation of MeV energy Polarized Electrons for the efficient production of Polarized Positrons.
Polarized Electrons for Polarized Positrons

## Slide 4
BREMSSTRAHLUNG
Longitudinal e- (Pe-) produce elliptical g whose circular (Pg) component is proportional to Pe-
COMPTON TRANSMISSION
Polarized e+ convert into polarized g (Pg) whose transmission through a polarized iron target (PT) depends on Pg.PT
PAIR PRODUCTION
In the same target, g produce e+e- pairs and transfer Pg into longitudinal (Pe+) and transverse polarization averages to zero
Pe-
e-
T1
Polarized Electrons
(< 10 MeV/c) strike production target
S1
D
D
S2
Pe+
Positron Transverse and Momentum Phase Space Selection
e+
T2
PT
Calorimeter
Compton Transmission Polarimeter
Ee = 6.3 MeV
Ie = 1 µA
T1 = 1 mm W
Geant4
PEPPo
J. Dumas, PhD Thesis (2011)
PEPPo measured the longitudinal polarization transfer from 8.25 MeV/c e- to e+ in the 3.07-6.25 MeV/c momentum range.
PEPPo Principle of Operation

## Slide 5
Compton Transmission Polarimeter Spectra
Compton physics asymmetries are obtained from the polarization sensitive energy deposition in the central crystal.
The location of the 511 keV peak is an in-situ monitor of the gain of the detection chain and provides a link to radioactive source calibration data.
The coincidence time between the central crystal and a charge sensitive trigger scintillator allows for accidental subtraction.
Energy
Central
Detector
Coincidence
Trigger and
Central Detector

## Slide 6
The experimental Compton asymmetry for an electron beam of known polarization provides a measurement of the electron analyzing power (Ae) of the polarimeter.
A comparison between the experimental and the GEANT4 simulated response of the polarimeter establishes a calibrated model of the polarimeter.
The positron analyzing power (Ap) is then determined by simulation using the calibrated model.
Target polarization
Electron beam polarization
Electron-to-positron
polarization transfer
PT = 7.06% ±0.05%Sta.± 0.07%Sys.
A. Adeyemi (Hampton University)
Compton Transmission Analyzing Power

## Slide 7
PEPPo Result
PEPPo demonstrated efficient polarization transfer of 8.2 MeV/c polarized electrons to positrons, expanding polarized positron production using MeV electron beam energies.
(PEPPo Collaboration) D. Abbott et al. , Phys. Rev. Lett. 116 (2016) 214801
electron beam polarization
85.2 ± 0.6 ± 0.7 %
Whenever producing e+ from e-, polarization is coming for free
if initial electrons are polarized.

## Slide 8
Two NaI detectors measured coincidence of back-to-back photons emitted by annihilation of positrons in a viewscreen.
Positron Yield
T1
T2
S1
S2
D
D
e+
e-
pe-= 8.2 MeV/c
e+
For these data we had a yield of ~10-5 e+/e-.
A3
A1
A3
A1

## Slide 9
P. Adderley1, A. Adeyemi4, P. Aguilera1, M. Ali1, H. Areti1, M. Baylac2, J. Benesch1,
G. Bosson2, B. Cade1, A. Camsonne1, L. Cardman1, J. Clark1, P. Cole5, S. Covert1,
C. Cuevas1, O. Dadoun3, D. Dale5, J. Dumas1,2, E. Fanchini2, T. Forest5, E. Forman1,
Freyberger1, E. Froidefond2, S. Golge6, J. Grames1, P. Guèye4, J. Hansknecht1,
P. Harrell1, J. Hoskins8, C. Hyde7, R. Kazimi1, Y. Kim1,5, D. Machie1, K. Mahoney1,
R. Mammei1, M. Marton2, J. McCarter9, M. McCaughan1, M. McHugh10, D. McNulty5, T. Michaelides1, R. Michaels1, C. Muñoz Camacho11, J.-F. Muraz2, K. Myers12,
Opper10, M. Poelker1, J.-S. Réal2, L. Richardson1, S. Setiniyazi5, M. Stutzman1,
R. Suleiman1, C. Tennant1, C.-Y. Tsai13, D. Turner1, A. Variola3, E. Voutier2,11,
Y. Wang1, Y. Zhang12
1 Jefferson Lab, Newport News, VA, US 2 LPSC, Grenoble, France 3 LAL, Orsay, France
4 Hampton University, Hampton, VA, USA 5 Idaho State University & IAC, Pocatello, ID, USA
6 North Carolina University, Durham, NC, USA 7 Old Dominion University, Norfolk, VA, US
8 The College of William & Mary, Williamsburg, VA, USA 9 University of Virginia, Charlottesville, VA, USA 10 George Washington University, Washington, DC, USA 11 IPN, Orsay, France
12 Rutgers University, Piscataway, NJ, USA 13 Virginia Tech, Blacksburg, VA, USA
Many thanks for support from SLAC E166, DESY, Princeton, Cornell, International Linear Collider Project and Jefferson Science Associates
PEPPo Collaboration

## Slide 10
R. Dollan, K. Laihem, A. Schälicke, NIM A 559 (2006) 185,
J. Dumas, J. Grames, E. Voutier, JPos09, AIP 1160 (2009) 120
J. Dumas, Doctorate Thesis (2011)
Optimum energy
Optimum
FoM
The polarization distribution of generated positrons is dominated by low-energy events.
The positron energy at the optimum FoM (P2I) is about half of the electron beam energy.
Figure of Merit (e.g. Ee- = 60 MeV)

## Slide 11
J. Dumas, Doctorate Thesis (2011)
Using a 100 MeV electron beam and a more realistic momentum spread dp/p <1% (DE ~ 1 MeV) the conversion efficiency is 1-5 x 10-4.
In the 10-100 MeV electron beam energy one can simulate at the FoM, with dp/p < 10% and angle<10°
  conversion efficiency (e) varies from about 10-5 - 10-3 e+/e-
  electron polarization transfer is “flat” ~75% at FoM
Using the CEBAF Polarized Electron Injector

## Slide 12
Concept for a Dedicated e+ Source
What are some requirements to use a 100 MeV electron beam for generating a positron beam with intensity Ie+ > 100 nA and polarization Pe+ > 65% (at max FoM) ?
  Collecting e+ at 60 MeV with ~10-4 e+/e- efficiency suggests ~1 mA polarized electron beam and a high power conversion target (typ. >10% in target).
Concept S. Golge Thesis
Drawing A. Freyberger
Existing
CEBAF
Electron
Injector
Concept for dedicated Positron Injector

## Slide 13
QE ~ 5%, 30 mA/W
Pol ~ 35% @ 780 nm
Bulk GaAs
QE ~ 0.2%, 1 mA/W
Pol ~ 75% @ 850 nm
Strained GaAs:
GaAs on GaAsP
100 nm
Superlattice GaAs:
Layers of GaAs on GaAsP
QE ~ 1%, 6 mA/W
Pol ~ 85% @ 780 nm
100 nm
14 Layers
2 μm
350 μm
625 μm
CEBAF GaAs Photocathode Evolution
Spin Polarized Electron programs (particularly PV Users) have
driven the need for improved performance over last 20+ years
Pe- 35% 35% 75% 75% 85% 89%
Ie- 30mA 100mA 50mA 100mA 150mA 200mA
1995 1998 1999 2000 2004 2012 2017
Notes: FOR US AT JLAB, HOWEVER, SAW THIS AS AN OPPORTUNITY TO EXPLOIT WHAT WE’VE BEEN DOING W/ POLARIZED E- BEAMS FOR TWO DECADES
OVER THAT TIME THE SPIN PROGRAM HAS DRIVEN IMPROVEMENT
GAAS PHOTOCATHODES THAT BREAK DEGENERACY, YET RETAIN HIGH QUANTUM EFFICIENCY
THIS MEANS HIGH SPIN POLARIZATION (85%) AND HIGH QE (>1%)
LEARNING HOW TO SUSTAIN THIS FOR LONG PERIODS MAKES THIS VIABLE

## Slide 14
High current (1-10 mA) studies with low-P photocathodes demonstrated that charge lifetime is improved by increasing laser spot size (spreading out ion damage).
Measurements are underway using the CEBAF polarized source to characterize lifetime vs. spot size with high-P (>85%) photocathodes with intensities of 0.5-2 mA
CEBAF Polarized Inverted Load Lock Gun
1mA
Slope is proportional to QE Decay
Increasing laser size reduces QE decay proportionally
Phys. Rev. ST Accel. Beams 14, 043501 (2011)
Photocathode Lifetime at mA Beam Currents

## Slide 15
Electron Polarization at mA Beam Current
Chart: Polarization (%)
| 1.67 | 10.4 | 50.5 | 100.5 | 250.5 | 504.0 | 755.0 | 1011.0 | 1.06
 | 85.6704 | 84.5218 | 84.3896 | 85.3479 | 84.9536 | 86.116 | 84.7714 | 85.9647 | 87.1486
For the first time, the spin polarization of a high-P superlattice photocathode is measured from low to milliAmpere intensity.
CEBAF Mott Polarimeter
The spin polarization of a high current (mA) beam is measured at CEBAF by extracting and accelerating a small fraction of the beam to a sub-percent accuracy Mott polarimeter.

## Slide 16: High Polarization Photocathode R&D
GaAs/GaAsP superlattice photocathode with GaAsP/AlAsP Distributed Bragg Reflector (DBR)
The highest QE & FOM of any reported high polarization photocathode
W. Liu, S. Zhang, M. Stutzman, M. Poelker, Y. Chen, W. Lu, and A. Moy
Appl. Phys. Lett. 109, 252104 (2016)
DBR Stack
Substrate
SLSP
Photocathode
CEBAF
DBR (R&D)
6.4

## Slide 17
High Power Target R&D
Stainless Steel Windows (0.25mm)
LBE (2mm)
Input (e-)
Output (e-,e+,γ)
Liquid Metal Target – lead-bismuth eutectic (LBE)
  High Z = 82, 83
  Low melting point: 124°C
  High boiling point: 1670°C
Multiple LBE targets tested on various accelerators
  Natural Circulation
  Mechanical Pumping
  Electromagnetic Pumping
Approaching 10 kW power level, CW

## Slide 18
Still, many issues to discuss and resolve…
Magnetic Recirculation (e- beam goes clockwise)
  Inverted direction requires long transfer line and difficult inject-/extraction
  Clockwise direction requires reversal of unipolar dipole power supplies; focusing quadrupole and steering correctors have bipolar supplies
Low Current Operation (to tune-up and “see” the beam)
  Most of the Accelerator and Hall B is blind to <100 nA
  “Peak intensity” macro-pulse (1.5% duty factor) challenging
Delivering Positron Beams (setting up the machine)
  Requires setting up CEBAF initially with an electron beam
  Additional LINAC beam position monitors are needed for monitoring the low intensity beam between recirculation arcs
  Requires a number of well-placed upgrade receivers for 10 nA operation
  Supplemental monitors (SLM, wire scanners/OTR screens) will be needed to monitor the beam during operation

## Slide 19
The JPos17 International Workshop (Sep 12-15) at Jefferson Laboratory will review the Scientific and Technical basis for positron beams (polarized and unpolarized) in context of CEBAF 12 GeV, JLEIC, and for Low Energy Applications.
JPos17 and the Jefferson Lab Positron Working Group will serve as a basis to develop a White Paper on Positron Physics at JLab.
wiki.jlab.org/pwg pwg@jlab.org
www.jlab.org/conferences/JPos2017
Please Join Us !!!
JPos17 @ Jefferson Lab

## Slide 20
Summary
The PEPPo technique provides access to highly spin-polarized positrons opening access to a wide community.
A high-energy polarized positron beam program in the context of CEBAF 12 GeV (and JLEIC) based on the PEPPo technique is being explored.
Your input is important and timely:
    JPos17 => www.jlab.org/conferences/JPos2017/
    JLab PWG => wiki.jlab.org/pwg
I would like to acknowldge Larry Cardman, Arne Freyberger, Yves Robin, Michael Tiefenbeck, and Eric Voutier for their comments and input to this talk.

## Slide 21
Back Up Slides

## Slide 22
P(e+) = 73 ± 15(stat) ± 19(syst) %
Compton Backscattering (KEK)
T. Omori et al, PRL 96 (2006) 114801
Helical Undulator (SLAC E166)
G. Alexander et al, PRL 100 (2008) 210801
P(e+) = 80 ± 7(stat) ± 9(syst) %
47.7GeV
Polarized b+ Decay
L.A. Page & M. Heinberg. Phys. Rev.
106(6):1220-1224 (1957)
Polarized due to parity non-conservation in the weak interaction
P(e+) ~ 40 %
Sokolov-Ternov Effect
D. Barber , AIP Conf. Proc. 588, 338 (2001)
HERA 27.5 GeV e+/e-
P(e+) ~ 70 %
Collecting Polarized Positrons
Notes: TO PROVIDE SOME CONTEXT, POLARIZED POSITRONS CAN BE COLLECTED IN A NUMBER OF WAYS
BETA DECAY – WEAK INTERACTION (NOT EFFICIENT FOR RF ACCEL)
ST – QUANTUM EMISSION OF SYNC. RAD. (NOT COMPATIBLE W/ CW BEAM)
PAIR PRODUCTION BY POLARIZED GAMMAS (PLAUSIBLE, BUT HIGH TECHNICAL CHALLENGE – INTENSE LASERS, HIGH ENERGY BEAMS)
WE WONDERED IF WE COULD SIMPLY USE OUR POLARIZED ELECTRON BEAM

## Slide 23
PEPPo ran at the CEBAF injector, taking advantage of the existing beam diagnostics that determine with precision the properties of the polarized electron beam entering the PEPPo apparatus.
Polarization controls
    30 Hz fast heilicity reversal (delayed)
    Slow laser polarization reversal (half-wave plate)
    4p spin rotator
Variable energy
3.1-8.2 MeV/c
Polarization measurement
dP/P < 2%
Energy measurement
dp/p < 0.5%
PEPPo
Laser
Intensity controls
10 pA – 1 µA
CEBAF Polarized Electron 10 MeV Injector

## Slide 24
Positron Yield using 10 MeV Electrons
>100nA e+ at IP2 for CEBAF => >1.0 milliAmp e- beam
Electro-magnetic Shower
e+ yield ~ e- beam power (E*I)
High Z-target increases yield
Operate at low energy below photo-neutron threshold to mitigate radioactivity
10 MeV e- shower
e+/e- yield ~ 0.1 % (optimized)
Collection efficiency ~ 1-10 %

## Slide 25: JLEIC/CEBAF Positron Injector
10 MeV polarized e-
1.33 pC @ 1500 MHz
10 MeV pol e-
0.67 nC bunches
@ 1500 MHz
500-Turn
Accumulator Ring
(22m)
Bunch
Management
10 MeV polarized e-
0.67 nC @ 68.1 MHz
Positron Conversion/Collection Efficiency ~ 10-4
5-7 MeV Polarized e+
67 fC @ 68.1 MHz
to CEBAF/JLEIC
Harmonic
Extraction Ring
(22m)
 | Polarized Electron Source | Accumulator/ Extractor Rings | Electrons at Converter | Polarized Positron Source | R&D Challenge
JLEIC | Ave = 100 mA 1.33 pC @ 1500 MHz 2 mA w/ DF=5% | Ave = 1 A 1500 MHz | Ave = 100 uA 68.1 MHz 44 mA @ DF=0.23% | Ave = 10 nA 68.1 MHz 4.4 uA @ DF = 0.23% | Electron accumulator Harmonic extraction Target: 440 kW peak
CEBAF | Ave = 1-10 mA 4-40 pc @ 250 MHz (cw) | Not Necessary | Ave = 1-10 mA 250 MHz (cw) | Ave = 100 nA - 1 mA 250 MHz (cw) | High-QE photocathode High voltage gun Target: 10-100 kW ave
Polarized
Electron
10 MeV Injector
J. Grames, SPIN 2016 @ UIUC, Sep 26-30 2016
25
Slide courtesy of Fanglei Lin