## Slide 1: 200 mA Magnetized Beam for MEIC Electron Cooler
MEIC Collaboration Meeting
Spring 2015
March 30, 2015
Riad Suleiman and Matt Poelker

## Slide 2: Outline
MEIC Magnetized Electron Beam Cooling Requirements
Source Pros and Cons
Gun Options:
  CW RF guns, warm and cold
  Thermionic gun
  Photogun
Magnetized Beam
Summary

## Slide 3: Bunched Magnetized Electron Gun Requirements
Bunch length | 100 ps (3 cm)
Repetition rate | 476 MHz
Bunch charge | 420 pC
Peak current | 4.2 A
Average current | 200 mA
Emitting area | 6 mm ɸ
Transverse normalized emittance | 10s microns
Solenoid field at cathode | 2 kG

## Slide 4: Source Pros and Cons
Warm CW RF gun: thermionic emitter or photocathode, the promise of high bunch charge, but long low-energy tail, managing heat load for CW operation (AES and LANL examples)
CW SRF gun: huge potential, but also huge technical challenges including applied mag field (Rossendorf and BNL)
RF-pulsed grid thermionic gun: simple, long lifetime, but also long pulse and worst emittance (TRIUMF and BINP’s NovoFEL)
DC high voltage photogun: good emittance, delicate photocathodes, high bunch charge demands high bias voltage (JLab and Cornell)

## Slide 5: Source Dependencies
Thermal Emittance: Intrinsic property of a cathode. Depends on work function, surface roughness, laser wavelength, temperature.
Achievable Current: QE, laser wavelength, laser power, laser damage, heating, emitter size, temperature.
Bunch Charge: laser peak power, repetition rate, active cathode area, bunch length.
Cathode Lifetime: ion back bombardment, dark current, contamination by residual gas, evaporation, beam loss, halo beam.
What will applied magnetic field do?

## Slide 6: Warm CW RF gun options
Example 1: Advanced Energy Systems (AES), Inc., NCRF gun (A. Todd, ERL11):
RF frequency | 1 GHz
Bunch length | 1 – 5 ps
Bunch charge | 0.2 nC
Normalized emittance | 20 microns
Bean energy (after pre-booster) | 1 MeV
Micropulse length | 1 – 8 µs
Micropulse repetition rate | 10 Hz
To be used as CW gun – instead of pulsed gun

## Slide 7
Example 2: LANL/AES 2.5-cell NCRF gun:
RF frequency | 700 MHz
Bunch repetition rate | 35 MHz
Average current | 100 µA
Bunch length | 9 ps
Bunch charge | 1 – 3 nC
Normalized emittance | 7 microns
Bean energy | 2.5 MeV
Energy spread | <1.3%
Ohmic losses | 780–820 kW
E cathode | 10 MV/m
D.C. Nguyen et al., NIM A 528, 71 (2004)

## Slide 8: CW SRF Gun Options
Example 1: Rossendorf (BESSY-DESY-FZD):A. Burrill, EIC14
 | Injector 0 | Injector 1 | Injector 2
Goal | Beam Demonstrator | Brightness R&D Injector | High-current injector
Electron energy | ≥ 1.5 MeV |  | 
RF frequency | 1.3 GHz |  | 
Design peak field | ≤ 50 MV/m |  | 
Operation launch field | ≥ 10 MV/m |  | 
Bunch charge | ≤ 77 pC |  | 
Repetition rate | 30 kHz | 54 MHz / 25 Hz | 1.3 GHz
Cathode material | Pb | CsK2Sb | CsK2Sb
Cathode QE | 10−4 at 258 nm | 2-10% at 532 nm | 2-10% at 532 nm
Laser wavelength | 258 nm | 532 nm | 532 nm
Laser pulse energy | 0.15 µJ | 1.8 nJ | 1.8 nJ
Laser pulse shape | Gaussian | Gaussian/Flat-top | Gaussian/Flat-top
Laser pulse length | 2.5 ps FWHM | ≤ 20 ps | 20 ps
Average current | 0.5 µA | ≤ 10 mA / 0.1 mA | 100 mA
2015 focus

## Slide 9
Example 2: BNL SRF guns program (S. Belomestnykh, EIC14):
Two SRF photoemission guns are under active development:
704 MHz ½-cell elliptical gun to deliver high bunch charge and high average current beams for R&D ERL
112 MHz QWR gun is designed to produce high bunch charges, but low average beam currents for Coherent electron Cooling (CeC) Proof-of-Principle experiment
Preparing for first beam test
Two other SRF guns under development:
1.3 GHz SRF plug gun for GaAs photocathodes
84.5 MHz SRF gun for eRHIC CeC injector

## Slide 10: Thermionic Gun Options
Example 1: TRIUMF e-Linac for photo-fission of actinide target materials to produce exotic isotopes:
      BaO: 6 mm diameter, 775˚C
Grid at 650 MHz
Gun HV: 300 kV
Average current: 25 mA
Bunch charge: 38 pC
Normalized emittance: 30 microns. Emittance is dominated by electric field distortion caused by grid.
rf tuner
ceramic waveguide
high voltage shroud
support

## Slide 11
Example 2: Thermionic Gun and 1.5 MeV Injector of BINP’s NovoFEL. B.A. Knyazev et al., Meas. Sci. Tech. 21, 054017 (2010):
Gun HV | 300 kV
Maximum peak current | 1.8 A
Maximum average current | 30 – 45 mA
Maximum bunch repetition rate | 22.5 MHz
Bunch length | 1.3 ns
Bunch charge | 1.5 – 2 nC
Normalized emittance | 10 microns

## Slide 12: Photogun Options
Example 1: JLab 200 kV Inverted dc Gun with K2CsSb photocathode:
  Average beam current: 10 mA
  Laser: 532 nm, dc
  Lifetime: very long (weeks)
  Thermal emittance: 0.7 microns/mm(rms)
Mammei et al., Phys. Rev. ST AB 16, 033401 (2013)

## Slide 13
 | 200 kV Gun | 350/500 kV Gun
Chamber | 14” ɸ | 18’’ ɸ
Cathode | 2.5” T-shaped | 6” ɸ Ball
Cathode Gap | 6.3 cm | 6.3 cm
Inverted Ceramic | 4” long | 7” long
HV Cable | R28 | R30
HV Supply | Spellman 225 kV, 30 mA | Glassman 600 kV, 5 mA
Maximum Gradient | 4 MV/M | 7 (10) MV/m
Example 2: JLab 350/500 kV Inverted dc Gun:
Achieved 350 kV with no FE, next:
Keep pushing to reach 500 kV
Run beam with K2CsSb photocathode

## Slide 14
Example 3: Cornell dc Gun with K2CsSb photocathode:
      Dunham et al., Appl. Phys. Lett. 102, 034105 (2013)
Gun HV: currently operating at 350 kV (designed 500-600 kV)
Average beam current: 65 mA for 9 hours (lifetime 2.6 days)
Bunch charge: 50 pC
Bunch length: 10 ps, 1.3 GHz
Normalized emittance: <0.5 microns

## Slide 15: Magnetized Beam and Emittance Compensation
Solenoids (Bz~2kG)
(space-charge emittance growth compensation)
Solenoid (Bz~2kG)
(magnetized beam)
Magnetized Cathode:
  To produce magnetized (angular-momentum-dominated) electron beam to ensure zero angular momentum inside cooling-solenoid section)
Injector Solenoids:
  To compensate space-charge emittance growth
Will be easier to implement with compact gun (inverted photogun or thermionic gun)

## Slide 16: Summary
Thermionic gun would be our first choice (less maintenance but may need complicated injector):
    TRIUMF/BINP Gun with Inverted Ceramic
For better emittance, a dc HV photogun is good option:
    JLab 350/500 kV Inverted Gun and JLab multi-alkai photocathode (Na2KSb or K2CsSb)
If one gun cannot provide 200 mA, then use two or three guns and combine beams using RF combiner or dipole magnet

## Slide 17: LDRD: 200 mA Magnetized Beam
Use JLab 350/500 kV Inverted Gun and K2CsSb photocathode
Design and build Cathode Solenoid
Generate magnetized beam
Measure beam magnetization:
  Measure beam emittance vs. beam size
  Measure directly using slit and screen
Study transportation of magnetized beam and magnetized to flat beam transformation
Measure magnetized photocathode lifetime at high currents
Repeat with 100 kV thermionic gun loaned to TRIUMF

## Slide 18: Backup Slides

## Slide 19: Magnetized Electron Cooling

## Slide 20: Busch’s Theorem
On entering or exiting solenoid, beam acquires a kick that makes beam to rotate
Busch’s Theorem: Canonical angular momentums is conserved,
Canonical angular momentum:
Magnetic emittance:
emag[microns] ~ 30 B[kG] σe[mm]2

## Slide 21
Cathode Solenoid
Cathode
Electrons born in uniform Bz
BCath_Sol = 2 kG
B=0
Upon exit of Cathode Solenoid
Cooling Solenoid
Ion Beam
Upon entering Cooling Solenoid
BCool_Sol = 2 T
σe= Rlaser = 3 mm
σe= 1 mm
Electron
Beam
Magnetized Cooling

## Slide 22: Why: Magnetized beam?
Magnetic field limits transverse motion of electrons; cooling rate is determined by longitudinal velocity spread:
Cooling rate for non-magnetized beam:

## Slide 23: Cooling Solenoid
Cooling solenoid: 30 m long and 2 T field
Electron and ion are moving at same speed in cooling section (solenoid)
Inside cooling solenoid, electron beam is calm: not to have any angular motion
Cooling solenoid must have high parallelism of magnetic field lines:

## Slide 24: Cooling Rate: Dependencies on Electron Beam Properties
Proportional to average beam current (does not depend on peak current)
Independent of ion beam intensity
Proportional to cooler length
Magnetized cooling is less dependent on electron beam transverse emittance
Cooling rates with magnetized electron beam are ultimately determined by electron longitudinal energy spread only
Non-magnetized beam depends on transverse electron velocity (a weak field may be used for focusing – i.e., FNAL dc cooler, 100 G)
Bunched electron (from SRF gun) cooling planned at BNL – without any magnetization, shield magnetic field < 0.2 mG

## Slide 25: Electron – ion Recombination Suppression
Suppresses ion-electron recombination in cooling section if loss of luminosity is not negligible
  No suppression is planned at BNL. Future upgrade to use undulator field, 3 G and 8 cm period
  For magnetized beam, large transverse temperature in cooling section suppresses recombination

## Slide 26: Paraxial Beam Envelope Equation
Acceleration Damping
Injector Solenoids
(for space-charge emittance growth compensation)
Cathode Emission
Space Charge
Cathode Solenoid
Cooling Solenoid
Bz=20 kG
Bz=2 kG

## Slide 27
MEIC Polarized Electron Source

## Slide 28: MEIC Polarized Source
…
…
…
…
Helicity Reversal
72.07 µs
Damping Time
3 GeV – 12 GeV
700 ms – 12 ms
3.233 µs
Bunch Charge
26 pC – 6.6 pC
220 bunches
at 68.05 MHz
(14.69 ns)
Pockels cell switching time at CEBAF today ~70 us. Planned for Moller Exp. ~10 us
Bunch charge 72 x larger than typical CEBAF, 20 x greater than G0 – Expect to use a gun operating at higher voltage
68.05 MHz pulse repetition rate not be a problem for gun, maybe for LINACs
We are not considering simultaneous beam delivery to fixed target halls, using typical CEBAF beam
Message: MEIC polarized source requirements do not pose significant challenges

## Slide 29: Source Parameter Comparison
Parameter | JLab/FEL | CEBAF | EIC MEIC | EIC eRHIC | Cornell ERL | LHeC | CLIC | ILC
Polarization | No | Yes | Yes | Yes | No | Yes | Yes | Yes
Photocathode | Bulk GaAs | GaAs / GaAsP |  |  | K2CsSb |  |  | 
Width of microbunch (ps) | 35 | 50 | 50 | 100 | 2 | 100 | 100 | 1000
Time between microbunches (ns) | 13 | 2 | 14.69 | 106 | 0.77 | 25 | 0.5002 | 337
Microbunch rep rate (MHz) | 75 | 499 | 68.05 | 9.4 | 1300 | 40 | 1999 | 3
Width of macropulse | - | - | 3.233 µs | - | - | - | 156 ns | 1 ms
Macropulse repetition rate (Hz) | - | - | 2x83 | - | - | - | 50 | 5
Charge per microbunch (pC) | 133 | 0.36 | 26 | 5300 | 77 | 640 | 960 | 4800
Peak current of microbunch (A) | 3.8 | 0.008 | 0.52 | 53 | 38.5 | 6.4 | 9.6 | 4.8
Laser spot size (cm, diameter) | 0.5 | 0.1 | 0.3 | 0.6 | 0.3 | 0.5 | 1 | 1
Peak current density (A/cm2) | 19 | 1 | 7.4 | 188 | 500 | 32 | 12 | 6
Average current from gun (mA) | 10 | 0.2 | 0.001 | 50 | 100 | 25 | 0.015 | 0.072
Proposed
* Unpolarized: Bulk GaAs (Cs,F), K2CsSb, Na2KSb, …
Polarized: GaAs/GaAsP (Cs,F).
Notes: Why multi-alkali (bulk material, Eg = 1.5 eV) photocathodes are not sensitive to ion bombardment?
No NEA activation layer.
eRHIC: electron Relativistic Heavy Ion Collider
LHeC: Large Hadron electron Collider
CLIC: Compact Linear Collider
ILC: International Linear Collider
---
Why Laser Spot Size? to reduce space-charge emittance growth and suppress surface charge limit.
---
eRHIC: 20 photocathodes, 2.5 mA from each
---
How to fill the numbers:
Microbunch rep rate = 1.0/Time between microbunches
Number of microbunches = Width of macropulse / Time between microbunches
For CW machines: Duty Factor = 100% (for CW machines)
For pulsed machines: Duty Factor = Width of macropulse * Macropulse repetition rate
Charge per microbunch = Number electrons/microbunch * Electron Charge(1.6e-19 C)
Peak current of microbunch = Charge per microbunch / Width of microbunch
Peak current density = Peak current of microbunch / ( (Laser Spot Size/2)**2 * Pi)
Average Current = Charge per microbunch * Microbunch rep rate * Duty Factor

## Slide 30: Addressing MEIC Bunch Charge
Larger Laser Size (reduces space-charge emittance growth and suppresses surface charge limit)
Higher Gun Voltage:
  Reduce space-charge emittance growth, maintain small transverse beam profile and short bunch-length; clean beam transport
  Compact, less-complicated injector
To accelerate large bunch charge in CEBAF: use RF feedforward system for C100 cryomodules
20 to 72 times larger than CEBAF

## Slide 31: JLab 500 kV Inverted Gun
Longer insulator
Spherical electrode
200 kV Inverted Gun
5”
7”