## Slide 1: Mott Run Time Estimates
DAQ rate < 5,000 Hz
Beam current < 50 µA
Target thickness extrapolation from Steigerwald is included
Dump events: 25 Hz/µA per detector
Beam polarization: 85%
Statistical error (dp/p): 0.5%

## Slide 2: Target Thickness Extrapolation

## Slide 3: Au Target

## Slide 4: Au Target - 3.0 MeV
Target Thickness (µm) | I (µA) | Time (hr) | DAQ Rate (Hz) | Asym (%) | Seff
0.05 | 12.76 | 0.04 | 5000 | -40.49 | -0.4763
0.10 | 7.31 | 0.03 | 5000 | -40.16 | -0.4725
0.35 | 2.33 | 0.03 | 5000 | -38.62 | -0.4543
1.0 | 0.84 | 0.04 | 5000 | -35.11 | -0.4130
5.0 | 0.17 | 0.09 | 5000 | -22.51 | -0.2649

## Slide 5: Au Target - 5.0 MeV
Target Thickness (µm) | I (µA) | Time (hr) | DAQ Rate (Hz) | Asym (%) | Seff
0.05 | 29.77 | 0.06 | 5000 | -43.77 | -0.5150
0.10 | 21.19 | 0.04 | 5000 | -43.20 | -0.5083
0.35 | 8.69 | 0.03 | 5000 | -40.57 | -0.4773
1.0 | 3.43 | 0.04 | 5000 | -35.02 | -0.4120
5.0 | 0.73 | 0.12 | 5000 | -19.01 | -0.2237

## Slide 6: Au Target - 8.0 MeV
Target Thickness (µm) | I (µA) | Time (hr) | DAQ Rate (Hz) | Asym (%) | Seff
0.05 | 41.54 | 0.17 | 5000 | -38.98 | -0.4586
0.10 | 35.52 | 0.11 | 5000 | -38.19 | -0.4493
0.35 | 20.61 | 0.06 | 5000 | -34.68 | -0.4080
1.0 | 9.85 | 0.07 | 5000 | -27.98 | -0.3292
5.0 | 2.34 | 0.29 | 5000 | -12.79 | -0.1504

## Slide 7: Ag Target - 5.0 MeV
Target Thickness (µm) | I (µA) | Time (hr) | DAQ Rate (Hz) | Asym (%) | Seff
0.05 | 45.18 | 0.95 | 5000 | -22.02 | -0.2591
0.10 | 41.20 | 0.53 | 5000 | -21.74 | -0.2557
0.35 | 28.62 | 0.25 | 5000 | -20.41 | -0.2401
1.0 | 15.95 | 0.21 | 5000 | -17.62 | -0.2073
5.0 | 4.28 | 0.53 | 5000 | -9.57 | -0.1125

## Slide 8: Cu Target - 5.0 MeV
Target Thickness (µm) | I (µA) | Time (hr) | DAQ Rate (Hz) | Asym (%) | Seff
0.05 | 47.87 | 7.82 | 5000 | -11.55 | -0.1359
0.10 | 45.92 | 4.18 | 5000 | -11.40 | -0.13.42
0.35 | 38.13 | 1.63 | 5000 | -10.71 | -0.1260
1.0 | 26.46 | 1.11 | 5000 | -9.24 | -0.1087
5.0 | 9.18 | 2.16 | 5000 | -5.02 | -0.0590

## Slide 9
Fall 2013 Gold Plan

## Slide 10: Au Target
Beam current < 2 µA

## Slide 11: Au Target - 3.0 MeV
Target Thickness (µm) | I (µA) | Time (hr) | DAQ Rate (Hz) | Asym (%) | Seff
0.050 | 2.00 | 0.23 | 783 | -40.49 | -0.4763
0.100 | 2.00 | 0.12 | 1368 | -40.16 | -0.4725
0.225 | 2.00 | 0.05 | 2828 | -39.38 | -0.4632
0.350 | 2.00 | 0.04 | 4288 | -38.62 | -0.4543
0.500 | 1.66 | 0.03 | 5000 | -37.75 | -0.4441
0.625 | 1.33 | 0.03 | 5000 | -37.05 | -0.4359
0.750 | 1.12 | 0.03 | 5000 | -36.38 | -0.4280
0.875 | 0.96 | 0.04 | 5000 | -35.73 | -0.4204
1.000 | 0.84 | 0.04 | 5000 | -35.11 | -0.4130
5.000 | 0.17 | 0.09 | 5000 | -22.51 | -0.2649

## Slide 12: Au Target - 5.0 MeV
Target Thickness (µm) | I (µA) | Time (hr) | DAQ Rate (Hz) | Asym (%) | Seff
0.050 | 2.00 | 0.85 | 336 | -43.77 | -0.5150
0.100 | 2.00 | 0.44 | 472 | -43.20 | -0.5083
0.225 | 2.00 | 0.21 | 812 | -41.84 | -0.4922
0.350 | 2.00 | 0.14 | 1151 | -40.57 | -0.4773
0.500 | 2.00 | 0.11 | 1559 | -39.14 | -0.4604
0.625 | 2.00 | 0.09 | 1898 | -38.88 | -0.4473
0.750 | 2.00 | 0.08 | 2239 | -36.96 | -0.4349
0.875 | 2.00 | 0.07 | 2579 | -35.96 | -0.4231
1.000 | 2.00 | 0.07 | 2918 | -35.02 | -0.4120
5.000 | 0.73 | 0.12 | 5000 | -19.01 | -0.2237

## Slide 13: Au Target - 8.0 MeV
Target Thickness (µm) | I (µA) | Time (hr) | DAQ Rate (Hz) | Asym (%) | Seff
0.050 | 2.00 | 3.59 | 241 | -38.98 | -0.4586
0.100 | 2.00 | 1.87 | 282 | -38.19 | -0.4493
0.225 | 2.00 | 0.92 | 383 | -36.35 | -0.4277
0.350 | 2.00 | 0.65 | 485 | -34.68 | -0.4080
0.500 | 2.00 | 0.50 | 608 | -32.86 | -0.3866
0.625 | 2.00 | 0.44 | 709 | -31.49 | -0.3705
0.750 | 2.00 | 0.40 | 811 | -30.23 | -0.3556
0.875 | 2.00 | 0.37 | 913 | -29.06 | -0.3419
1.000 | 2.00 | 0.35 | 1015 | -27.98 | -0.3292
5.000 | 2.00 | 0.33 | 4276 | -12.79 | -0.1504