## Slide 1: Jefferson Lab: Inverted Insulator Photogun
CEBAF 200 kV Gun
350 kV gun for GTS and UITF
with optimized triple point shields and mildly conductive insulators
Both designs, maximum field strength < 10 MV/m

## Slide 2: Jefferson Lab: High Voltage (200-350 kV) Inverted Insulator Photo-guns
CEBAF 200 kV
Installed June 2018
(operates at 130kV until an upgrade in 2020)
UITF 350 kV
Polarized Gun
Under assembly
GTS 350 kV
In operation since Nov 2016 with CsK2Sb photocathode

## Slide 3: Metric of Success: High Voltage without Field Emission
Reached
360 kV in 70 hours
Vacuum and radiation levels indistinguishable from background at 350kV
10 MV/m at 350 kV

## Slide 4: Magnetized Beam Photogun at the Gun Test Stand (GTS)
Load-lock inverted insulator photo-gun (multiple photocathodes), like CEBAF geometry.
Cable connection from HVPS to gun.
Over 1000 hours operating >300kV; HV conditioning about 1 week.
Operating with CsKSb photocathodes at >10 mA average current, and 0.7nC bunch charge.
Magnetized Beam LDRD, PI's: R. Suleiman and M. Poelker

## Slide 5: Higher voltages present a challenge
The 350 kV FEL vent-bake gun is based on large cylindrical insulators
Demonstrated 10 mA with with ~500 Coulombs 1/e lifetime
Takes about 4 weeks to replace a photocahode (no load-lock)
Requires large SF6 filled tank to connect with high voltage power supply
Electrodes
Vacuum chamber
Ceramic stand-offs
Corona shield
High voltage feed
(3) 1000 l/s NEG pumps
RGA, extractor gauge
and leak valve
Photocathode
Photocathode retractor mechanism
80 cm
End flange
End flange
Anode

## Slide 6: Our quest for higher voltage inverted insulator guns using cables
CEBAF 200 kV Gun
350 kV GTS Gun
The next step:
400 kV
R&D !
R28 200kV
R30 300kV
R350, 400kV ?
12"
CONCEPT !

## Slide 7: The next step: our 400kV R&D plan
Can the commercial plugs and receptacles be operated at 400kV sustained for days?
What is the highest voltage limit before breakdown?
Design coupling between large insulator and R350 cable plug
  (spinoff: partner with industry to design new conical insulator to mate with commercial R350 cable plug as done now for 200kV and 300kV)
Test all of this in SF6-filled chamber
Design electrode and triple junction shields
Build and test in vacuum, likely will need larger chamber to keep gradient < 10 MV/m at 450kV
Success? Then:
Our HV chamber