## Slide 1: 200 kV Gun and Electron Transport Operations and Concerns from Source Group Perspective
Joe Grames
June 13, 2018

## Slide 2
Motivation
  130 keV Gun
  Injector Upgrade
Major Components of the Upgrade
  200 kV Electrode
  High Voltage Power Supply
  SF6 Management
  Addition of modified M20 BPM’s
Injector Operations
  Routine 130 keV operations (until QCM 2020)
  Test injector performance w/ 200 keV “probe beam’
  Study 200 keV beam (PQB, Lifetime, Transmission)
Outline

## Slide 3
CEBAF Polarized Inverted Load Lock Gun (Spring 2017)
CEBAF Gun 2 (130kV)

## Slide 4
Injector Upgrade Project
Stage 1 - Increase gun voltage and Wien filters for 200kV operation
Stage 2 - Locate Wien filters (energy filter) upstream of pre-buncher cavity
Stage 3 - New SRF booster eliminates warm capture, RF deflection and x/y coupling
Our new “1/4 cryomodule”:
2 cell capture section + 7 cell cavity,
should provide 10 MeV beam and introduce no x/y coupling, allow better matching, more adiabatic damping
200 kV

## Slide 5
Modify spare CEBAF/ILC gun for reliable 200 kV operation
  Retain extreme high vacuum (XHV) 1E-12 Torr
  Reliable 200 kV operation w/o field emission
Work of G. Palacios, C.H. Garcia
200 kV Gun Design Goals

## Slide 6: COMSOL model of gun improvements
Work of G. Palacios, C.H. Garcia
Original CEBAF Inverted Electrode @ 200 kV
Upgraded Electrode @ 200kV
Pure alumina insulator
No triple point shielding
Mildly conductive alumina insulator for charge dissipation
Triple point shielding to prevent arcing across HV plug

## Slide 7
Side-by-Side Comparison (May 2018)

## Slide 8
Testing the 200 kV Electrode/Gun at UITF
HV conditioned to 227 kV (w/ Kr) using the 450 kV Glassman HVPS
Field emission onset >200 kV
Operated the gun at 200 kV routinely w/ stable vacuum and low radiation monitor levels

## Slide 9
Making 200 keV Beam using the 200 kV Electrode at UITF
  Delivered beam to dumps (upstream of new QCM)
Incident laser through hole
Retroreflection from photocathode
200 keV beam on first viewer

## Slide 10
Tunnel Penetration
Tunnel Floor
Gun
Little Oil Tank
ISB Rack
Big Oil Tank
HV Interlocks
PSS/MPS
Bus Bar
Gun Switches (x3)
HV Switch
Ross Probe (1000:1)
Bias Switch
Bus Bar
Short
Resistor
Glassman (150kV)
Software
HV Enable
Knife Switch
Ross Probe DVM
Slow Lock (software)
Battery Bias (cathode)
QE scan
Before (150kV)
Tunnel Penetration
Tunnel Floor
Gun
ISB Rack
HV Interlocks
PSS/MPS
Glassman (350 kV)
Software
HV Enable
Knife Switch
Battery Bias (anode)
QE scan
350kV HVPS
SF6 Tank
(Short or 200 Mohm)
Now (350kV max)
Upgrading the CEBAF HVPS for 200 kV Operation

## Slide 11
CEBAF Glassman 350 kV HVPS
High Voltage Ops (Power/Beam)
HVPS Enabled = Making Beam
Stages rectify 5 kV AC waveform
Max voltage at torus : -350 kV
Max current at torus : 4.5 mA
Low Voltage Ops (Restricted)
HVPS Disabled = QE Wafer Scan
Stages rectify 18V AC waveform
Max voltage at torus : -28 V
Max current at torus : 6 microAmp

## Slide 12
SF6 Pressure Tank
Design Authority : George Biallas
Docushare : PS-ACC-17-001
Parameter | Pressure
Vessel rating | 100 psi
Burst valve | 75 psi
Operating | 60 psi
HVPS Interlock | 55 psi

## Slide 13
SF6 Recovery System (June 11, 2018)
SF6 transfers are performed using the DILO D-320-R006 B143R01 Gas transfer and recovery unit.
Charging : SF6 Alum. Cylinder to Tank
Recovery : Tank to SF6 storage
Pumpdown : Tank evacuation (venting)
J. Willliams (EHS&Q) formalizing SF6 spill assessment – amounts to < 3” above floor surface.
Parameter | Value
Tank Volume | 25 cf
SF6 weight (60psi) | 47 lb
Alum. Bottle Capacity | 75 lb
Alum. Bottle Lifetime | 5 years
J. Hansknecht, “SF6 Gas Transfer Tech Note” (February 1, 2017)

## Slide 14
150kV/350kV HVPS Controls (IN01B01)
Glassman 350 kV Controller
350 kV Interlock Interface Unit
150 kV Interlock Interface Unit
Glassman 150 kV Controller/Supply
Multimeters (PS Voltage/Current)
Same for 150/350 kV Systems

## Slide 15
350 kV HVPS Operations Control (Software)
Glassman Interface
Turn supply ON/OFF (when HV Ready)
Set and Read PS Voltage and Current
Monitors Gun Performance + SF6
Writes limits to Glassman controller
Controls Ramp rates
HV Enable Interlocks (PSS, SF6, Dipole, Gun Valve, Gun Vac, Bias Circuit)

## Slide 16
Augment NEG tube w/ BPM’s
Improve gun monitoring
Restore “Spot Move Steer”
Include S/H cards for PQB tests
Mapped on Gabou test stand
Explore 2nd moment
Adding Modified M20 BPM’s to the NEG tube

## Slide 17
 | T | E | g | p | BL | PS | Current Density
 | [MeV] | [MeV] | [#] | [MeV/c] | [G-cm] | [A] | [A/mm2]
T-Gun | 0.100 | 0.611 | 1.196 | 0.335 | 291.476 | 2.024 | 2.459
Inv. Gun | 0.130 | 0.641 | 1.254 | 0.387 | 336.747 | 2.339 | 2.841
 | 0.150 | 0.661 | 1.294 | 0.419 | 364.851 | 2.534 | 3.079
Upgrade | 0.200 | 0.711 | 1.391 | 0.494 | 430.186 | 2.987 | 3.630
 | 0.250 | 0.761 | 1.489 | 0.564 | 490.704 | 3.408 | 4.141
 | 0.300 | 0.811 | 1.587 | 0.630 | 548.002 | 3.806 | 4.624
UITF (Max) | 0.350 | 0.861 | 1.685 | 0.693 | 603.000 | 4.187 | 5.088
 | 0.400 | 0.911 | 1.783 | 0.754 | 656.275 | 4.557 | 5.538
MAX HVPS | 0.450 | 0.961 | 1.881 | 0.814 | 708.217 | 4.918 | 5.976
15° Dipole (MDS1I01) at 200 keV
AWG#18 Round Ampacity = 7 A
Designers Rule of Thumb < 5 A/mm2
We have tested a DS dipole at 3.5A, sufficient 200 keV beam, and operated safely at UITF.

## Slide 18
 |  |  |  |  |  | FH | FB | FA | FQ |  | FH | FB | FA | FQ
 | T | E | g | p | F=0.5m | 861.780 | 998.820 | 1111.030 | 1342.440 | F=0.75m | 861.780 | 998.820 | 1111.030 | 1342.440
 | [MeV] | [MeV] | [#] | [MeV/c] | [G2-m] | [A] | [A] | [A] | [A] | [G2-m] | [A] | [A] | [A] | [A]
T-Gun | 0.100 | 0.611 | 1.196 | 0.335 | 998.729 | 1.077 | 1.000 | 0.948 | 0.863 | 665.820 | 0.879 | 0.816 | 0.774 | 0.704
Inv. Gun | 0.130 | 0.641 | 1.254 | 0.387 | 1333.063 | 1.244 | 1.155 | 1.095 | 0.997 | 888.709 | 1.016 | 0.943 | 0.894 | 0.814
 | 0.150 | 0.661 | 1.294 | 0.419 | 1564.854 | 1.348 | 1.252 | 1.187 | 1.080 | 1043.236 | 1.100 | 1.022 | 0.969 | 0.882
Upgrade | 0.200 | 0.711 | 1.391 | 0.494 | 2175.486 | 1.589 | 1.476 | 1.399 | 1.273 | 1450.324 | 1.297 | 1.205 | 1.143 | 1.039
 | 0.250 | 0.761 | 1.489 | 0.564 | 2830.624 | 1.812 | 1.683 | 1.596 | 1.452 | 1887.082 | 1.480 | 1.375 | 1.303 | 1.186
 | 0.300 | 0.811 | 1.587 | 0.630 | 3530.269 | 2.024 | 1.880 | 1.783 | 1.622 | 2353.512 | 1.653 | 1.535 | 1.455 | 1.324
CEBAF (Max) | 0.350 | 0.861 | 1.685 | 0.693 | 4274.420 | 2.227 | 2.069 | 1.961 | 1.784 | 2849.614 | 1.818 | 1.689 | 1.602 | 1.457
CEBAF Solenoids at 200 keV
We have re-mapped lens types for 200 keV operation and safely operated at them at UITF:
Type | Element(s) | Old Limit/Map (A) | New Limit/Map (A) | Comment
FH | MFH2I01 | 2 | 3 | OK
FB | MFB1I02 | 2 | 3.5 | OK
FA | MFA0I03/5/6 | 1.5 | 2.5 | OK
FQ | MFQ0I01 | 2 | 2.5 | OK
FD | MFD0I04 | 1 | 1.75 | Will one 20A supply work ?
FG | MFG1I04A/B |  |  | TBD

## Slide 19
Chopper Operation at 200 keV
CEBAF 499 MHz chopper studies for 200 keV Ops (May-June 2018)
  200 keV operation requires ~200 W per channel (C1X,C1Y,C2X,C2Y)
  Drive line attenuators (not probes) removed to provide higher power
Cable maintenance performed
  Requires standard chopper setup (phasing), to be done initially at 130 keV
  Restore original 130 keV probe values (measure new drive values)
Test performance at 200 keV
  Perform chopper setup with increased power levels to set (measure) chopping circle
  Benchmark R/Q at desired power levels for chopping
Parameter | Forward (W) | Reflected (W)
C1X | 200 | 1
C1Y | 200 | 10
C2X | 194 | ?
C2Y | 215 | ?

## Slide 20
Spares and Contingencies
Function | Spare | Contingency
Electrode | Fabricate w/ shed(s) | 130 kV SS electrode 200 kV Nb electrode
High Voltage Power Supply | 450 kV Glassman | 150 kV Glassman Rollback
350 kV Interface Unit | (2) Tested Spares | 150 kV Glassman Rollback
R350 Socket | (2) Spare on shelf | 150 kV Glassman Rollback
R350-R28 HV Cable | (1) Spare due July (1) Purcahse add’l | 150 kV Glassman Rollback
200 MOhm resistor pair | (1) Spare UITF | 150 kV Glassman Rollback
Short | (1) Spare UITF | 150 kV Glassman Rollback
SF6 Tank | (1) Spare UITF | 150 kV Glassman Rollback
SF6 Gas | (1) Order cylinder or GTS | 150 kV Glassman Rollback
SF6 Recovery Al Cylinder | (1) Replace 2nd cylinder (5 yr) | 150 kV Glassman Rollback
The following table is in the context of a 200 keV capable gun.
Items in red need to be purchased or fabricated.

## Slide 21
Spares and Contingencies (con’t)
Function | Spare | Contingency
SF6 Pressure Monitor | (1) Spare system at UITF | 150 kV Glassman Rollback
Low Voltage Bias Circuit | (2) Spare at UITF and GTS | Ground electrode
Keithley PS Voltage Monitor | (3) UITF, Vacuum Lab 1137 | n/a
Keithley PS Current Monitor | (3) Same as Keithley voltage | n/a
The following table is in the context of a 200 keV capable gun.
Items in red need to be purchased or fabricated.

## Slide 22
Summer 2018 SAD Plans and Gun2 Status
May – June
  Replace Gun2 electrode one w/ shed + conductive insulator
  Install and commission 350 kV HVPS
  Replace existing NEG tube w/ one that has two BPM’s
June – July
  High voltage condition to 200 kV (no beam)
  Restore at 130 keV to quantify electrode, HVPS stability, NEG tube BPM’s, PSS kicker
  Transition to 200 keV beam, define PSS kicker, test beam line (magnets + choppers at 200 keV)
  Quantify 200 keV beam (lifetime, PQB, transmission/emittance)