## Slide 1: JLEIC Interaction Region
Vacuum system design and modeling for the
Jefferson Lab
Electron Ion Collider
Interaction Region
Marcy Stutzman for the
JLEIC IR working group
Friday July 5, 2019

## Slide 2: US Department of Energy National Labs
Jefferson Lab
Newport News
Virginia, USA

## Slide 3: Thomas Jefferson National Accelerator Facility
12 GeV electrons, recirculating linear accelerator
Up to 90% polarization from DC photoemission source
Electron currents to 200μA beam (CW) to four experimental halls
Study nucleon structure and interactions
Halls A, B, C
Hall D
Source

## Slide 4: July 2018: National Academy of Science Priority
Recommendation of US-Based Electron Ion Collider
High-energy, high-luminosity polarized beams
Brookhaven National Laboratory and Jefferson Lab have already developed preliminary plans for EICs that would take advantage of existing on-site accelerators.
EIC goals: answer questions in quantum chromodynamics (QCD)
  Nucleon mass
  Spin properties of nucleons
  Gluon role within nuclei
Build on experiments from
  RHIC at BNL
  CEBAF at Jefferson Lab
  HERA at DESY

## Slide 5: JLEIC Layout
100m
12 GeV CEBAF
Electron source
Interaction
point
Electron complex
CEBAF
Electron collider ring
  3000 mA @ 5GeV/c
  400 mA @ 12GeV/c
Up to two detectors at minimum background locations
Crab Crossing for Luminosity
Figure 8 for Polarization Preservation
Ion complex
SRF linac: 150 MeV for protons
Low / High Energy Boosters
Ion collider ring: 100 (200) GeV/c
Ion Source and booster

## Slide 6: HERA Interaction Region Vacuum
Luminosity upgrade dealt with background issues
Synchrotron Radiation
  Degradation of vacuum
Beam gas interactions
  Radiation / beam spread
Higher order mode losses
  Heating
  Degradation of vacuum
Ref: Uwe Schneekloth, EIC workshop 2008
Lessons Learned
Need Excellent Vacuum System
Need careful design of IR and masks

## Slide 7: JLEIC interaction region working group
“R&D Proposal for EIC Background Studies and the Impact on the IR and Detector design”
Simulations of synchrotron radiation and beam-gas interactions
Latifa Elouadrhiri: JLab physics
Charles Hyde: ODU physics
Vasiliy Morozov: JLab accelerator
Christine Ploen: ODU physics
Marcy Stutzman: JLab accelerator
Mike Sullivan: SLAC physics
Yulia Furleova: JLab physics
Mark Wiseman: JLab engineering
Andrey Kim: UConn physics
Vitaly Baturin: ODU physics
Youri Sharabian: JLab physics
Nick Markov: JLab physics
Kyungseon Joo: UConn physics
Pavel Degtiarenko: JLab RadCon
Frank Marhauser: JLab RF
Collaboration between
Accelerator optics
Detector experts
Engineering
Radiation Control
Notable quotes
  “There have to be stanchions to support the beam pipe?”
  “That background radiation from the electron beam hitting the ion beam is my physics result!”

## Slide 8: JLEIC Interaction Region Design Iterations
Elctron
beam
Ion
beam
Synchrotron radiation mask
60 mm ID ion beam exit tube
40 mm ID ion beam entrant tube
60 mm ID electron beam entrant and exit tube
~2390 mm
beryllium central chamber
Central IR chamber
Change from hourglass shape to funnel
  Reduce impedance heating
  Reduce outgassing, required pumps
old

## Slide 9: Interaction Region Detector System
Solenoid magnet
Calorimeter for e- endcap
GEM tracker surrounding IR
Cryostats upstream & downstream for superconducting quadrupoles
Vacuum pumps need to fit in there
Pumps
e-

## Slide 10: Interaction Region: Molflow+ pressure simulations
CAD design has been integrated into Molflow+
Assumptions
  Outgassing rate 1x10-12 mbarLs-1cm-2
  Idealized pumps now
    NEG/ion pumps later
  Cryogenic sections at 4.5K
    Outgassing rate ~0
    Sticking factor ~0.1
  Cryogenic transition sections from 293 to 4.5K
    Approximated as 77 K
    Sticking factor 0.01
Molflow+ model of IR

## Slide 11: Room temperature beamline pressure distribution
e-
ion
200 L/s
2500 L/s
750 L/s
1500 L/s
200 L/s
130 L/s
150 L/s
1500 L/s
650 L/s
Chart: Beamline position s(cm)
| -936 | -935.7 | -926 | -926 | -795.7 | -795.7 | -700 | -560 | -440 | -398.55 | -250 | -208.8 | -208.8 | -208.5 | -178.8 | -132 | -132 | -121.5 | -122 | 0 | 141 | 141.4 | 151 | 151 | 233.2 | 240 | 243.2 | 244.5 | 254.5 | 254.5 | 284.45999999999998 | 326 | 446 | 487.53999999999996 | 487.53999999999996 | 517.54 | 528 | 527.5 | 538 | 538 | 639.5 | 669.5 | 801 | 961 | 1358.4 | 1358.4 | 1383.4 | 1383.4 | 1393 | 1393
electron line warm | 1e-08 | 650 | 650 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 200 | 200 | 1e-08 | 1e-08 | 1e-08 | 200 | 200 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1500 | 1500 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 750 | 750 | 1e-08
ion line warm | 1e-08 | 650 | 650 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 130 | 130 | 1e-08 | 1e-08 | 1e-08 | 150 | 150 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 2500 | 2500 | 1e-08

## Slide 12: Beamline pressure distribution: magnets cold
e-
ion
Chart: Beamline position s(cm)
| -936 | -935.7 | -926 | -926 | -795.7 | -795.7 | -700 | -560 | -440 | -398.55 | -250 | -208.8 | -208.8 | -208.5 | -178.8 | -132 | -132 | -121.5 | -122 | 0 | 141 | 141.4 | 151 | 151 | 233.2 | 240 | 243.2 | 244.5 | 254.5 | 254.5 | 284.45999999999998 | 326 | 446 | 487.53999999999996 | 487.53999999999996 | 517.54 | 528 | 527.5 | 538 | 538 | 639.5 | 669.5 | 801 | 961 | 1358.4 | 1358.4 | 1383.4 | 1383.4 | 1393 | 1393
electron line cold | 1e-08 | 650 | 650 | 1e-08 | 1e-08 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1.3 | 1e-08 | 1e-08 | 1e-08 | 200 | 200 | 1e-08 | 1e-08 | 1e-08 | 200 | 200 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1.6 | 1.6 | 1.6 | 1.6 | 1.6 | 1e-08 | 1e-08 | 1500 | 1500 | 1e-08 | 1e-08 | 1.4 | 1.4 | 1.4 | 1.4 | 1.4 | 1e-08 | 750 | 750 | 1e-08
ion line cold | 1e-08 | 650 | 650 | 1e-08 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 130 | 130 | 1e-08 | 1e-08 | 1e-08 | 150 | 150 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 1e-08 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 1e-08 | 2500 | 2500 | 1e-08
Cryogenic transition: 293 to 4.5K
  Approximated as 77 K
  Sticking factor 0.01
Cryogenic sections at 4.5K
  Outgassing rate ~ 0
  Sticking factor ~ 0.1 (underestimate)

## Slide 13: Pressure profiles: 293K and 4.5K static vacuum
Significant cryopumping due to quadrupole beamline at 4.5K
IR pressure ~3x10-10 mbar
Highest pressure
  1x10-9 mbar, upstream ion line
  Background from ion gas interaction: detector background?
  GEANT4 simulations in parallel for detector background rates
Chart: Ion Line Pressure Profile
labels | 1e-08 | 1e-09 | 1e-10 | 1e-11 | 1e-12
ion
Chart: Electron Line Pressure Profile
labels | 1e-08 | 1e-09 | 1e-10 | 1e-11 | 1e-12

## Slide 14: Cold Magnet Bore Saturation: Cryopumping on bare steel
Time to Monolayer formation depends on
Pressure
Gas composition
Temperature
Sticking coefficient
Surface area
Time to monolayer formation
t(saturation) < 1month ion upstream
t(saturation) > 1 year ion downstream
Mitigation required?
Differential pumping
Cryosorber in beamline
Refs. Kersevan JUAS 2017
Crawford Hydrogen in the LCLS2 Beamline Vacuum

## Slide 15: HERA synchrotron radiation Molflow+/Synrad Benchmark
HERA High Lumi upgrade
Summer student, published literature
  Beamline cross sections
  Magnet strengths
  Ideal electron beam
  Quad/Dipole simplified to Dipole
Comparisons to published
  Synchrotron radiation power
  Vacuum performance
    ongoing
Geometry, simulation by Adam Hutchinson
Louisiana State University through the US DOE
SULI summer undergraduate research program
Power (W/cm2)
e-
Ion / e+
Preliminary
~ 6kW

## Slide 16: Applying lessons learned from HERA
Synchrotron Radiation
  Last e- dipole ~75m upstream
Beam gas interactions
  Design upstream ion line vacuum to minimize gas
  Studying ion & e- beam induced synch. radiation
Higher order mode losses
  Chamber material
  Collimator size, position

## Slide 17: Synrad model of JLEIC Interaction Region: 12 GeV
12 GeV beam, 390 mA current
e- optics, 3 upstream quads
Collimator
  12 mm radius, 1 m upstream
Synchrotron radiation
  Collimator max 100 W/cm2
  Collimator total power <10W from quad synch rad
  IR walls μW/cm2
  Downstream absorber mW/cm2
Synch light from Beam gas interactions? GEANT4 simulations
e-
ion
collimator
End of simulation
(100% absorbed)

## Slide 18: Conclusions
FUTURE
Effect of Beam: radiation/heating
Engineering design of pumping
  Space constraints
Bremstrahlung from beam gas interactions: ions and electrons
Refine Gas load into cryogenic magnets
Collimator optimization
DownSelect between
  Jefferson Lab JLEIC
  Brookhaven eRHIC
Questions?
SUMMARY
JLEIC IR Background working group: physics, engineering, accelerator, radcon
Detectors, cryogenic quadrupoles: little room for pumping
Experience at HERA shows vacuum, synchrotron radiation management critical
Molflow+ calculations for vacuum distribution
  First try for static warm & cryo
Synchrotron radiation calculations
  Synrad compared to 2D code from SLAC
Molflow+/Synrad calculations for HERA: benchmark

## Slide 19: Backup

## Slide 20: Comparing JLEIC and HERA beam parameters
JLEIC
Electrons
  5 GeV electrons 3000 mA
  12 GeV electrons 390 mA
Ions
  40 GeV at 450 mA
  200 GeV ions at 750 mA
Luminosity > 2x1034 cm-2s-1
High Polarization: figure-8 ring design
  Complete cancellation of spin precession in left/right arcs (net spin precession zero, energy-independent)
  Spin easily controlled by small magnetic fields for any particle species
Full acceptance primary detector including far-forward acceptance
HERA
27.5 GeV electrons, 58 mA
820 GeV positrons, 140 mA
Luminosity 7x1031 cm-2s-1
Beam Design
High repetition rate
Low bunch charge
Short bunch length
Small emittance
IR Design
Small β*
Large beam-beam
Crab crossing
Damping Design
Synch. radiation
Beam cooling

## Slide 21: JLEIC Parameters and Luminosity Performance
CM energy | GeV | 21.9 |  | 44.7 |  | 63.3 |  | 89.4 |  | 98 | 
 |  | p | e | p | e | p | e | p | e | p | E
Beam energy | GeV | 40 | 3 | 100 | 5 | 200 | 5 | 200 | 10 | 200 | 12
Collision frequency | MHz | 476 |  | 476 |  | 476/2=238 |  | 476/4=119 |  | 476/4=119 | 
Particles per bunch | 1010 | 0.59 | 3.9 | 0.98 | 4.7 | 1.97 | 6.8 | 3.93 | 4.2 | 3.93 | 2.05
Beam current | A | 0.45 | 3 | 0.75 | 3.5 | 0.75 | 2.58 | 0.75 | 0.8 | 0.75 | 0.39
Polarization |  | 85% | >85% | 85% | >80% | 85% | >80% | 85% | ~80% | 85% | ~80%
RMS bunch length | cm | 2.5 | 1 | 2.5 | 1 | 2.1 | 1 | 4 | 1 | 4 | 1
Norm. emitt, hori. | mm mrad | 0.5 | 18 | 0.65 | 83 | 0.96 | 83 | 3.1 | 664 | 3.1 | 1145
Norm. emitt, vert. | mm mrad | 0.2 | 3.6 | 0.13 | 16.6 | 0.25 | 16.6 | 1.5 | 133 | 1.5 | 229
Horizontal β* | cm | 8 | 30 | 8 | 5.72 | 21 | 11.2 | 21 | 9.1 | 21 | 6.6
Vertical β* | cm | 1.3 | 9.8 | 1.3 | 0.93 | 1.6 | 1.1 | 1.6 | 1.65 | 1.6 | 1.15
Beam-beam, hori. |  | 0.015 | 0.12 | 0.015 | 0.045 | 0.015 | 0.09 | 0.003 | 0.02 | 0.0013 | 0.014
Beam-beam, vert. |  | 0.01 | 0.15 | 0.013 | 0.041 | 0.008 | 0.065 | 0.001 | 0.02 | 0.0005 | 0.012
Laslett tune-shift |  | 0.055 | small | 0.018 | small | 0.008 | Small | 0.0014 | Small | 0.0014 | Small
Hour-glass (HG) |  | 0.85 |  | 0.73 |  | 0.82 |  | 0.73 |  | 0.67 | 
Peak lumi., w/ HG | 1033/cm2s | 3.2 |  | 14.7 |  | 15.5 |  | 1.9 |  | 0.86 | 
Average lumi.* | 1033/cm2s | 2.3 |  | 10.6 |  | 9.3 |  | 1.6 |  | 0.71 | 
* Average luminosity was calculated assuming a one or two hour proton beam store without or with high energy bunched beam electron cooling plus 5 min beam formation time (mainly due to detector overhead), and a 75% duty factor of machine operation.

## Slide 22: Synchrotron Radiation Collimator
Limit Synchrotron radiation at IR
  Pumping constriction
  Impedance heating

## Slide 23: Synchrotron radiation power
Chart: Power on collimator

## Slide 24
marcy@jlab.org
Marcy Stutzman
Thomas Jefferson National Accelerator Facility
SUMMARY
JLab Electron Ion Collider interaction region background working group: physics, engineering, accelerator, radcon
Detectors, cryogenic quadrupoles: little room for pumping
Experience at HERA shows vacuum, synchrotron radiation management critical
Molflow+ calculations for vacuum distribution
  Dynamic vacuum with heating
Synchrotron radiation calculations
  Synrad compared to 2D code from SLAC
Molflow+/Synrad calculations for HERA: benchmark