## Slide 1: Polarized Electron Source: A brief introduction
Joe Grames

## Slide 2
Outline
Part I - Photocathodes
  Electron emission
  GaAs
  PEA & NEA & QE
  Polarization
  Higher polarization
  Even higher polarization
Part II - Photoguns
  High Voltage
  Drive Laser
  Extreme High Vacuum
2

## Slide 3
Accelerators need “free” electrons ! How might we acquire them?
Field Emission (electronic energy)
Thermionic Emission (thermal energy)
Photo Emission (optical energy)
All are manifestations of electromagnetism
3

## Slide 4
The Canonical Emission Equations
Field Emission Fowler Nordheim E.L. Murphy, and R.H. Good, Physical Review 102, 1464 (1956).
Thermal Emission Richardson-Laue-Dushman C. Herring, and M. Nichols, Reviews of Modern Physics 21, 185 (1949).
Photoemission Fowler-Dubridge L.A. DuBridge Physical Review 43, 0727 (1933).
(slide courtesy of Dr. K. Jensen, Naval Research Laboratory)
4

## Slide 5: Photo Emission from GaAs
Bare GaAs surface
Large Work Function
Positive Electron Affinity (PEA)
PEA=4.07 eV
Egap
Conduction
Band
Valence
Band
GaAs
Vacuum
Dipole layers of
Cesium + NF3
Reduces Work Function
Negative Electron Affinity (NEA)
+
-
-
χNEA ~ 0.2 eV
GaAs
Vacuum
Light
NEA Surface Activation
5

## Slide 6
Quantum Efficiency
Photons IN
Electrons Out
In practical terms, the quantum efficiency “QE” is the metric used to assess the number of electrons emitted per number of illuminating photons.
Al-Naser, Qusay & Hilou, Hassan & Abdulkader, Abbas. (2009). The last development in III-V multi-junction solar cells. 1. 10.1109/CCCM.2009.5268104.
6

## Slide 7
Beam Polarization
P = (N+ - N-)/(N+ + N-)
The polarization is defined as the net fraction of spin states along a preferred direction; photoemission is oriented along the beam helicity.
(2 - 2) / (2 + 2) = 0%
(3 - 1) / (3 + 1) = 50%
Modern high polarization photocathodes provide spin alignment of about 19 out of 20 electrons
7

## Slide 8
Spin Polarized Photoemission from Bulk GaAs
Laser excitation from P3/2 to S1/2 : Egap < E < Egap+Δ
Electron Polarization:
Reverse electron polarization by reversing light polarization
σ+: Right circularly polarized light
σ- : Left circularly polarized light
mj
E
-1/2
+1/2
J
P1/2
-3/2
-1/2
+3/2
+1/2
P3/2
-1/2
+1/2
S1/2
σ+
σ-
3
1
S1/2
P3/2
P1/2
Egap=1.42 eV
Δ=0.34 eV
E
k
EF
3
1
8

## Slide 9
First Observation of Polarization from GaAs
9

## Slide 10
First HV GaAs photogun used on an accelerator
Built for SLAC parity-violation experiment E122
December 1977 - Polarized electrons accelerated at SLAC
June 1978 - E122 announces parity violation (Standard Model)
10

## Slide 11: How is the spin polarization used?
Target
You measure
an experimental
asymmetry !
11

## Slide 12: Parity Violation Experiments at Jefferson Lab
PV experiments have motivated polarized e-source R&D
12

## Slide 13: What does “APV = 234 ppb” even mean?
Target
1,000,000,000
A
B
A - B
1,000,000,000
A = 500,000,117
B = 499,999,883
= 0.000000234
e = (A - B)/(A + B)
13

## Slide 14
Polarized source figure of merit (FOM)
= (A - B)/(A + B)
= P * A
DA ~ 1/ N=(A+B)
Measured asymmetry
Physics asymmetry
Error on analyzing power
For example, increasing the beam polarization from 30% to 90% achieves the same uncertainty in events needs by (30/90)2 ~ 1/9th the time.
Experiments could be done in one year,
not one decade.
14

## Slide 15
Breaking the P=50% barrier
The band gap of the substrate layer must be larger than surface layer
Lattice constants must differ enough to introduce suitable strain
Adjust lattice constant of substrate by varying concentration of third element
Lattice mismatch provides stress
Pablo Saez, PhD Thesis, SLAC Report 501, 1997
1% lattice mismatch provides equivalent force as hydraulic press!
15

## Slide 16
Strained layer GaAs
MOCVD-grown epitaxial spin-polarizer wafer
+3/2
mj = -1/2
+1/2
S1/2
P3/2
mj = -3/2
-1/2
+1/2
σ+
σ-
Strained GaAs
GaAs1-xPx (x=0.29)
p-type GaAs
substrate
600 μm
250 μm
250 μm
0.1 μm
GaAs1-xPx (0<x<0.29)
Polarization 75% >> 50% 
Strain relaxes in 0.1 mm layer
Not all electrons reach surface
QE 0.1% << 6% 
16

## Slide 17
Strained GaAs
GaAsP
Strained GaAs
GaAsP
Strained GaAs
GaAsP
30 A
30 A
GaAs Substrate
GaAs(1-x)Px Graded Layer
GaAs0.64P0.36
Buffer
Active Region
2.5mm
2.5mm
1000 A
From Aaron Moy, SVT Assoc and SLAC, PESP2002
D. Luh et al, SLAC, PESP2002
QE 1% and Polarization 85%
Strained layer superlattice GaAs/GaAsP
17

## Slide 18
Polarization from GaAs (JLab: 1997 – 2019)
?
workhorse
18

## Slide 19
Standard Photocathode : absorption < 5% in the GaAs/GaAsP superlattice
  Most light passes into the substrate leading to unwanted heating
DBR photocathode : absorption > 20% in the GaAs/GaAsP superlattice
  Less light required to make required beam, less light means less heat
Diffraction Bragg Reflector Strained Superlattice
QE 6% and Polarization 90%
19

## Slide 20: How to make the electrons “energetic” ?
Air ~ 6 MV/m
Sulfur hexafluoride ~15 MV/m
Ceramic ~ 30 MV/m
20

## Slide 21
-130kV
light in
electrons out
photocathode
Applying high voltage to the photocathode
21
<Joe => put GaAs/puck fig here)>

## Slide 22
Polarized electron source
22

## Slide 23: Continuous vs. Pulsed Beams
1 Coulomb
1 Coulomb
23

## Slide 24: …but continuous does NOT mean DC
DC beam (on ALL the time)
2 ns/revolution
A B C
Beam pulse (on each RF cycle)
Short e- bunch <50 psec
24

## Slide 25: Polarized source laser
1560 nm
780 nm
Low-Power (1 mW)
1560 nm Fiber Diode
Follows RF sine wave
Frequency-doubler
1560 nm to 780 nm
30% Efficiency (2 W)
High Power (6 W) 1560 nm Fiber Amplifier
Master Oscillator
499 MHz
200 mW @ 780 nm
50 ps @ 499/249.5 MHz
=> 6 uA/mW/%
25

## Slide 26
CEBAF 4-Beam Drive Laser
Controls intensity, polarization, rep rate
Synchronized with RF, diagnostics
Should be stable, reliable, pragmatic
26

## Slide 27
Fast helicity reversal
Pockels cell λ/2 transition optical result. ~70us with no ringing.
Pockels cell λ/2 flipping at 1kHz.
Perfect symmetry and no voltage droop over time.
Electro-optic waveplate

## Slide 28
Part of the ”bigger picture”

## Slide 29
QE degradation (charge lifetime)
Does QE degrade with time? Yes, and no.

## Slide 30
“The woods were dark and foreboding, and Alice sensed that sinister eyes were watching her every step. Worst of all, she knew that Nature abhorred a vacuum” – Gary Larson
We understand Alice’s worry…
Air ~ 1016 / Torr-cm3
  (molecules ~2 nm apart)
Gun ~ 10-12 Torr
  (molecules ~1 mm apart)

## Slide 31
Ion back-bombardment leads to QE reduction
These ions may strike the photocathode, generate secondary electrons or x-rays, and desorb gas from surfaces; all leading to a reduction of the photocathode quantum efficiency (QE).

## Slide 32
Achieving Extreme High Vacuum
Avoid contamination by oils due to roughing pumps, fingerprints, machining.
Baking used to get pressures below 10-10 Torr
  250°C for 30 hours removes water vapor bonded to surface that otherwise limits pressure
Getter Pumps
  Chemically active surface
    Titanium sublimed from hot filament
    Non-Evaporative Getters
  Molecules stick when they hit
    Does not work well for inert gasses such as Argon, Helium or for methane
Ion Pumps
  Electric field to ionize gasses
  Magnetic field to direct gasses into cathodes where they are trapped
    Has some pumping capability for noble gasses
NEG pump array
Ion Pump

## Slide 33
Vacuum conditions in an accelerator
Application | Pressure Range | Location | Vacuum Regime
Beamline to dumps | 10-5 Torr | Target to dump line | Medium
Insulating vacuum for cryogens | 10-4 Torr to 10-7 Torr | Cryomodules, transfer lines | Medium to high
Targets, Scattering Chambers | 10-6 to 10-7 Torr | Experimental Halls | High to very high
RF waveguide warm to cold windows | 10-7 to 10-9 Torr | Between warm and cold RF windows | High to very high
Warm beamline | 10-7 to 10-8 Torr | Arcs, Hall beamline, BSY, some injector | High to very high
Warm region girders | 10-9 Torr or better | Girders adjacent to cryomodules | Very high to ultrahigh
Differential pumps | Below 10-10 Torr | Ends of linacs, isolate cryomodules | Ultrahigh vacuum
Baked beamline | 10-10 to 10-11Torr | Y chamber, Wien filter, Pcup | Ultra high vacuum
Polarized guns | 10-11 to 10-12 Torr | Photoguns | Ultra to Extreme high vacuum
SRF cavity vacuum | < 10-12 Torr | Inside SRF cavities with walls at 2K | Extreme high vacuum

## Slide 34
Mitigating ion back-bombardment
Work of J. Yoskowitz (Old Dominion University), Proc. of PSTP-2019

## Slide 35
Always Tweaking the Design
The endless (?) quest for perfection
1
3
4
2
5

## Slide 36
I did not cover…
Low energy spin rotations
Dipole
Solenoid
Wien filter
Spin flipping
Low energy polarimetry
Mott Scattering