## Slide 1: Booster Studies
Y. Wang
Feb 28, 2021

## Slide 2: Incoming Beam Conditions
Gun HV: 200 KeV
Chopper: off
Buncher: on, negative slope zero crossing, gset = 40, pset = -65 degs.
Solenoids: beam centered
Apertures #3 and #4: beam centered

## Slide 3: Gradient Calibration of 2-Cell Cavity
2-cell
7-cell
Q501
Q502
Q503
Q504
ITVM601
ITVM703
30 deg.
MDML601

## Slide 4: Gradient Calibration of 2-Cell Cavity
Preparation for beam:
7-cell cavity: off and detuned
MQJM501, 502, 503 and 504: beam centered
MQJM701 and 703: cycled at zero field and turned off
Established good beam to ITVM601
Established good beam to ITVM703
At each gset: cavity on crest and beam centered; quads beam centered; beam path unchanged

## Slide 5: Gradient Calibration of 2-Cell Cavity
Chart: Beam Momentum after 2-cell vs. Gradient
| 3.4 | 3.35 | 3.3 | 3.25 | 3.2 | 3.15 | 3.1 | 3.05 | 3 | 2.95 | 2.9 | 2.85 | 2.8 | 2.75 | 2.7 | 2.65 | 2.6 | 2.5499999999999998 | 2.5 | 2.4500000000000002 | 2.4
 | 1.321 | 1.2564 | 1.2074 | 1.1662 | 1.1315 | 1.1028 | 1.0777 | 1.0574 | 1.0389 | 1.0221 | 1.0066 | 0.99163 | 0.97848 | 0.96593 | 0.95397 | 0.94262 | 0.93246 | 0.9211 | 0.91213 | 0.90197 | 0.89181

## Slide 6: Gradient Calibration of 2-Cell Cavity
Chart: Beam KE gain from 2-Cell vs. Gradient
| 3.4 | 3.35 | 3.3 | 3.25 | 3.2 | 3.15 | 3.1 | 3.05 | 3 | 2.95 | 2.9 | 2.85 | 2.8 | 2.75 | 2.7 | 2.65 | 2.6 | 2.5499999999999998 | 2.5 | 2.4500000000000002 | 2.4
 | 0.70537 | 0.64537 | 0.60009 | 0.56221 | 0.53054 | 0.50445 | 0.48171 | 0.46338 | 0.44673 | 0.43173 | 0.41786 | 0.40455 | 0.39288 | 0.38177 | 0.37121 | 0.36122 | 0.3523 | 0.34235 | 0.33452 | 0.32567 | 0.31684

## Slide 7: Gradient Calibration of 2-Cell Cavity
Chart: Beam Momentum after 7-cell (7-cell gset at 12 MV/m) vs. 2-cell Cavity Gradient
| 3.3 | 3.2 | 3.1 | 3 | 2.9 | 2.8 | 2.7 | 2.6 | 2.5 | 2.4 | 2.2999999999999998 | 2.2000000000000002 | 2.1 | 2 | 1.9 | 1.8 | 1.7 | 1.6 | 1.5 | 1.4 | 1.3 | 1.2 | 1.1000000000000001 | 1 | 0.9 | 0.8 | 0.7 | 0.6 | 0.5 | 0.4 | 0.3 | 0.2 | 0.1 | 0
 | 10.0801 | 9.9791 | 9.9325 | 9.8661 | 9.7974 | 9.7657 | 9.731 | 9.6999 | 9.6736 | 9.6539 | 9.6366 | 9.6186 | 9.5941 | 9.5744 | 9.5421 | 9.5254 | 9.5039 | 9.4883 | 9.4638 | 9.4387 | 9.4011 | 9.3825 | 9.3521 | 9.3216 | 9.2726 | 9.2206 | 9.1668 | 9.0867 | 9.0496 | 8.9647 | 8.8069 | 8.5965 | 8.3652 | 8.2672

## Slide 8: Gradient Calibration of 2-Cell Cavity
The plots in the previous slides are not linear
My explanation is the beam is not fully relativistic yet
either at entrance or exit of the 2-cell cavity.
Energy gains from the 2-cell and the 7-cell
are not simple arithmetic

## Slide 9: Gradient Calibration of 7-Cell Cavity
Preparation for beam:
2-cell cavity: gset at 3.3 MV/m, and on crest
MQJM501, 502, 503 and 504: beam centered
MQJM701 and 703: cycled at zero field and turned off
Established good beam to ITVM601
Established good beam to ITVM703
At each gset: cavity on crest and beam centered; quads beam centered; beam path unchanged

## Slide 10: Gradient Calibration of 7-Cell Cavity
Chart: Beam Momentum after Booster vs. 7-cell Gradient
| 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.43 | 12
 | 2.2445 | 2.5708 | 2.9372 | 3.373 | 3.7143 | 4.0801 | 4.4866 | 4.838 | 5.22 | 5.6228 | 5.9797 | 6.3491 | 6.7322 | 7.0879 | 7.4567 | 7.8512 | 8.2092 | 8.581 | 8.9534 | 9.318 | 9.6342 | 10.0801

## Slide 11: Gradient Calibration of 7-Cell Cavity
Chart: Beam KE Gain from 7-cell Cavity vs. Gradient
| 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10 | 10.5 | 11 | 11.43 | 12
 | 1.1473 | 1.4665 | 1.8268 | 2.2569 | 2.5947 | 2.9574 | 3.361 | 3.7103 | 4.0903 | 4.4914 | 4.8469 | 5.215 | 5.597 | 5.9517 | 6.3196 | 6.7132 | 7.0705 | 7.4416 | 7.8133 | 8.1774 | 8.4931 | 8.9384

## Slide 12: Recommended Settings
2-cell cavity gradient: 2.5 MV/m
  Kinetic energy gain: 334.5 KeV.
7-cell cavity gradient: 7.4 MeV/m
  Beam momentum downstream Booster: 6.3 MeV/c
Very stable beam
  No beam motion observed on spectrometer viewer ITVM703

## Slide 13: Stable 6.3 MeV/c Beam on Spectrometer Viewer

## Slide 14: X/Y Coupling Baseline
Booster: off and detuned
MHB403H&V: steer beam horizontally and vertically using MHB403V
Measure beam positions on ITVM201
ITVM201
7-cell
2-cell
MHB403H&V

## Slide 15: X/Y Coupling Baseline (Booster off)
-2.7°
5.1°
H
V

## Slide 16: X/Y Coupling Caused By Booster
Beam Displacement Direction and Rotation | Baseline (Booster off) | 2-cell (gset = 2.5 MV/m) | 7-cell (gset = 7.4 MV/m) | Booster (6.3 MeV/c)
H, Rotation (deg) (cw = +) | -2.7486863 | 1.082646967 | 3.668817087 | 4.751464054
V, Rotation (deg) (cw = +) | 5.097034794 | 0.807545637 | -1.174272579 | -0.366726942

## Slide 17: Kicks From Cavities
Measure beam positions on ITVM201 with cavities on/off
Calculate angular displacements
2-cell
7-cell
ITVM201
 | Distance to ITVM201 (mm)
2-cell center | 1946.86155
7-cell center | 1116.17185
θ

## Slide 18: Kicks From 2-cell Cavity
Chart: Kicks from 2-cell Cavity vs. Gradient
| 3.4 | 3.35 | 3.3 | 3.25 | 3.2 | 3.15 | 3.1 | 3.05 | 3 | 2.95 | 2.9 | 2.85 | 2.8 | 2.75 | 2.7 | 2.65 | 2.6 | 2.5499999999999998 | 2.5 | 2.4500000000000002 | 2.4
x_kick | 0.14472 | 0.13625 | 0.13158 | 0.12663 | 0.11976 | 0.11605 | 0.11298 | 0.10946 | 0.10625 | 0.10355 | 0.10085 | 0.098968 | 0.093656 | 0.092099 | 0.091595 | 0.089671 | 0.087931 | 0.087015 | 0.084725 | 0.081977 | 0.080604
y_kick | 0.20152 | 0.19257 | 0.18765 | 0.18318 | 0.17758 | 0.17199 | 0.16953 | 0.16573 | 0.16238 | 0.16036 | 0.1579 | 0.15589 | 0.15634 | 0.15365 | 0.14896 | 0.14605 | 0.14404 | 0.14202 | 0.13956 | 0.13733 | 0.13554

## Slide 19: Kicks From 7-cell Cavity relative to 2-cell
Chart: Kicks from 7-cell vs Gradient
| 12 | 11.5 | 11 | 10.5 | 10 | 9.5 | 9 | 8.5 | 8 | 7.5 | 7 | 6.5 | 6 | 5.5 | 5 | 4.5 | 4 | 3.5 | 3 | 2.5 | 2
x-kick | 0.19251 | 0.19052 | 0.18772 | 0.18612 | 0.18373 | 0.18133 | 0.17814 | 0.17494 | 0.17334 | 0.17015 | 0.16775 | 0.16296 | 0.15936 | 0.15497 | 0.14938 | 0.14459 | 0.13859 | 0.12861 | 0.12182 | 0.11024 | 0.095858
y_kick | 0.1104 | 0.11079 | 0.11001 | 0.10962 | 0.10884 | 0.10884 | 0.10845 | 0.10767 | 0.10767 | 0.10845 | 0.10689 | 0.10611 | 0.10494 | 0.10475 | 0.10396 | 0.10318 | 0.10182 | 0.10143 | 0.098698 | 0.095577 | 0.094017

## Slide 20: Kicks From Booster
Chart: Kicks From Booster (2-cell gest = 2.5) vs. 7-cell Gradient
| 12 | 11.5 | 11 | 10.5 | 10 | 9.5 | 9 | 8.5 | 8 | 7.5 | 7 | 6.5 | 6 | 5.5 | 5 | 4.5 | 4 | 3.5 | 3 | 2.5 | 2
x_kick | 0.30115 | 0.29915 | 0.29636 | 0.29476 | 0.29236 | 0.28997 | 0.28677 | 0.28358 | 0.28198 | 0.27878 | 0.27639 | 0.27159 | 0.268 | 0.26361 | 0.25802 | 0.25322 | 0.24723 | 0.23725 | 0.23046 | 0.21887 | 0.2045
y_kick | 0.19506 | 0.19545 | 0.19467 | 0.19428 | 0.1935 | 0.1935 | 0.1931 | 0.19232 | 0.19232 | 0.1931 | 0.19154 | 0.19076 | 0.18959 | 0.1894 | 0.18862 | 0.18784 | 0.18647 | 0.18608 | 0.18335 | 0.18023 | 0.17867

## Slide 21: Some Observations
2-cell and 7-cell are not perfectly aligned: need to adjust MHBK403H by 0.1 Gcm, and MHBK403V by 1.6 Gcm after beam centering 2-cell cavity.
When moving the incoming beam horizontally and vertically with the 2-cell cavity on only and on crest, the exit beam moved accordingly. When the cavity phase was adjusted by -16 degrees the exit beam movement started to change polarity. No polarity changes were observed when the phase was increased.
When moving the incoming beam horizontally and vertically with both cavities on and on crest, the exit beam moved in opposite direction. When the 7-cell cavity phase was adjusted by +10 degrees the exit beam movement started to change polarity. No polarity changes were observed when the phase was decreased. And -/+ 20 degrees adjustment of 2-cell phase did not affect it.
When the incoming beam moves horizontally and vertically with the 7-cell cavity on only and on crest, the exit beam move accordingly. When the 7-cell cavity phase was adjusted by -20 degrees, the exit beam movement started to change polarities. No polarity changes were observed when the phase was increased.

## Slide 22: To Do list
Energy spread
Bunchlength
Adiabatic Damping
(emittances upstream and downstream of Booster)
6.3 MeV/c beam setup with Gun HV at 130 KV

## Slide 23: Correctors and Viewer Used
MHBK403H&V: 20.5” upstream
ITVM201: 10.5” downstream
No other correctors or lenses between MHBK403 and ITVK201
ITVM201
MHBK403H&V
10.5”
Booster
90”
20.5”

## Slide 24: Booster and Upstream MHB403H&V
MHBK403H&V
Fcup and Viewer
Ion Pump
Booster

## Slide 25: Booster and Downstream ITVM201
Booster
ITVM201
Ion pump

## Slide 26: ITVM201 Calibration

## Slide 27: ITVM201 Calibration
Assume 1 pixel in x plane is equal to1 pixel in y plane
ITVM201
θ
Rotation angle (deg) | Conversion | factor (mm/px)
wrt y axis | x | y
26.03 | 0.15561602 | 0.07599734