## Slide 1: CEBAF Polarized Electron Source
JLab Summer Lecture Series, June 27, 2019
Joe Grames
Deputy Group Leader
Center for Injectors and Sources
wiki.jlab.org/ciswiki

## Slide 2
7Li

## Slide 3
Energy scale to probe massive particles…
energy ~ 1/l ~ mass
M ~ 938 MeV/c2
m ~ 0.511 MeV/c2
E = mc2

## Slide 4: What to do?
Build a 5 mile long electron microscope!
Make electrons energetic enough (Ebeam) to peek inside proton or neutron (Mnucleon).
Neutron
Proton
Electron

## Slide 5
Where do we find energetic electrons ?
Storage batteries, power generators, wall-plug power, Nature, movies and… in particle accelerators!!!

## Slide 8: How to make the electrons “energetic” ?
?
?
Accelerating voltage
Decelerating voltage
Electrons gain energy on each crest!
Use oscillating voltage !!!
How about static voltage?
Air ~ 6 MV/m
Sulfur hexafluoride ~15 MV/m
Ceramic ~ 30 MV/m

## Slide 9: The “C” in CEBAF
1 Coulomb
1 Coulomb

## Slide 10: Accelerators need “free” electrons ! How might we acquire them?
Field Emission (electronic energy)
Thermionic Emission (thermal energy)
Photo Emission (optical energy)
All are manifestations of electromagnetism

## Slide 11: The Canonical Emission Equations (slide courtesy of Dr. K. Jensen, Naval Research Laboratory)
Field Emission Fowler Nordheim E.L. Murphy, and R.H. Good, Physical Review 102, 1464 (1956).
Thermal Emission Richardson-Laue-Dushman C. Herring, and M. Nichols, Reviews of Modern Physics 21, 185 (1949).
Photoemission Fowler-Dubridge L.A. DuBridge Physical Review 43, 0727 (1933).

## Slide 12: Field Emitter Sources
Explained by Fowler and Nordheim (1928): a quantum mechanical tunneling effect
Small emission area makes for a very “bright” beam, good for surface science
I = BV2 exp(-C/V)
Vacuum diode
60°
human hair

## Slide 13: Thermionic Emission
Studied since early 1800’s and perfected over 100 years
Thermionic emission from Tungsten filaments and metalloids like LaB6 operating at >1000K are common
>90% of consumed power simply generates heat
Edison’s patent,
Long-lasting filament
Melts 3695K

## Slide 14: Thermionic Emission
Used to make x-ray light….
1880s
X-rays are generated when a DC electron beam, typically a few mA, strikes a tungsten target at 60-200 keV. e-Beam quality is not a big concern
Rotating anode to distribute heat
1930’s
bias at high voltage

## Slide 15: Photo-Emission from bulk GaAs
Bare GaAs surface
Large Work Function
Positive Electron Affinity (PEA)
PEA=4.07 eV
Egap
Conduction
Band
Valence
Band
GaAs
Vacuum
Dipole layers of
Cesium + NF3
Reduces Work Function
Negative Electron Affinity (NEA)
+
-
-
χNEA ~ 0.2 eV
GaAs
Vacuum
Light
NEA Surface Activation
Quantum Efficiency ~ 10% (1e-/10 photons)

## Slide 16
Electron Bunch Spin & Polarization
0% Polarization

v
50% Polarization

v

## Slide 17
Spin Polarized Photoemission from Bulk GaAs
Laser excitation from P3/2 to S1/2 : Egap < E < Egap+Δ
Electron Polarization:
Reverse electron polarization by reversing light polarization
σ+: Right circularly polarized light
σ- : Left circularly polarized light
mj
E
-1/2
+1/2
J
P1/2
-3/2
-1/2
+3/2
+1/2
P3/2
-1/2
+1/2
S1/2
σ+
σ-
3
1
S1/2
P3/2
P1/2
Egap=1.42 eV
Δ=0.34 eV
E
k
EF
3
1

## Slide 18: What about the probing with spin ?
Target
You measure
an experimental
asymmetry !

## Slide 19: Parity Violation Experiments at CEBAF
Experiment | Energy (GeV) | I (µA) | Target | Apv (ppb) | Maximum Charge Asym (ppb) | Maximum Position Diff (nm) | Maximum Angle Diff (nrad) | Maximum Size Diff (δσ/σ)
HAPPEx-II (Achieved) | 3.0 | 55 | 1H (20 cm) | 1400 | 400 | 1 | 0.2 | Was not specified
HAPPEx-III (Achieved) | 3.484 | 100 | 1H (25 cm) | 16900 | 200±100 | 3±3 | 0.5±0.1 | 10-3
PREx | 1.063 | 70 | 208Pb (0.5 mm) | 500 | 100±10 | 2±1 | 0.3±0.1 | 10-4
QWeak | 1.162 | 180 | 1H (35 cm) | 234 | 100±10 | 2±1 | 30±3 | 10-4
Møller | 11.0 | 75 | 1H (150 cm) | 35.6 | 10±10 | 0.5±0.5 | 0.05±0.05 | 10-4
PV experiments motivate polarized e-source R&D

## Slide 20: What does “234 ppb” even mean?
Target
1,000,000,000
A
B
A - B
1,000,000,000
A = 500,000,117
B = 499,999,883
= 0.000000234

## Slide 21: The CEBAF polarized source “Big Three”
Photocathode
Many electrons/photon
High polarization
Fast response time

## Slide 22: Breaking the 50% Barrier
The band gap of the substrate layer must be larger than surface layer
Lattice constants must differ enough to introduce suitable strain
Adjust lattice constant of substrate by varying concentration of third element
Lattice mismatch provides stress
Pablo Saez, PhD Thesis, SLAC Report 501, 1997
1% lattice mismatch provides equivalent force as hydraulic press!
Notes: Interior Page Design 2

## Slide 23
Strained layer GaAs
MOCVD-grown epitaxial spin-polarizer wafer
+3/2
mj = -1/2
+1/2
S1/2
P3/2
mj = -3/2
-1/2
+1/2
σ+
σ-
Strained GaAs
GaAs1-xPx (x=0.29)
p-type GaAs
substrate
600 μm
250 μm
250 μm
0.1 μm
GaAs1-xPx (0<x<0.29)
Strain relaxes in 0.1 mm layer
Not all electrons reach surface
Polarization 75% >> 50% 
QE 0.1% << 6% 

## Slide 24
Strained GaAs
GaAsP
Strained GaAs
GaAsP
Strained GaAs
GaAsP
30 A
30 A
GaAs Substrate
GaAs(1-x)Px Graded Layer
GaAs0.64P0.36
Buffer
Active Region
2.5mm
2.5mm
1000 A
From Aaron Moy, SVT Assoc and SLAC, PESP2002
Strained-Superlattice GaAs/GaAsP
D. Luh et al, SLAC, PESP2002
QE 1% and Polarization 85%

## Slide 25
P I
2
P I
2
sup.
str.
= 1.38
Experiment Figure of Merit
And, it really works!
QE ~ 0.2%
QE ~ 1.0%

## Slide 26
World Record QE from High Polarization Photocathode
6.4% QE & 84% polarization at 776 nm from strained GaAs/GaAsP superlattice photocathode with GaAsP/AlAsP Distributed Bragg Reflector (DBR)
The highest QE & FOM of any reported high polarization photocathode
Candidate photocathode for mA ops
SBIR partnership
W. Liu, S. Zhang, M. Stutzman, M. Poelker, Y. Chen, W. Lu, and A. Moy, Appl. Phys. Lett. 109, 252104 (2016)
DBR
Substrate
Photo-cathode

## Slide 27: The CEBAF polarized source “Big Three”
High frequency
High power
Synchronous RF
Laser
Photocathode
Many electrons/photon
High polarization
Fast response time

## Slide 28: RF Frequency- Doubled Fiber Laser
1560 nm
780 nm
Low-Power (1 mW)
1560 nm Fiber Diode
Follows RF sine wave
Frequency-doubler
1560 nm to 780 nm
30% Efficiency (2 W)
High Power (6 W) 1560 nm Fiber Amplifier
Master Oscillator
499 MHz
200 mW @ 780 nm
50 ps @ 499/249.5 MHz
=> 6 uA/mW/%

## Slide 29: Photo Finish at 2 billionths of a second !!!
A B C
Pulsed beam (on each RF pulse)
A
B
C
Bunch~50 ps
DC beam (on ALL the time)
500 MHz = 2 ns/revolution

## Slide 30
Combine 4 lasers onto a single path !!!

## Slide 31
Continuous Electron Beam Accelerator Facility
A
B
C
A
B
C
RF Synchronous
Lasers
499 MHz,
ΔФ = 120
Pockels Cell
Gun
2 Linacs
1497 MHz
RF Separators
499 MHz
B
A
C
A B C A B C
100 ps
D
D

## Slide 32: The CEBAF polarized source “Big Three”
High frequency
High power
Synchronous RF
Laser
Very high voltage
Ultra high vacuum
No field emission
DC HV Gun
Photocathode
Many electrons/photon
High polarization
Fast response time

## Slide 33
-130kV
light in
electrons out
photocathode
DC High Voltage Electron Gun

## Slide 34
“The woods were dark and foreboding, and Alice sensed that sinister eyes were watching her every step. Worst of all, she knew that Nature abhorred a vacuum” – Gary Larson
We understand Alice’s worry…
Air ~ 1016 / Torr-cm3
  (molecules ~2 nm apart)
Gun ~ 10-12 Torr
  (molecules ~1 mm apart)

## Slide 35
Vacuum regimes
Low, Medium Vacuum (>10-3 Torr)
  Viscous flow
    interactions between particles are significant
  Mean free path less than 1 mm
High, Very High Vacuum (10-3 to 10-9 Torr)
  Transition region
Ultra High Vacuum (10-9 - 10-12 Torr)
  Molecular flow
    interactions between particles are negligible
    interactions primarily with chamber walls
  Mean free path 100 - 10,000 km (~Earth!!!)
Extreme High (<10-12 Torr)
  Molecular flow
  Mean free path 100,000 km or greater
Air ~ 1016 / Torr-cm3

## Slide 36
Ion Bombardment

## Slide 37: Ion back bombardment
Ion bombardment – with characteristic QE “trench” from laser spot to electrostatic center of photocathode – damages NEA of GaAs
High energy ions are focused to electrostatic center: create QE “hole”
  Don’t run beam from electrostatic center.
QE can be restored, but takes about 8 hours to heat and reactivate
Photocathode “QE scan”
  Active area = 5 mm
  Laser size = 0.35 mm

## Slide 38
Ultra High Vacuum
Avoid contamination by oils due to roughing pumps, fingerprints, machining.
Baking used to get pressures below 10-10 Torr
  250°C for 30 hours removes water vapor bonded to surface that otherwise limits pressure
Getter Pumps
  Chemically active surface
    Titanium sublimed from hot filament
    Non-Evaporative Getters
  Molecules stick when they hit
    Does not work well for inert gasses such as Argon, Helium or for methane
Ion Pumps
  Electric field to ionize gasses
  Magnetic field to direct gasses into cathodes where they are trapped
    Has some pumping capability for noble gasses
NEG pump array
Ion Pump

## Slide 39
Vacuum conditions at CEBAF
Application | Pressure Range | Location | Vacuum Regime
Beamline to dumps | 10-5 Torr | Target to dump line | Medium
Insulating vacuum for cryogens | 10-4 Torr to 10-7 Torr | Cryomodules, transfer lines | Medium to high
Targets, Scattering Chambers | 10-6 to 10-7 Torr | Experimental Halls | High to very high
RF waveguide warm to cold windows | 10-7 to 10-9 Torr | Between warm and cold RF windows | High to very high
Warm beamline | 10-7 to 10-8 Torr | Arcs, Hall beamline, BSY, some injector | High to very high
Warm region girders | 10-9 Torr or better | Girders adjacent to cryomodules | Very high to ultrahigh
Differential pumps | Below 10-10 Torr | Ends of linacs, isolate cryomodules | Ultrahigh vacuum
Baked beamline | 10-10 to 10-11Torr | Y chamber, Wien filter, Pcup | Ultra high vacuum
Polarized guns | 10-11 to 10-12 Torr | Photoguns | Ultra to Extreme high vacuum
SRF cavity vacuum | < 10-12 Torr | Inside SRF cavities with walls at 2K | Extreme high vacuum
1 Atmosphere ~ 760 Torr

## Slide 40
So, where are we going…
…well, where have we been?

## Slide 41: First Observation of Polarization from GaAs

## Slide 42
Built for SLAC parity-violation experiment E122
December 1977 - Polarized electrons accelerated at SLAC
June 1978 - E122 announces parity violation (Standard Model)
First HV GaAs photogun used on an accelerator
mA

## Slide 43
Always Tweaking the Design
The endless (?) quest for perfection
1
2
3
4

## Slide 44
High Polarization from GaAs:
Trending toward higher current…
Year
Ave. Beam Current (mA)
First polarized beam from GaAs photogun
EIC
First low polarization, then high polarization at CEBAF
(Insert your name) breaks world record !!!
?