## Slide 1: Polarized Electrons for Polarized Positron Beams
International Workshop on Future Linear Colliders (LCWS 2018)
October 22-26, 2018
Polarized Electrons for Polarized Positrons (PEPPo)
Positrons at CEBAF
  Low Energy Concept
  High Energy Concept
Positrons for JLab Electron Ion Collider (JLEIC)
Why not PEPPo for the ILC ?
Polarized Electron Source R&D
Joseph Grames, Jefferson Laboratory, USA
Malek Mazouz, University of Monastir, Tunisia
Eric Voutier, IPN-Orsay, France

## Slide 2: Jefferson Lab : CEBAF @ 12 GeV
Users: 1500 (230 Institutions/30 Countries)
Multiplicity: 4 Halls (simultaneously)
Beam Polarization: >85% (90%)
Beam Energy: 11 GeV (ABC) / 12 GeV (D)
Beam Power: 1 MW (85 mA @ 11 GeV)
Cryogenics: Two 4.5 kW plants @ 2.1 K

## Slide 3: Why Polarized Positrons at Jefferson Lab?
Polarized electron beams have supported some of the highest impact results from the JLab program:
  The strangeness distribution in the nucleon (HAPPEX and G0)
  Precision Tests of the Standard Model (QWeak)
  Measurement of the neutron skin in 208Pb
  Polarization transfer measurement of GE/GM for the proton
Unpolarized positron beams offer greater precision
  Comparison of e- with e+ tests our understanding of two photon effects
Polarized positron beams provide a key tool
  Unraveling nucleon structure through the measurement of charge-sensitive General Parton Distributions
  Expand the nature of these tests (e.g. for GE/GM via polarization transfer)
Parameter | CEBAF 12 GeV Electron Beam | Proposed 12 GeV Positron Beam
Beam Intensity | 85 mA | > 100 nA (pol) > 1 mA (unpol)
Duty Factor | 100% (cw) | 100% (cw)
Bunch Frequency | 249.5/499 MHz | 249.5/499 MHz
Spin Polarization | >85% | >50%
Helicity Reversal | 30 – 2000 Hz (Pockels cell) | 30 – 2000 Hz (Pockels cell)

## Slide 4: Letter of Intent to PAC46 (LOI-12-18-004)
Jefferson Lab Positron Working Group (JLAB-PWG) formed in 2016
  120 members (>90% are Users), and growing
  39 institutions
Letter of Intent “Physics Program with Positron Beams at CEBAF 12 GeV” submitted to PAC46 (July 2018), highlighting 7 mini-LOI’s
Summary: “These measurements all have significant physics interest. The proposers should carefully evaluate feasibility and present the best case possible in a future proposal.”

## Slide 5: Enabling Technology : CEBAF Polarized Electron Sources based on GaAs
QE ~ 5%, 30 mA/W
Pol ~ 35% @ 780 nm
Bulk GaAs
QE ~ 0.2%, 1 mA/W
Pol ~ 75% @ 850 nm
Strained GaAs:
GaAs on GaAsP
100 nm
Strained Superlattice GaAs:
Layers of GaAs on GaAsP
QE ~ 1%, 6 mA/W
Pol ~ 89% @ 780 nm
100 nm
14 Layers
2 μm
350 μm
625 μm
Figure-of-Merit (P2I) has improved by a factor of 43
over the span of the CEBAF “6 GeV era”
Pe- 35% 35% 75% 75% 85% 89% 90%
Ie- 30mA 100mA 50mA 100mA 150mA 250mA 4000mA
1995 1998 1999 2000 2004 2012 2017
High Current Lifetime
Studies at CEBAF

## Slide 6: New Method : Exploit Electron Beam Spin Polarization
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
Polarized Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Polarized Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)
Longitudinal spin polarization passes from incident electrons to outgoing pair-produced positrons in the electromagnetic shower, when incident on a target, e.g. high-Z material useful.

## Slide 7: PEPPo Experiment : Feasibility Demonstration at the CEBAF Injector (2012)
J. Grames, E. Voutier et al., JLab Experiment E12-11-105 (2011)
PEPPo (Polarized Electrons for Polarized Positrons) => demonstrate feasibility of using bremsstrahlung radiation of MeV energy Polarized Electrons for production of Polarized Positrons.
8 MeV, 1mA, 85% polarization
Tungsten (1mm)
PEPPo possible due to support from SLAC E166, DESY, Princeton, Cornell, International Linear Collider Project and the Jefferson Science Associates

## Slide 8: PEPPo : Polarized Positron Production
PEPPo demonstrated efficient polarization transfer of 8.2 MeV/c polarized electrons to positrons, expanding polarized positron production using MeV electron beam energies.
(PEPPo Collaboration) D. Abbott et al. , Phys. Rev. Lett. 116 (2016) 214801
electron beam polarization
85.2 ± 0.6 ± 0.7 %
Whenever producing e+ from e-, polarization is coming for free, if initial electrons are polarized.

## Slide 9: Figure of Merit for Electron Energy 60 MeV (Injector Energy of 6 GeV CEBAF)
R. Dollan, K. Laihem, A. Schälicke, NIM A 559 (2006) 185,
J. Dumas, J. Grames, E. Voutier, JPos09, AIP 1160 (2009) 120
J. Dumas, Doctorate Thesis (2011)
Optimum energy
Optimum
FoM
The polarization distribution of generated positrons is dominated by low-energy events.
The positron energy at the optimum FoM (P2I) is about half of the electron beam energy.

## Slide 10: 12 GeV CEBAF: Low Energy (123 MeV) with High Current + Modest Bunch Charge
Positrons would be created at the CEBAF injector, using the 123 MeV electron beam.
Selecting 60 MeV positrons maximizes the FoM (60%, 100 nA).
Selecting 6 MeV positrons maximizes the flux (> 1 mA).
Positron source should have tunability
to optimize for Intensity or Polarization
Sz

## Slide 11: CEBAF: High Energy (11 GeV) with Low Current + Low Bunch Charge

## Slide 12: Polarized Positrons at the Jefferson Lab Electron Ion Collider
A polarized positron injector suitable for the Jefferson Lab Electron Ion Collider (JLEIC) has also been considered.
L ≥1033cm-2s-1 Pe+≥40%
Iave > 10 nA (~1010 e+/s)
Ipeak > 4 mA (~1013 e+/s)
e+
Challenge is accumulating positron bunch charge with JLEIC bunch pattern.

## Slide 13: JLEIC: Low Energy (50 MeV) with Low Current + High Bunch Charge
200 keV polarized e-
8 pC @ 748.5 MHz
(DF=100%)
50 MeV polarized e-
4 nC bunches @ 748.5 MHz
Accumulator Ring (36m)
500-turn
phase-space painting
Bunch
Management
50 MeV polarized e-
4 nC @ 17 MHz
Positron Conversion/Collection Efficiency ~ 5 x 10-4
60% in polarization
25 MeV Polarized e+
0.2 pC @ 17 MHz
(DF=0.26%)
to CEBAF
Harmonic kicker
Extraction
Polarized Electron
50 MeV Injector
Power on target
3.4 MW peak power
0.6 kW average
350 keV polarized e-
2 nC @ 17 MHz
(DF=0.26%)

## Slide 14: ILC : Spin Polarized Electron Driven Source ?
What is expected (w/o any cuts) for a 3 GeV spin polarized electron beam over range of target thickness (5mm – 16 mm)
Thicker targets improve yield of lowest energy positrons, and provide a degree of spin filtering.
Thinner targets conversely improve yield of highest energy positrons, and with less impact by spin filtering.
E(e+) | N(e+)/N(e-) | <Sz> | P (%)
150 MeV | 0.436 | 0.23 | 21
350 MeV | 0.056 | 0.41 | 37
E(e-)=3 GeV
W=16mm

## Slide 15: ILC : Spin Polarized Electron Driven Source ?
What is expected (w/o any cuts) if the electron beam energy were lowered, for the same target thickness (16mm).
Lower electron beam energy results in lower yield, expectedly, preferentially at low positron energy.
Lower electron beam energy results in high spin polarization at same positron energy
E (e-) | N(e+)/N(e-) | <Sz> | P (%)
3 GeV | 0.436 | 0.23 | 21
1 GeV | 0.091 | 0.44 | 40
E (e-) | N(e+)/N(e-) | <Sz> | P (%)
3 GeV | 0.056 | 0.41 | 37
1 GeV | 0.007 | 0.71 | 64
E(e+)=150 MeV
W=16mm
E(e+)=350 MeV
W=16mm

## Slide 16: ILC : Spin Polarized Electron Driven Source ?
What is expected (w/o any cuts) if the electron beam energy were 1 GeV, and target thickness reduced.
Small reduction in target thickness has the effect of increasing yield (at this lower electron beam energy).
Target thickness has less impact when positron energy large fraction of electron energy.
E (e-) | Target | N(e+)/N(e-) | <Sz> | P (%)
3 GeV | 16 mm | 0.436 | 0.23 | 21
1 GeV | 10 mm | 0.178 | 0.39 | 35
E (e-) | Target | N(e+)/N(e-) | <Sz> | P (%)
3 GeV | 16 mm | 0.056 | 0.41 | 37
1 GeV | 10 mm | 0.018 | 0.69 | 62
E(e+)=150 MeV
E(e+)=350 MeV

## Slide 17: GaAs Polarized Electron Source Parameters
Parameter \ Machine => | CEBAF | SLC | JLab/FEL | Cornell ERL | LHeC | eRHIC | CLIC | ILC | JLEIC(e+) | CEBAF (e+)
Polarization | Yes | Yes | No | No | Yes | Yes | Yes | Yes | Yes | Yes
Number electrons/microbunch | 2.5 x 106 | 1 x 1011 | 8.3 x 108 | 4.8 x 108 | 1 x 109 | 2.2 x 1010 | 6 x 109 | 3 x 1010 | 1.2 x 1010 | 2.5 x 108
Number of microbunches | CW | 2 | CW | CW | CW | CW | 312 | 3000 | 900 | CW
Width of microbunch | 50 ps | 2 ns | 35 ps | 2 ps | 100 ps | ~ 100 ps | ~ 100 ps | ~ 1 ns | 100 ps | 50 ps
Time between microbunches | 2 ns | 61.6 ns | 13 ns | 0.77 ns | 25 ns | 71.4 ns | 0.5002 ns | 337 ns | 1.33 ns | 4 ns
Microbunch rep rate | 499 MHz | 16 MHz | 75 MHz | 1300 MHz | 40MHz | 14MHz | 1999 MHz | 3 MHz | 750 MHz | 250 MHz
Width of macropulse | - | 64 ns | - | - | - | - | 156 ns | 1 ms | 1.1 ms | -
Macropulse repetition rate | - | 120 Hz | - | - | - | - | 50 Hz | 5 Hz | 50 Hz | -
Charge per micropulse | 0.4 pC | 16 nC | 133 pC | 77 pC | 500 pC | 3.6 nC | 0.96 nC | 4.8 nC | 2 nC | 40 pC
Charge per macropulse | - | 32 nC | - | - | - | - | 300 nC | 14420 nC | 1800 nC | -
Average current from gun | 200 uA | 2 uA | 10 mA | 100 mA | 20 mA | 50 mA | 15 uA | 72 uA | 88 uA | 10 mA
Average current in macropulse | - | 0.064 A | - | - | - | - | 1.9 A | 0.0144 A | 0.034 A | -
Duty Factor | 2.5 x 10-2 | 2.8 x 10-7 | 2.6 x 10-3 | 2.6 x 10-3 | 4 x 10-3 | 1.4 x 10-3 | 0.2 | 3x10-3 | 2.6 x 10-3 | 1.2 x 10-2
Peak current of micropulse | 8 mA | 8 A | 3.8 A | 38.5 A | 5 A | 35.7 A | 9.6 A | 4.8 A | 20 A | 0.8 A
Current density* | 4 A/cm2 | 10 A/cm2 | 19 A/cm2 | 500 A/cm2 | 100 A/cm2 | 182 A/cm2 | 12 A/cm2 | 6 A/cm2 | 20 A/cm2 | 16 A/cm2
Laser Spot Size* | 0.05 cm | 1 cm | 0.5 cm | 0.3 cm | 0.5 cm | 0.5 cm | 1 cm | 1 cm | 1 cm | 0.10 cm
Demonstrated
Proposed (excuse outdated values)
* Loose estimates
My Speculations

## Slide 18: Jefferson Lab: Inverted Insulator Photogun
CEBAF 200 kV Gun
350 kV gun for GTS and UITF
with optimized triple point shields and mildly conductive insulators
Both designs, maximum field strength < 10 MV/m

## Slide 19: Jefferson Lab: High Voltage (200-350 kV) Inverted Insulator Photo-guns
CEBAF 200 kV
Installed June 2018
(operates at 130kV until an upgrade in 2020)
UITF 350 kV
Polarized Gun
Under assembly
GTS 350 kV
In operation since Nov 2016 with CsK2Sb photocathode

## Slide 20: Metric of Success: High Voltage without Field Emission
Reached
360 kV in 70 hours
Vacuum and radiation levels indistinguishable from background at 350kV
10 MV/m at 350 kV

## Slide 21: Magnetized Beam Photogun at the Gun Test Stand (GTS)
Load-lock inverted insulator photo-gun (multiple photocathodes), like CEBAF geometry.
Cable connection from HVPS to gun.
Over 1000 hours operating >300kV; HV conditioning about 1 week.
Operating with CsKSb photocathodes at >10 mA average current, and 0.7nC bunch charge.
Magnetized Beam LDRD, PI's: R. Suleiman and M. Poelker

## Slide 22: Roadmap: Jefferson Lab
Based upon preliminary simulations that suggest a CW polarized positron source can be built to meet the CEBAF requirements, a conceptual design study report is now essential to inform a plausible scheme that is integrated into the CEBAF program.
The next R&D priorities include designing, building and testing a positron beam collection system to define/optimize useful positron phase space (6D+spin) and assessing the performance of CEBAF for new positron beam conditions (magnet reversal, low intensity, 6D acceptance).
JPos’09
(2009)
PEPPo
(2012-2015)
JPos’17
(2017)
LOI-12-18-004
(2018)

## Slide 23: Summary
Jefferson Lab Users are making the physics case for both high energy polarized and unpolarized positron beams at CEBAF 12 GeV.
PEPPo demonstrated high positron polarization from polarized electrons at low energy w/ small footprint (cost, energy, radioactivity), extensible to high energy.
We are exploring concepts to produce positron beams for both CEBAF (CW, pC, mA) and JLEIC (pulsed, nC, mA) with tunability on intensity and polarization.
Recent progress is promising to develop a 350 kV polarized source based on the inverted insulator geometry necessary for >nC bunch charge.
Can the PEPPo concept applied to the ILC electron driven positron source turn a “no polarization” scheme into a “polarization scheme”, even for a later upgrade?