## Slide 1: Booster Commissioning at UITF
Yan
February 18, 2022

## Slide 2: Contents
Gradient calibration of Booster cavities
Beam deflection caused by Booster
Beam x/y coupling generated from Booster
Beam energy spread downstream of Booster
Beam emittances upstream and downstream of Booster
Beam instability
Future work

## Slide 3: Booster
Booster, a SRF cryomodule, installed and commissioned at UITF
  Composed of a 2-cell cavity and a 7-cell cavity,
  Designed to accelerate 200 keV beam to energies up to 10 MeV
  Installed at CEBAF in 2023
Two successful runs
  9.6 MeV run for HDice experiment in 2020 & 2021
  8.0 MeV run for Water Irradiation experiment in 2021.
Beam based evaluation of Booster

## Slide 4: Partial UITF Beamline
Solenoids
Booster
Quads
ITVM601
ITVM703
30°
MDML601
Gun
MDS201
z
ITVM803
25°
Chopper Buncher
ITVM201/401

## Slide 5: Beam Conditions
Gun HV: 130/180/200 KV
Chopper: on/off
Buncher: on & at negative zero crossing
Booster: on crest & beam centered
Beam momentum: 6.3 MeV/c
All solenoids: beam centered & cycled
All quads: beam centered, zero field & cycled

## Slide 6: Beam Images with Gun HV at 130 KV
2-cell on (gset at 2.5 MV/m), 7-cell off
7-cell on (gset at 7.5 MV/m), 2-cell off

## Slide 7: Stable 6.3 MeV/c Beam with Gun HV at 130 KV (2-cell Gset at 2.5 MV/m, 7-cell Gset at 7.5 MV/m)

## Slide 8: Beam Images with Gun HV at 200 KV
2-cell on (gset at 2.5 MV/m), 7-cell off
7-cell on (gset at 7.5 MV/m), 2-cell off

## Slide 9: Stable 6.3 MeV/c Beam With Gun HV at 200 KV (2-cell Gset at 2.5 MV/m, 7=cell Gset at 7.46 MV/m)

## Slide 10: Beam Momentum vs. 2-Cell Cavity Gset
Chart: 2-Cell Gset (MV/m) (7-Cell Off, Gun HV = 180 KV)
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5
 | 0.75902 | 0.89749 | 1.0368 | 1.1979 | 1.3738 | 1.5823

## Slide 11: Kinetic Energy Gain from 2-Cell Cavity
Chart: 2-Cell Gset (MV/m) (7-Cell Off, Gun HV = 180 KV)
| 1 | 1.5 | 2 | 2.5 | 3 | 3.5
 | 0.224 | 0.34177 | 0.46485 | 0.61138 | 0.77474 | 0.97176

## Slide 12: Beam Momentum vs. 7-Cell Cavity Gradient
Chart: 7-Cell Gset (MV/m) (2-Cell On, Gun HV = 180 KV)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
 | 1.4665 | 2.3697 | 3.1497 | 3.8323 | 4.5723 | 5.3129 | 6.0039 | 6.7391 | 7.477 | 8.1742 | 8.9029 | 9.6399

## Slide 13: Emittance Measurement
UITF
  KeV region: MQZK203 & ITVK203
  MeV region: MQJM501 & ITVM603
CEBAF
  KeV region: MFX2I01 & ITV2I01
  MeV region: MQJ0L02, MQJ0L02A & IHA0L03

## Slide 14: Emittance Measurement
Gun HV (kV) | UITF | ɛx (m-rad) (E-7) | ɛy (m-rad) (E-7) | ɛnx (m-rad) (E-7) | ɛny (m-rad) (E-7)
130 | KeV | 7.02 +/- 0.23 | 6.84 +/- 0.02 | 5.32 +/- 0.18 | 5.18 +/- 0.18
130 | 6.3 MeV/c | 0.44 +/- 0.01 | 0.39 +/- 0.02 | 5.42 +/- 0.02 | 4.76 +/- 0.02
180 | KeV | 4.35 +/- 0.03 | 4.37 +/- 0.07 | 3.87+/- 0.03 | 3.89 +/- 0.06
180 | 6.3 MeV/c | 0.38 +/- 0.02 | 0.57 +/- 0.04 | 4.64 +/- 0.02 | 6.98 +/- 0.05
Gun HV (kV) | CEBAF | ɛx (m-rad) (E-7) | ɛy (m-rad) (E-7) | ɛnx (m-rad) (E-7) | ɛny (m-rad) (E-7)
130 | KeV | 10.40+/- 2.76 | 8.63 +/- 1.67 | 7.88 +/- 2.09 | 6.54 +/- 1.27
130 | 6.3 MeV/c | 0.35 +/- 0.01 | 0.36 +/- 0.01 | 4.60 +/- 0.03 | 4.70 +/- 0.01

## Slide 15: Normalized Emittance, courtesy of A. Hofler

## Slide 16: Beam Deflection by Booster
d
L
Deflection angle θ = ATAN(d/L)
Booster
ITVM201
θ

## Slide 17: Beam Deflection by Booster
Measure beam positions on ITVM201 with cavities on/off
Calculate angular displacements
2-cell
7-cell
ITVM201
 | Distance to ITVM201 (mm)
2-cell center | 1946.9
7-cell center | 1116.2
θ
1946.86
1116.17

## Slide 18: Correctors & Viewer Used (for x/y coupling and deflection studies)
MHBK403H&V: 20.5” upstream
ITVM201: 10.5” downstream
No other magnets between MHBK403 and ITVK201
ITVM201
MHBK403H&V
10.5”
Booster
90”
20.5”
z

## Slide 19: Booster and Upstream MHB403H&V
MHBK403H&V
Fcup and Viewer
Ion Pump
Booster

## Slide 20: Booster and Downstream ITVM201
Booster
ITVM201
Ion pump

## Slide 21: Beam on ITVM201

## Slide 22: Beam Deflection
UITF Gun HV (KV) | 130 | 130 | 180 | 180
Beam deflection | x (deg) | y (deg) | x (deg) | y (deg)
2-cell Cavity on | 0.11 +/- 0.01 | 0.18 +/- 0.01 | 0.13 +/- 0.01 | 0.19 +/- 0.01
Both Cavities on | 0.34 +/- 0.01 | 0.22 +/- 0.01 | 0.27 +/- 0.01 | 0.17 +/- 0.01

## Slide 23: x/y Coupling Caused by Booster
Move beam on a viewer horizontally
or vertically
Measure the beam position
changes in both planes
Calculate beam rotation angle
θ

## Slide 24: x/y Coupling caused by Booster
UITF Gun HV (KV) | 130 | 130 | 180 | 180
x/y Coupling (Baseline) | x (deg) | y (deg) | x (deg) | y (deg)
2-cell Cavity off | 1.65 +/- 0.16 | -0.09 +/- 0.03 | 2.83 +/- 0.40 | 0.01 +/- 0.20
Both Cavities off | 1.65 +/- 0.16 | -0.09 +/- 0.03 | 2.83 +/- 0.40 | 0.01 +/- 0.20
UITF Gun HV (KV) | 130 | 130 | 180 | 180
x/y Coupling (measured) | x (deg) | y (deg) | x (deg) | y (deg)
2-cell Cavity on | 5.18 +/- 0.29 | -0.38 +/- 0.03 | 4.57 +/- 0.17 | 0.63 +/- 0.09
Both Cavities on | 2.61 +/- 0.14 | 0.38 +/- 0.03 | 3.26 +/- 0.10 | 1.07 +/- 0.06
UITF Gun HV (KV) | 130 | 130 | 180 | 180
x/y Coupling (net) | x (deg) | y (deg) | x (deg) | y (deg)
2-cell Cavity on | 3.53 +/- 0.33 | -0.29 +/- 0.04 | 1.74 +/- 0.43 | 0.62 +/- 0.22
Both Cavities on | 0.96 +/- 0.21 | 0.47 +/- 0.04 | 0.43 +/- 0.41 | 1.06 +/- 0.21

## Slide 25: Energy Spread Measurement
Booster
ITVM703/803
ITVM601
MDLM504/601
Spectrometer Dipole MDLM504/601
ITVM401
VP
σ1
σ2

## Slide 26: Energy Spread Measurement
MDLM601
MDLM504
θ1
θ2
No focusing/de-focusing in bending plane
Weak de-focusing in bending plane

## Slide 27: Energy Spread Measurement
All quads are beam centered, zero field, and cycled
Measure beam sizes σ1 at ITVM703/803
Measure beam sizes at ITVM401/601
Calculate beam sizes σ2 at Virtual Point using that at ITVM401/601
Beam size change =
Deflection angle change , where 𝐿 is the spectrometer length

## Slide 28: Energy Spread Measurement
Chopper / Slit Position | Buncher Aplitude change (KeV) | Buncher Phase change (deg) | 7-cell Phase change (deg) | dp/p at ITVM803 gun hv = 130 KV | dp/p at ITVM803 gun hv = 180 KV | dp/p at ITVM703 gun hv = 180 KV
Off / Out |  |  | 0 | 1.21E-004 | 4.36 +/- 0.26 E-4 | 4.94 +/- 0.28 E-4
Off / Out |  |  | -5 | 1.16E-003 | 8.35 +/- 0.72 E-4 | 7.99 +/- 0.19 E-4
Off / Out |  |  | -10 | 5.32E-003 | 1.32 +/- 0.01 E-3 | 1.29 +/- 0.02 E-3
Off / Out |  |  | 5 | 4.12E-004 | 4.93 +/- 0.33 E-4 | 6.46 +/- 0.40 E-4
Off / Out |  |  | 10 | 7.02E-004 | 6.28 +/- 0.19 E-4 | 8.70 +/- 0.28 E-4
Off / Out |  | -5 |  | 1.13E-003 | 5.83 +/- 0.27 E-4 | 7.13 +/- 0.08 E-4
Off / Out |  | -10 |  | N/A | 8.60 +/- 0.43 E-4 | 1.09 +/- 0.03 E-3
Off / Out |  | 5 |  | 5.42E-003 | 1.24 +/- 0.03 E-3 | 1.24 +/- 0.03 E-3
Off / Out |  | 10 |  | N/A | 2.53 +/- 0.02 E-3 | 2.51 +/- 0.01 E-3
Off / Out | -5 |  |  | 4.42E-004 | 7.91 +/- 0.22 E-4 | 4.89 +/- 0.19 E-4
Off / Out | -10 |  |  | 1.47E-003 | 1.83 +/- 0.01 E-3 | 1.48 +/- 0.02 E-3
Off / Out | 5 |  |  | 1.28E-003 | 5.48 +/- 0.06 E-4 | 4.08 +/- 0.13 E-4
Off / Out | 10 |  |  | N/A | 9.44 +/- 0.42 E-4 | 3.16 +/- 0.05 E-4
On / 285 (hole) |  |  |  | N/A | 2.09E-004 | N/A
On / 430 |  |  |  | N/A | 2.93E-004 | N/A
On / 530 |  |  |  | N/A | 2.92E-004 | N/A
On / 630 |  |  |  | N/A | 4.30E-004 | N/A
On / 730 |  |  |  | N/A | 5.72E-004 | N/A

## Slide 29: Kinetic Energy, Energy Spread, courtesy of A. Hofler

## Slide 30: Beam Instability
A few-Hz horizontal beam jitter observed downstream of Booster
  On the straight-line viewers ITVM401, 504, 601 and 603
  On the spectrometer-line viewer ITVM703
  On the chicane viewer ITV803
  Would last a minute or two when it comes
  Not energy related. Root cause not identified yet
Beam instability studies by Max Bruker and company
Microphonic studies by SRF group
Inconsistent Booster trips. Unstable cryo?

## Slide 31: Beam Jitter on ITVM401

## Slide 32: Beam Jitter on ITVM803

## Slide 33: Future Work
High current run
  Radiation shielding needed for high current run (150 – 200 uA)
Bunch length measurement
  Hardware and software not ready yet downstream of Booster
Anything else?