## Slide 1: Design of a 10 MeV Beamline at the Upgraded Injector Test Facility for e-beam Irradiation
Xi Li1 (xli009@odu.edu), Fay Hannon2, Helmut Baumgart1,3,
Gianluigi Ciovati2, Shaoheng Wang2.
1 Department of Electrical and Computer Engineering, Old Dominion University, Norfolk, VA 23529.
2 Thomas Jefferson National Accelerator Facility, Newport News, VA 23606
3 The Applied Research Center at Thomas Jefferson National Accelerator Facility, Newport News, VA 23606
12th International Particle Accelerator Conference - IPAC’21, May 24 – 28, 2021.

## Slide 2
Pollutants in wastewater
Micro-organisms, bacterial, viral, phatogen.
Metal, toxic chemicals.
Manufactured organic compounds..
  1,4 dioxane
  PFAS (Perfluoroalkyl and Polyfluoroalkyl Substances).
Miscible in water and difficult to be removed by the conventional treatment methods.
Charles N. Kurucz, et al. Full-scale electron beam treatment of hazardous wastes – effectiveness and costs, in High energy electron beam irradiation of water, wastewater and sludge. Advances in Nuclear Science and Technology. Vol. 22. p1-43.
Versatile, non-selective for kinds of pollutants
Effective and efficient, large-scale treatment with less time.
Risk-free, absence of extra chemicals or radioactive risks.
EB (electron beam) irradiation is proven to be the most suitable method to remove them.
EB irradiation for wastewater treatment
https://www.chesapeakequarterly.net/sealevel/main2/
Restoration of the Chesapeake Bay Land subsidence program
Treat the wastewater to the drinking water level and send it to the water aquifer to slow down and stop the sand sinking.
by HRSD (Hampton roads sanitation district).
Notes: 1,4 dioxane: cosmetics products, cleaning products. Stable. (https://www.eurofinsus.com/environment-testing/testing-services/specialty-services/1-4-dioxane-analysis/)

## Slide 3: UITF wastewater beamline at Jlab
Radius ~ 25 mm
Transverse: Gaussian distribution,
Joe Grames, UITF optics overview, March 2016. Jefferson lab report.
UITF (Upgraded injector test facility) in Jefferson lab. keV beamline.
Electron Gun
Facility: UITF at Jefferson lab. Energy: 8 MeV (Max: 10 MeV)
Current: 100 nA (CW)
Depth: 4 cm,
volume: 75 mL.
-> radius: ~2.43 cm
x
y
Notes: The energetic electrons interact with water molecules to produce oxidants and reducers, among which the hydroxyl radical is the main factor to oxide the 1,4 dioxane

## Slide 4
GPT simulation: 5000 macro particles.
Transverse spatial distribution.
Parameter name |  | 
Photocathode | GaAs | 
MTE | 0.04 eV (@780 nm) | 
Kinetic energy | 3/2 * MTE | Uniform distribution
Bunch charge | -1.33e-16 C | 100 nA, CW mode.
Beam size | 0.425 mm () | 3 cutoff, Gaussian.
Bunch length | ~14.86 ps () | 4 cutoff, Gaussian.
Parameter name |  | 
Photocathode | GaAs | 
MTE | 0.04 eV (@780 nm) | 
Kinetic energy | 3/2 * MTE | Uniform distribution
Bunch charge | -1.33e-16 C | 100 nA, CW mode.
Beam size |  | 3 cutoff, Gaussian.
Bunch length |  | 4 cutoff, Gaussian.
Electron beam initial parameters
The electrons are assumed to be emitted uniformly from the photocathode.
Notes: In the reality, the treated water is flowing.

## Slide 5
The electron beam is accelerated to 8 MeV after the 2 cavities with the crest energy phases. The energy spread is around 75 keV when the acceleration is not at the crest energy.
SRF acceleration
2-cell cavity: 0.333 MeV energy gain, 169 degree phase shift.
7-cell cavity: ~7.5 MeV energy gain, 234 degree phase shift.

## Slide 6
The optimum position of the solenoid is between 20 to 20.5 m, which is simulated by a fixed peak magnetic strength on axis. The quadrupoles are adjusted to let the beam radius of 𝜎 ~ 1.1 - 1.2 mm at the entrance of the solenoid.
Defocusing solenoid
Quads and solenoid magnets

## Slide 7
Beam envelope
Parameters at the end of the beamline | 
Electron energy | 8 MeV
Energy spread | < 75 keV ()
Transverse maximum radius | ~25 mm
Beam size | 8 - 9 mm ()
Parameters at the end of the beamline | 
Electron energy | 8 MeV
Energy spread | 
Transverse maximum radius | ~25 mm
Beam size | 
With space charge effect considered, the beam size at the end of the beamline is increasing with the beam current or bunch charge increasing, while it does not affect the beam envelop under 100 nA current.
Space charge effect with higher beam current.

## Slide 8: Conclusions and outlook
With the ability to remediate kinds of organic compounds, bacteria, virials and other pollutants in the wastewater, EB irradiation is versatile and prospective for the wastewater treatment.
Based on the UITF at Jefferson lab, the EB wastewater treatment beamline is designed and achieved successfully with 8 MeV electron energy and 0.8 cm to 0.9 cm statistic transverse radius.
The principle for a big beam size is utilizing a high magnetic strength solenoid to to over focus the electron beam and blow it up. Despite that there is no necessity to worry about the space charge effect under the 100 nA beam current, knowledge about the influences from it will help understand the beamline operation.
For further study, the beamline will be installed, commissioned and run for the wastewater sample irradiation.

## Slide 9: Thank you!
Design of a 10 MeV Beamline at the Upgraded Injector Test Facility
for e-beam Irradiation
Xi Li (xli009@odu.edu), Fay Hannon,
Helmut Baumgart, Gianluigi Ciovati, Shaoheng Wang.
12th International Particle Accelerator Conference - IPAC’21, May 24 – 28, 2021.