## Slide 1: Ce+BAF
Joe Grames
Machine concept and status
Topics we’ll address at this meeting
  Joe, polarized e- source
  Andriy, high power e+ target
  Sami, formation of e+ beam
  Dennis, transport of e+ beam to halls

## Slide 2: Ce+BAF Working Group
J. Benesch, A. Bogacz, L. Cardman, J. Conway, S. Covrig, J. Grames, J. Gubeli, C. Gulliford, S. Habet, C. Hernandez-Garcia, A. Hofler,
R. Kazimi, V. Kolstrum, F. Lin, V. Lizarraga-Rubio, M. Poelker, Y. Roblin, A. Seryi, K. Smolenski, M. Spata, R. Suleiman, A. Sy, D. Turner, A. Ushakov, C. Valerio, E. Voutier, S. Zhang, Y. Zhang

## Slide 3: 12 GeV Ce+BAF : Polarized Electron or Polarized Positron Beams
Machine Parameter | Electrons | Positrons
Hall Multiplicity | 4 | 1 or 2
Energy (ABC/D) | 11/12 GeV | 11/12 GeV
Beam Repetition | 249.5/499 MHz | 249.5/499 MHz
Duty Factor | 100% cw | 100% cw
Unpolarized Intensity | 170 mA | > 1 mA
Polarized Intensity | 170 mA | > 50 nA
Beam Polarization | > 85% | > 60%
Fast/Slow Helicity Reversal | 1920 Hz/Yes | 1920 Hz/Yes
2020 JLAAC Recommendations
  “R6: Augment the scientific case with a plan to translate the R&D into a realistic facility.”
  “R7: Include radiation protection considerations into the evaluation of the electron beam energy choice.”
2021 JLAAC Recommendations
  “R4: Elaborate on the possibility for fielding a rapid operational switching mode between e- and e+ operation in FFA arcs.”
  “Q5: …required photocathodes to enable polarized e+ production should continue to be developed.”
  “R20: Work out how efficient magnet polarity switching (~8 hours) could be implemented between e- and e+ operation.”

## Slide 4: Turning the LERF into a positron injector facility
One year ago we were exploring e+ production at 10, 100, 1000 MeV…
Today we are focused on producing 123 MeV e+ utilizing the Low Energy Research Facility
123 MeV
Build e+ injector at the LERF
Build new LERF to CEBAF tunnel
Build new transport line along South Linac and West Arc
Inject e+ into North Linac to usual 12 GeV (w/ magnets reversed)
123 MeV

## Slide 5: LERF Polarized Positron Injector Concept
5
#6 – SRF accelerate e+ to 123 MeV
#4 - Produce and collect e+ 20 to 60 MeV
#2 - SRF accelerate to 120 MeV
#1 – Compact 10 mA P-Gun, Wien filter, 10 MeV e- injector
#3 – Extract e- to target
#8 – Transport e+ at 123 MeV to CEBAF
#5 – Transport e+
Focus is developing a S2E technical report based on a polarized e+ injector at LERF
  High current polarized electron injector (10 MeV/10 mA)
  High current 1-3 mA LINAC (two C75 CM)
  Positron conversion target (~100 kW)
  Positron bunch collection and momentum selection
  Positron bunch compression and acceleration to 123 MeV
#7 – Evaluating 123 MeV spin rotator concept

## Slide 6: CEBAF : spin polarization from GaAs photocathodes
….…
J. Dumas, J. Grames, E. Voutier, “A Polarized Positron Source for CEBAF”, arXiv:0907.5348 (2009)
Reliable
expectation
Reliable
expectation
GaAs photocathodes with both high QE and POL is the enabling technology.

## Slide 7: Exploit electron spin polarization to produce polarized positrons
E.A. Kuraev, Y.M. Bystritskiy, M. Shatnev, E.Tomasi-Gustafsson, PRC 81 (2010) 055208
Polarized Bremsstrahlung
Pcirc(g) / Pz (e-)
Eg / Te-
Polarized Pair Creation
Pz (e+) / Pcirc (g)
Te+ / (Eg – 2me+)
…so why not take advantage of this?
When a longitudinally polarized e- beam strikes matter, e+ produced in the shower carrying >50% of the e- beam energy are significantly longitudinally spin polarized…

## Slide 8: PEPPo : Polarized Electrons for Polarized Positrons
D. Abbott et al., Phys. Rev. Lett. 116 (2016) 214801
P(e+) = 82.2 %
Efficiency >95%
Record for linac positron polarization.
J. Grames, E. Voutier et al.,JLab Experiment E12-11-105 (2011)
8 MeV, 1mA, 85% polarization
PEPPo possible due to support from SLAC E166, DESY, Princeton, Cornell, International Linear Collider Project and the Jefferson Science Associates
Tungsten (1mm)
The spin transfer from e- to e+ was tested in a feasibility experiment at CEBAF in 2012 (remember, the energy argument is scalable…)

## Slide 9: Yield and Polarization at Target vs Energy. Polarized and Unpolarized Modes
e+ Polarization vs Energy
Efficiency
FoM
120 MeV e‒
4 mm Tungsten Target
e+
e‒
e‒
e+
Positron beamline has to be designed for efficient capture and transport of e+ with different energies

## Slide 10: Diffracted Bragg Reflector (DBR) superlattice
W. Liu, S. Zhang, M. Stutzman, M. Poelker, Y. Chen, W. Lu, and A. Moy, Appl. Phys. Lett. 109, 252104 (2016)
July 2022 (unpublished) results of collaboration between Old Dominion University, Brookhaven National Lab and Jefferson Lab
MOCVD growth of DBR-SLSP by industrial partner
  QE > 2%
  Polarization > 90%
> 10 mA/W

## Slide 11: Charge lifetime...
Show calculation of what is needed….
Will CEBAF source do it? No.
Strategy to get there.

## Slide 12: Can the CEBAF photo-gun support an e+ program?
PhD work of J. Yoskowitz in preparation for PR-AB
With a >400 C lifetime we could operate at 1 mA for almost 1 week
Positively biasing the photo-gun anode has had a tremendous impact on JLab gun lifetime.

## Slide 13: Optimizing the gun voltage for charge lifetime
Fewer ions created as gun voltage increases
Ion generation largest here
What about the cathode potential, i.e. is there is “best” potential for increasing charge lifetime?

## Slide 14: Modeling ion generation and bombardment
GPT custom element IONATOR simulates electron-impact ionization of residual beam line gasses and tracks outgoing particles.
Simulations of ion back-bombardment predict ions created within the cathode-anode gap, depositing their energy at the photocathode, closely resembles the measured damage pattern.
Measured
PhD work of Josh Yoskowitz
Simulated
Simulated
QE Loss
e- beam
ions
ejected e-
scattered e-
Simulation of biased anode

## Slide 15: PES: reducing ion surface density to increase lifetime
J. Grames, et al., Phys. Rev. ST Accel. Beams 14 043501 (2011)
Bulk 532nm
GaAs/GaAsP 780nm
Increasing laser beam size at photocathode has increased charge lifetime…

## Slide 16: GaAs/GaAsP charge lifetime at milliamp current
J. Grames, P. Adderley, J. Hansknecht, R. Kazimi, M. Poelker, D. Moser, M. Stutzman, S. Zhang, “Milliampere beam studies using high polarization photocathodes at the CEBAF Photoinjector” Polarized Sources, Targets and Polarimeters Workshop, Dajeon South Korea (2017)
Days
Trend we want to realize
Measurements were performed without anode biasing
Results from PSTP’17 suggests increasing laser spot size is viable to exceed >500 C lifetime; however we need to build another gun to test this assertion.

## Slide 17: Build a mA polarized gun for e+
  Next, we want to combine our lessons learned and experience with the Magnetized 4mA/300 kV gun and new Polarized CEBAF 200 kV gun to build a new third gun optimized for positron generation…
300 kV Magnetized Beam Electron Source (CsKSb)
C. Hernandez-Garcia et al., Phys. Rev. Accel. Beams 22, 113401 (2019)
R30 inverted geometry ceramic insulator
Conditioned to 350 kV
Demonstrated 4.5 mA CW 300 keV
Operate at >200 kV without field emission
HV conditioning >350 kV (uses R30 inverted ceramic insulator)
Dynamic pressure (during beam delivery) ~ 1x10-12 Torr
CEBAF 200 KV Polarized Gun (GaAs/GaAsP)

## Slide 18: Measuring charge lifetime dependence on cathode potential
100 vs. 180 kV
NA-PAC 2022 (WEPA13)
Biased
Exploratory measurement to map out conditions for an experiment at the UITF.

## Slide 19: Present Workforce
Beginning in FY22 positron research was supported at the division level
  ~2 FTE spread across CIS, CASA, OPS departments
  Includes one full-time scientist and one PhD grad student
In FY23 the Ce+BAF working group has grown and with broader collaboration
  JLab Physics division supporting target and magnet R&D
  JLab Eng. division supporting evaluation of electrical requirements (magnets reversal, diagnostics)
  SRF discussions for NC capture linac R&D and SRF integration starting
  ORNL contributing to conceptual design of a 123 MeV e+ spin rotator
  IJCLab (France) remains an important collaborator, contributing to target development
  Xelera Inc. awarded SBIR Phase 1 to evaluate a liquid metal target option
  HEP proposal submitted in support of e+ collaboration (SLAC/KEK/JLAB)
Looking forward to FY24
  S2E technical report (Jun, Sep, Dec)

## Slide 20: Summary and Outlook
Jefferson Lab’s framework of a 22 GeV/e+ upgrade has helped define the goals of the Ce+BAF working group
We are on track to deliver in 2023 a technical report describing a start-to-end concept of positron beams for CEBAF 12 GeV
The concept is based on repurposing the LERF as a high power electron and positron injector (of course there is much to do after this, working towards technical design of critical injector components (target, solenoid, NC linac).
Spin polarized e- sources operating at milliamp intensities, with high spin polarization >90% and large charge lifetime >1 kC are essential.
In N years we could make >100 nA positron beams, this means with good beam quality, suitable for acceleration.