## Slide 1
Mott Target Ladder Gold Foil Thickness Measurements
M. L. Stutzman, Md. A. Mamun
JLab-TN-16-049
Thickness

## Slide 2
Good Events
For each detector (L/R/U/D) in an individual run…
Determine the mean mt and sigma st of a Gaussian fit to the timing region around the events from the coil.
Apply timing cuts at mt ± 2st.
For remaining events determine the mean mE and sigma sE of a Gaussian fit to energy channels [8000:9000].
Apply energy cut from mE– 0.5sE to mE + 2sE .
Sum remaining events.

## Slide 3
Asymmetries
For each run form respective (L/R) and (U/D) super-ratio:
  Physics asymmetry
  Detector asymmetry
  Beam asymmetry
We statistically average the asymmetries for a set of runs for a given foil.
Note that a different pair of detectors were used for each run:
  Run I polarization was horizontal so we use the U/D physics asymmetry
  Run II polarization was vertical so we use the L/R physics asymmetry

## Slide 4
Rates
For each run we first compute an un-normalized rate (Hz) and then correct for:
  Electronics dead time, typically 0.1%
  DAQ dead time, typically 5-20%
For each run we average the un-normalized L/R/U/D and normalize to BCM calibrated average current to form normalized average rate detector rate (Hz/uA).
For each run we use the average of the (Run I/II) 1um Au foil runs to correct the corresponding rates of the extrapolation foil measurements:
  Run I – correction was 1.0 (no correction)
  Run II – correction of 1.0372 +/- 0.0008 applied to foil#15 (1um), foil#2(0.625um) and two of six runs for foil#13(0.050um)
We statistically combine the the normalized (Hz/uA) L/R/U/D average corrected rate for a set of runs for a given foil.
For each foil we combine three uncertainties to the final rate:
  Statistical – per recipe above
  Systematic – average of BCM uncertainties (dI/I) of runs per foil, typically 1%
  Systematic – drift uncertainty of 1.32% (Run I) and 1.47% (Run II)

## Slide 5
DRIFT UNCERTAINTY = (MAX-MIN)/(MAX+MIN) = 1.32%
DRIFT UNCERTAINTY = (MAX-MIN)/(MAX+MIN) = 1.47%
Rate Corrections and Drift Uncertainties