## Slide 1: VERTICAL Wien filter GPT simulations with spline electrodes profile surveyed by metrology group 01/08/21
Gabriel Palacios Serrano
04/06/2021
gabrielp@jlab.org

## Slide 2: Details of GPT simulations
This presentation compares results from 3 models for the Wien filter all for 15 mm electrode gap
  Initial fields maps generated by Gabriel using CST contain a geometrical mistake where the electrode’s flat transitions to the Rogowski profile
    This was Gabriel’s working model until realizing the presence of a ‘hump’ in the electric field map compared to that generated by Bruce Dunham in POISSON. Upon close inspection, it was realized that the very first coordinate defining the start of the Rogowski profile was inadvertently omitted. This was corrected and correspondingly named Spline electrode profile model.
    The GPT deck with its corresponding field map can be found in: O:\inj_group\Gabriel\Wien filter\200 keV Gabs E field

## Slide 3: Details of GPT simulations continued
  Spline (our latest working model to 04/05/2021)
    The ME under D. Machie created a 3D spline model based on the manufacturing drawing and thus representing the actual VERTICAL Wien electrodes. The Horizontal Wien electrodes are faceted, not spline.
    Gabriel then used this 3D model to produce E field maps using CST that now agree with Dunham’s and subsequently generated GPT beam simulations for his PhD dissertation and Wien filter paper.
    The GPT deck with its corresponding field map can be found in: O:\inj_group\Gabriel\Wien filter\200 keV Spline E field
HORIZONTAL Wien electrodes are faceted
VERTICAL Wien electrodes have spline profile

## Slide 4: Details of GPT simulations continued
  VERTICAL Wien with spline electrode profile Surveyed (based on the S&A data from 01/08/21). The modeling process for this one is explained in the slides 3 to 11.
    This is the Spline model, but in this case Gabriel applied pitch and roll to both electrode plates, based on the information from S&A.
    The GPT deck with its corresponding fieldmap can be found in: O:\inj_group\Gabriel\Wien filter\200 keV Spline E field - surveyed

## Slide 5: Details of GPT simulations
The GPT simulations where all made with Alicia’s beam:
  Alicia produced a “good” description of the particle distribution at the photocathode, then propagated this beam in GPT through two simulated solenoids with “realistic” parameters, all the way to the entrance of the Wien filter location. Then she recorded the particle distribution information (i.e. coordinates and momentums) to a file named “gdfselect_jg_p_2.493772_unphased_results.gdf” that is used in my GPT deck as the initial particle distribution.
  The electric field maps correspond to each case (i.e. Gab’s fields, spline, or spline surveyed) and are in the deck folder. The scaling factor is found in the GPT deck file with extension *.mr (multiple run) with the variable name “Escale”.
  The magnetic field maps are scaled versions of Jay’s original field map (as far as I am aware). The scaling factor is found in the GPT deck file with extension *.mr (multiple run) with the variable name “Bscale”.
  For slides 13 to 20, the simulation results have all the same scaling of the electric field. This is to show how much deviation we get from the Surveyed model without changing the electric field.

## Slide 6: Reference frame S&A
1
2
3
4
5
6
7
8
9
10
Upstream
Downstream
Beam enters
Beam exits
Top plate points
1
2
3
4
5
6
7
8
9
10
Bottom plate points
Nose
Tail
Clockwise
Rotation!

## Slide 7: Reference frame CST based on S&A
Upstream
Downstream
Beam enters
Beam exits
Top plate
Bottom plate

## Slide 8: From S&A: ROLL
With respect to z-axis

## Slide 9: From S&A: PITCH
With respect to z-axis

## Slide 10: Setting up the problem based on S&A
Points used to contruct electrode plane |  |  |  |  |  |  |  | 
Top Plane | X (mm) | Y (mm) | Z (mm) |  | Bottom Plane | X (mm) | Y (mm) | Z (mm)
p1 US | 19.28 | 7.44 | -78.08 |  | p1 US | 13.71 | -7.63 | -76.93
p2 US | 8.39 | 7.41 | -78.62 |  | p2 US | 7.59 | -7.63 | -77.44
p3 US | 0.12 | 7.41 | -77.95 |  | p3 US | 0.55 | -7.61 | -77.63
p4 US | -8.52 | 7.39 | -77.90 |  | p4 US | -5.91 | -7.61 | -76.52
p5 US | -15.06 | 7.38 | -78.79 |  | p5 US | -11.28 | -7.60 | -77.95
AVG. |  | 7.41 |  |  | AVG. |  | -7.62 | 
p6 DS | -10.28 | 7.15 | 79.79 |  | p6 DS | -18.54 | -7.66 | 77.74
p7 DS | -1.43 | 7.16 | 77.76 |  | p7 DS | -11.00 | -7.66 | 77.94
p8 DS | 3.51 | 7.16 | 77.27 |  | p8 DS | -2.60 | -7.67 | 77.82
p9 DS | 10.35 | 7.17 | 77.17 |  | p9 DS | 4.99 | -7.68 | 76.88
p10 DS | 18.20 | 7.18 | 76.97 |  | p10 DS | 13.40 | -7.71 | 78.42
AVG. |  | 7.16 |  |  | AVG. |  | -7.68 | 
Top plate points, upstream
Top plate points, downstream
Bottom plate points, upstream
Bottom plate points, downstream
Remember: the points are not evenly distributed, so be careful when comparing (x, y, z) coordinates!

## Slide 11: Pitch: Top plate
Dealing with the top plate (plane):
  Points 1 to 5 upstream are higher than points 6 to 10 downstream
  This means the top plate’s nose is pointing downwards
Points used to contruct electrode plane |  |  |  |  |  |  |  | 
Top Plane | X (mm) | Y (mm) | Z (mm) |  | Bottom Plane | X (mm) | Y (mm) | Z (mm)
p1 US | 19.28 | 7.44 | -78.08 |  | p1 US | 13.71 | -7.63 | -76.93
p2 US | 8.39 | 7.41 | -78.62 |  | p2 US | 7.59 | -7.63 | -77.44
p3 US | 0.12 | 7.41 | -77.95 |  | p3 US | 0.55 | -7.61 | -77.63
p4 US | -8.52 | 7.39 | -77.90 |  | p4 US | -5.91 | -7.61 | -76.52
p5 US | -15.06 | 7.38 | -78.79 |  | p5 US | -11.28 | -7.60 | -77.95
AVG. |  | 7.41 |  |  | AVG. |  | -7.62 | 
p6 DS | -10.28 | 7.15 | 79.79 |  | p6 DS | -18.54 | -7.66 | 77.74
p7 DS | -1.43 | 7.16 | 77.76 |  | p7 DS | -11.00 | -7.66 | 77.94
p8 DS | 3.51 | 7.16 | 77.27 |  | p8 DS | -2.60 | -7.67 | 77.82
p9 DS | 10.35 | 7.17 | 77.17 |  | p9 DS | 4.99 | -7.68 | 76.88
p10 DS | 18.20 | 7.18 | 76.97 |  | p10 DS | 13.40 | -7.71 | 78.42
AVG. |  | 7.16 |  |  | AVG. |  | -7.68 | 
180° - 179.91° = 0.09°
Creates ~0.3 mm difference between nose and tail y-coordinates in S&A and in CST
 | RX FROM Y (PITCH) | RY FROM Z (Yaw) | RZ FROM X (Roll)
Top Electrode | -179.9100 | N/A | -89.9269
Bottom Electrode | -179.9763 | N/A | -90.0841

## Slide 12: Pitch: Bottom plate
Dealing with the bottom plate (plane):
  Points 1 to 5 upstream are higher than points 6 to 10 downstream
  This means the top plate’s nose is pointing downwards
180 - 179.9763 = 0.0237
Creates around 0.5 mm difference between nose and tail y-coordinates in S&A and in CST
 | RX FROM Y (PITCH) | RY FROM Z (Yaw) | RZ FROM X (Roll)
Top Electrode | -179.9100 | N/A | -89.9269
Bottom Electrode | -179.9763 | N/A | -90.0841
Points used to contruct electrode plane |  |  |  |  |  |  |  | 
Top Plane | X (mm) | Y (mm) | Z (mm) |  | Bottom Plane | X (mm) | Y (mm) | Z (mm)
p1 US | 19.28 | 7.44 | -78.08 |  | p1 US | 13.71 | -7.63 | -76.93
p2 US | 8.39 | 7.41 | -78.62 |  | p2 US | 7.59 | -7.63 | -77.44
p3 US | 0.12 | 7.41 | -77.95 |  | p3 US | 0.55 | -7.61 | -77.63
p4 US | -8.52 | 7.39 | -77.90 |  | p4 US | -5.91 | -7.61 | -76.52
p5 US | -15.06 | 7.38 | -78.79 |  | p5 US | -11.28 | -7.60 | -77.95
AVG. |  | 7.41 |  |  | AVG. |  | -7.62 | 
p6 DS | -10.28 | 7.15 | 79.79 |  | p6 DS | -18.54 | -7.66 | 77.74
p7 DS | -1.43 | 7.16 | 77.76 |  | p7 DS | -11.00 | -7.66 | 77.94
p8 DS | 3.51 | 7.16 | 77.27 |  | p8 DS | -2.60 | -7.67 | 77.82
p9 DS | 10.35 | 7.17 | 77.17 |  | p9 DS | 4.99 | -7.68 | 76.88
p10 DS | 18.20 | 7.18 | 76.97 |  | p10 DS | 13.40 | -7.71 | 78.42
AVG. |  | 7.16 |  |  | AVG. |  | -7.68 | 

## Slide 13: Roll: Top plate
Dealing with the top plate (plane):
  Upstream Point 1 is higher than point 5. This means the top plate’s is rotating clockwise.
  Downstream similarly.
Points used to contruct electrode plane |  |  |  |  |  |  |  | 
Top Plane | X (mm) | Y (mm) | Z (mm) |  | Bottom Plane | X (mm) | Y (mm) | Z (mm)
p1 US | 19.28 | 7.44 | -78.08 |  | p1 US | 13.71 | -7.63 | -76.93
p2 US | 8.39 | 7.41 | -78.62 |  | p2 US | 7.59 | -7.63 | -77.44
p3 US | 0.12 | 7.41 | -77.95 |  | p3 US | 0.55 | -7.61 | -77.63
p4 US | -8.52 | 7.39 | -77.90 |  | p4 US | -5.91 | -7.61 | -76.52
p5 US | -15.06 | 7.38 | -78.79 |  | p5 US | -11.28 | -7.60 | -77.95
AVG. |  | 7.41 |  |  | AVG. |  | -7.62 | 
p6 DS | -10.28 | 7.15 | 79.79 |  | p6 DS | -18.54 | -7.66 | 77.74
p7 DS | -1.43 | 7.16 | 77.76 |  | p7 DS | -11.00 | -7.66 | 77.94
p8 DS | 3.51 | 7.16 | 77.27 |  | p8 DS | -2.60 | -7.67 | 77.82
p9 DS | 10.35 | 7.17 | 77.17 |  | p9 DS | 4.99 | -7.68 | 76.88
p10 DS | 18.20 | 7.18 | 76.97 |  | p10 DS | 13.40 | -7.71 | 78.42
AVG. |  | 7.16 |  |  | AVG. |  | -7.68 | 
90 – 89.9269 = 0.0731 CLOCKWISE!
Creates ~0.06 mm difference on y-axis between tail’s left-most (p1) and right-most (p5) points in S&A and in CST.
This means I am rolling in the right direction.
 | RX FROM Y (PITCH) | RY FROM Z (Yaw) | RZ FROM X (Roll)
Top Electrode | -179.9100 | N/A | -89.9269
Bottom Electrode | -179.9763 | N/A | -90.0841
Seems displaced but it’s not because the points are not evenly distributed
Rotating clockwise
0.03 mm difference in y-axis in S&A vs 0.06 mm difference in CST on the nose’s left-most and right-most points.

## Slide 14: Roll: Bottom plate
Dealing with the bottom plate (plane):
  Upstream Point 1 is lower than point 5. This means the bottom plate is rotating counter-clockwise.
Points used to contruct electrode plane |  |  |  |  |  |  |  | 
Top Plane | X (mm) | Y (mm) | Z (mm) |  | Bottom Plane | X (mm) | Y (mm) | Z (mm)
p1 US | 19.28 | 7.44 | -78.08 |  | p1 US | 13.71 | -7.63 | -76.93
p2 US | 8.39 | 7.41 | -78.62 |  | p2 US | 7.59 | -7.63 | -77.44
p3 US | 0.12 | 7.41 | -77.95 |  | p3 US | 0.55 | -7.61 | -77.63
p4 US | -8.52 | 7.39 | -77.90 |  | p4 US | -5.91 | -7.61 | -76.52
p5 US | -15.06 | 7.38 | -78.79 |  | p5 US | -11.28 | -7.60 | -77.95
AVG. |  | 7.41 |  |  | AVG. |  | -7.62 | 
p6 DS | -10.28 | 7.15 | 79.79 |  | p6 DS | -18.54 | -7.66 | 77.74
p7 DS | -1.43 | 7.16 | 77.76 |  | p7 DS | -11.00 | -7.66 | 77.94
p8 DS | 3.51 | 7.16 | 77.27 |  | p8 DS | -2.60 | -7.67 | 77.82
p9 DS | 10.35 | 7.17 | 77.17 |  | p9 DS | 4.99 | -7.68 | 76.88
p10 DS | 18.20 | 7.18 | 76.97 |  | p10 DS | 13.40 | -7.71 | 78.42
AVG. |  | 7.16 |  |  | AVG. |  | -7.68 | 
90 – 90.0841 = -0.0841 COUNTER-CLOCKWISE!
Creates ~0.07 mm difference on y-axis between tail’s left-most (p1) and right-most (p5) points in CST vs a 0.03 difference in S&A
This means I am rolling in the right direction.
 | RX FROM Y (PITCH) | RY FROM Z (Yaw) | RZ FROM X (Roll)
Top Electrode | -179.9100 | N/A | -89.9269
Bottom Electrode | -179.9763 | N/A | -90.0841

## Slide 15: GPT results: Average vertical deviation
Chart: avg z [m]
Extra 1 mm introduced by the deviations
Negligible difference between Spline and Gab’s
In the case of the Spline surveyed, the trajectory deviates due to unintended electrodes pitch and roll after assembly. The trajectory was not restored in the simulation since it needs an extra correction to the electric field to do so. This study was to check how much extra deviation we get from introducing the pitch and roll from S&A.

## Slide 16: GPT results: Spot size
Chart: avg z [m]
~2.3 % variation between the three models at exit

## Slide 17: GPT results: Normalized vertical emittance
Chart: avg z [m]
Negligible variation between the three models at exit

## Slide 18: GPT results: Bunch length
Chart: avg z [m]
<1.0 % variation between the three models at exit. Normalized though!

## Slide 19: GPT results: Average kinetic energy
Chart: avg z [m]
Negligible variation between the three models at exit

## Slide 20: GPT results: Energy spread
Chart: avg z [m]
Negligible variation between the three models at exit

## Slide 21: GPT results: Avg vertical force
Chart: avg z [m]

## Slide 22: GPT results: Avg longitudinal force
Chart: avg z [m]

## Slide 23: FIN