## Slide 1: Polarized Electron Sources
JLAB Summer Lecture Series, July 17, 2014
Joe Grames

## Slide 2: Who needs electrons?
Storage batteries, man-made and natural power generators, power grids and distribution circuits, and…the “free” electrons used in particle accelerators…..

## Slide 3
7Li

## Slide 4
What you “are” is what you “see”…
mass ~ 1/l ~ energy
M ~ 938 MeV/c2
M ~ 0.511 MeV/c2
E=mc2

## Slide 5: What to do?
Build a 5 mile long electron microscope!
Make electrons energetic enough (Ebeam) to peek inside proton or neutron (Mnucleon).
Neutron
Proton
Electron

## Slide 6: How to make the electrons “powerful” ?
Debunching
Bunching
Accelerating
Decelerating
Electrons gain energy
on each crest!
Use radio(frequency) waves !!!

## Slide 7
Continuous Electron Beam Accelerator Facility
A B C A B C
A
B
C
A
B
C
RF Synchronous
Lasers
499 MHz,
ΔФ = 120
Pockels Cell
Gun
2 Linacs
1497 MHz
RF Separators
499 MHz
B
A
C
111 ps

## Slide 8: Photo Finish, but at 2 billionths of a second !!!
DC beam, not so useful
A B C A B C
1497 MHz
60 degrees
3 lasers pulsing
A
B
C
500 MHz

## Slide 9: The “C” in CEBAF

## Slide 10: Accelerators Need Electron Beams How do we make them?
Field Emission
Thermionic Emission
Photoemission

## Slide 11: The Canonical Emission Equations (slide courtesy of Dr. K. Jensen, Naval Research Laboratory)
Field Emission Fowler Nordheim E.L. Murphy, and R.H. Good, Physical Review 102, 1464 (1956).
Thermal Emission Richardson-Laue-Dushman C. Herring, and M. Nichols, Reviews of Modern Physics 21, 185 (1949).
Photoemission Fowler-Dubridge L.A. DuBridge Physical Review 43, 0727 (1933).
Listed chronologically

## Slide 12: Field Emitter Sources
Explained by Fowler-Nordheim, 1928: a quantum mechanical tunneling effect
“bright” e-beam, good for surface science
I = BV2 exp(-C/V)
Vacuum diode
60°
human hair

## Slide 13: Thermionic Emission
Used to make light….
Studied since early 1800’s and perfected over 100 years, by many inventors (why does Edison get so much credit?)
Thermionic emission from Tungsten filaments and metalloids like LaB6 operating at >1000K are common
~ 90% of consumed power simply generates heat
Edison’s patent,
Long-lasting filament
Melts 3695K

## Slide 14: Thermionic Emission
Used to make x-ray light….
1880s
X-rays are generated when a DC electron beam, typically a few mA, strikes a tungsten target at 60-200 keV. e-Beam quality is not a big concern
Rotating anode to distribute heat
1930s
bias at high voltage

## Slide 15: Modern X-Ray Sources
Courtesy Varian
Higher Voltage….
More penetrating x-ray beam
Higher e-beam current…..
Higher x-ray flux

## Slide 16
CEBAF’s First Electron Source
Make beam by running current through the filament biased at 100kV
Use “grid” to turn beam ON/OFF, i.e., create machine-safe macropulses
Apertures to improve emittance
Use RF “chopper” to create RF structure
Polarized GaAs photosource
Thermionic source
RF-chopper

## Slide 17: Klystrons — RF generators
Electrons make RF-energy…
Klystrons use a DC electron beam at a few mA to generate/amplify microwaves by velocity modulation.
Klystrons use thermionic cathodes to generate the required electron beam.

## Slide 18: What about the probing with spin ?
Target
You measure
an experimental
asymmetry

## Slide 19: Parity Violation Experiments at CEBAF
Experiment | Energy (GeV) | I (µA) | Target | Apv (ppb) | Maximum Charge Asym (ppb) | Maximum Position Diff (nm) | Maximum Angle Diff (nrad) | Maximum Size Diff (δσ/σ)
HAPPEx-II (Achieved) | 3.0 | 55 | 1H (20 cm) | 1400 | 400 | 1 | 0.2 | Was not specified
HAPPEx-III (Achieved) | 3.484 | 100 | 1H (25 cm) | 16900 | 200±100 | 3±3 | 0.5±0.1 | 10-3
PREx | 1.063 | 70 | 208Pb (0.5 mm) | 500 | 100±10 | 2±1 | 0.3±0.1 | 10-4
QWeak | 1.162 | 180 | 1H (35 cm) | 234 | 100±10 | 2±1 | 30±3 | 10-4
Møller | 11.0 | 75 | 1H (150 cm) | 35.6 | 10±10 | 0.5±0.5 | 0.05±0.05 | 10-4
PV experiments motivate polarized e-source R&D

## Slide 20: What does “234 ppb” even mean?
Target
1,000,000,000
A
B
A - B
1,000,000,000
A = 500,000,117
B = 499,999,883

## Slide 21
Electron Bunch Spin & Polarization
0% Polarization
(thermionic)

50% Polarization

v
v

## Slide 22: Polarized Source Landscape 1970s
Self-polarization via Sokolov-Ternov Effect
Electron Scattering (Mott)
Photo-ionization: Fano Effect
Photo-ionization of State Selected alkali atoms
Optically Pumped He Discharge
Field Emission from EuS
Photoemission from GaAs

## Slide 23: Sources can be problematic !
Fast spin reversal; some methods difficult to reverse spin greater than 1Hz second (present day experiments want >1kHz)
It would be nice to make RF-time structure directly, instead of DC beam
Most accelerators require reasonably small emittance
Maximize feasability; lasers, pounds of alkali metal, hot and cold things very near each other, strong magnetic fields, very high voltage, challenging vacuum issues can kill a concept
Long term reliability can be an issue (24/7 ops)
Reproducibility, getting the same result twice

## Slide 24: Polarized Source “Musts”
Lots of Photons
CW Pulses
High Polariztion
Good
Photocathode
Good
Laser
Accelerate Electrons
Happy Photocathode
Integrate Laser
Good
Electron Gun
Many electrons/photon
High Polarization
Fast response time

## Slide 25: GaAs….the method that caught on

## Slide 26: Photoemission from GaAs
Bare GaAs surface
Large Work Function
Positive Electron Affinity (PEA)
PEA=4.07 eV
Egap
Conduction
Band
Valence
Band
GaAs
Vacuum
Dipole layers of
Cesium + NF3
Reduces Work Function
Negative Electron Affinity (NEA)
+
-
-
χNEA ~ 0.2 eV
GaAs
Vacuum
Light
NEA Surface Activation
Quantum Efficiency = Ne- / Ng

## Slide 27
Bulk GaAs
Laser excitation from P3/2 to S1/2 : Egap < E < Egap+Δ
Electron Polarization:
σ+: Right-handed circularly polarized light
σ- : Left-handed circularly polarized light
Reverse electron polarization by reversing light polarization
mj
E
-1/2
+1/2
J
P1/2
-3/2
-1/2
+3/2
+1/2
P3/2
-1/2
+1/2
S1/2
σ+
σ-
3
S1/2
P3/2
P1/2
Egap=1.42 eV
Δ=0.34 eV
E
k
3
1
EF

## Slide 28: First Observation of Polarization from GaAs

## Slide 29
First High Voltage GaAs Photogun
Started with a thermionic gun housing

## Slide 30
First GaAs Photoinjector
Built for SLAC parity-violation experiment E122
Polarized electrons accelerated December, 1977
E122 announces parity violation June, 1978 - an important verification of the Standard Model

## Slide 31
Higher P: Breaking GaAs Degeneracy
Split degeneracy of P3/2 : Introduce strain on GaAs crystal by growing it on substrate (GaAsP) with different lattice constant
High polarization by laser excitation from P3/2 to S1/2 :
  Egap < E < Egap+δ
Higher QE: Alternating layers of GaAs and GaAsP – Superlattice GaAs
+3/2
Egap
δ=20–50
meV
mj = -1/2
+1/2
S1/2
P3/2
mj = -3/2
-1/2
+1/2
σ+
σ-

## Slide 32
Strained layer GaAs
Strained GaAs
Bandwidth Semiconductor (formerly SPIRE)
 split
degeneracy of P
3/2
GaAs
1-x
P
x
GaAs
1-x
P
x
x=0.29
p-type GaAs
substrate
MOCVD-grown epitaxial spin-polarizer wafer
Lattice mismatch
0<x<0.29
600 μm
250 μm
250 μm
0.1 μm

## Slide 33
Strained Layer - Superlattice GaAs
Be doping (cm )
-3
GaAs P
1-x
x
, 0<x<0.36 (2.5 μm)
p-type GaAs substrate
GaAs (5 nm)
GaAs (4 nm)
GaAsP (3 nm)
GaAs P
0.64
0.36
(2.5 μm)
14 pairs
5.10
19
5.10
17
5.10
18
SVT associates, per SLAC specs.

## Slide 34
P I
2
P I
2
sup.
str.
= 1.38
Experiment Figure of Merit
And, it really works!

## Slide 35: Polarized GaAs Source “Musts”
Lots of Photons
CW Pulses
High Polariztion
Good
Photocathode
Good
Laser
Accelerate Electrons
Happy Photocathode
Integrate Laser
Good
Electron Gun
Many electrons/photon
High Polarization
Fast response time

## Slide 36
Bird’s Eye View
Two Guns
Laser Room
Electron
Beam Line

## Slide 37
Laser Room for Dust & Climate Control
Lasers are cool !!!

## Slide 38
Gain-switched Diode Laser and Fiber Amplifier
Attenuator
PC WP LP
Shutter
Rotatable GaAs
Photocathode
V-Wien Filter
Vacuum
Window
15° Dipole
PZT
Mirror
IHWP
RHWP
Pockels
Cell
Delayed
Helicity Fiber
HV Supply
(0 – 4 kV)
HV Supply
(0 – 90 V)
CEBAF
Hall
T-Settle
Fiber
Charge Feedback (PITA)
Electron
Beam
Helicity Fiber
Charge Feedback (IA)
LP HWP LP
IA
Target
BCM
BPMs
5 MeV
Helicity Magnets
Parity
DAQ
nHelicity
Fiber
Position
Feedback
Helicity Generator
H-Wien Filter
Spin Solenoids

## Slide 39
Radio Frequency Pulsed Lasers
Diode seed laser
Diode amplifier
0.5 GHz
1 GHz
1.5 GHz
2 GHz
C
C
A
A
A
A
A
A
B
B
M. Poelker, Appl. Phys. Lett. 67, 2762 (1995).

## Slide 40: Fiber-based Drive Laser
1560 nm
780 nm
499 MHz
RF Locked Low-Power (1 mW)
1560 nm Fiber Diode
Frequency-doubler
1560 nm to 780 nm
30% Efficiency (2 W)
High Power (6 W) 1560 nm Fiber Amplifier

## Slide 41: Polarized GaAs Source “Musts”
Lots of Photons
CW Pulses
High Polarization
Good
Photocathode
Good
Laser
Accelerate Electrons
Happy Photocathode
Integrate Laser
Good
Electron Gun
Many electrons/photon
High Polarization
Fast response time

## Slide 43
“The woods were dark and foreboding, and Alice sensed that sinister eyes were watching her every step. Worst of all, she knew that Nature abhorred a vacuum” – Gary Larson
We understand Alice’s worry…

## Slide 44: Vacuum regimes
Low, Medium Vacuum (>10-3 Torr)
  Viscous flow
    interactions between particles are significant
  Mean free path less than 1 mm
High, Very High Vacuum (10-3 to 10-9 Torr)
  Transition region
Ultra High Vacuum (10-9 - 10-12 Torr)
  Molecular flow
    interactions between particles are negligible
    interactions primarily with chamber walls
  Mean free path 100-10,000 km
Extreme High (<10-12 Torr)
  Molecular flow
  Mean free path 100,000 km or greater
Air ~ 1016 / Torr-cm3

## Slide 45: Vacuum Conditions at CEBAF
Application | Pressure Range | Location | Vacuum Regime
Beamline to dumps | 10-5 Torr | Target to dump line | Medium
Insulating vacuum for cryogens | 10-4 Torr to 10-7 Torr | Cryomodules, transfer lines | Medium to high
Targets, Scattering Chambers | 10-6 to 10-7 Torr | Experimental Halls | High to very high
RF waveguide warm to cold windows | 10-7 to 10-9 Torr | Between warm and cold RF windows | High to very high
Warm beamline vacuum | 10-7 to 10-8 Torr or better | Arcs, Hall beamline, BSY, some injector | High to very high
Warm region girders | 10-9 Torr or better | Girders adjacent to cryomodules | Very high to ultrahigh
Differential pumps | Below 10-10 Torr | Ends of linacs, injector cryomodules and guns | Ultrahigh vacuum
Baked beamline | 10-10 to 10-11Torr | Y chamber, Wien filter, Pcup | Ultra high vacuum
Polarized guns | 10-11 to 10-12 Torr | Inside Polarized guns | Ultra/Extreme high vacuum
SRF cavity vacuum | < 10-12 Torr | Inside SRF cavities with walls at 2K | Extreme high vacuum

## Slide 46
Where does the gas come from?
Outgassing from the system
  Metal and non-metal (viton o-rings, ceramics) all outgas
  Primarily water in unbaked systems
  Primarily hydrogen from steel in baked systems
Leaks
  Real
    Gaskets not sealed
    Cracks in welds, bellows, ceramics, window joints
    Superleaks that only open at very low temperatures
  Virtual
    Small volumes of gas trapped inside system (screw threads, etc.) that pump out slowly over time
Gas load caused by the beam
  Desorption of gases by elevated temperatures, electrons or photons striking surfaces, etc.
Engineered Loads (targets, etc.) where gas is added
Permeation of gasses through materials
  Viton gaskets worse than metal seals
  Hydrogen can permeate through stainless steel!

## Slide 47: Ultra High Vacuum Pumps
Getter Pumps
  Chemically active surface
    Titanium sublimed from hot filament
    Non-Evaporative Getters
  Molecules stick when they hit
    Does not work well for inert gasses such as Argon, Helium or for methane
Ion Pumps
  Electric field to ionize gasses
  Magnetic field to direct gasses into cathodes where they are trapped
    Has some pumping capability for noble gasses
Baking used to get pressures below 10-10 Torr
  250°C for 30 hours removes water vapor bonded to surface that otherwise limits pressure
Avoid contamination by oils due to roughing pumps, fingerprints, machining residue.
NEG pump array
Ion Pump

## Slide 48: Always Tweaking the Design
Endless (?) quest for perfection
1
2
3
4

## Slide 49
High Polarization from GaAs:
Trending toward higher current…
Year
Ave. Beam Current (mA)
First polarized beam from GaAs photogun
E(L)IC
First low polarization, then high polarization at CEBAF
(Insert your name) breaks world record !!!
?