## Slide 1: e+ Beam Tracking in 1st Capture Solenoid
Magnetic Field and Beam Tracking in CST Studio Suite
Beam Tracking of 60 MeV e+ and 10 MeV e+ in 1st Solenoid (GPT)
A. Ushakov

## Slide 2: Beam, Target, Solenoid Parameters and Field (CST)
Primary Beam: 1 mA @ 120 MeV
Beam Size: σx = σy = 1 mm
Target Material: Tungsten
Target Thickness: 4 mm
Solenoid:
Length: 30 cm
Radius: 10 cm
Current: 2E6 A*Turns/m
Solenoid-to-Target Distance: 5 mm

## Slide 3: Tracking of Positrons in CST

## Slide 4: Distributions of e+ at Target Exit in Forward Direction. Ee+ = 60 MeV 3 MeV
Ne+ = 26093
Ne- = 107

## Slide 5: X-X’ Phase Space of Positrons in Forward Direction. Ee+ = 60 MeV 3 MeV
Ne+ = 26093
Ne- = 107
Mean E = 59.85 MeV
εx = 0.143 mm·rad
εnorm x = 16.9 mm·rad
= 1.077 mm2
= 0.020
= 0.0291 mm

## Slide 6: Field Profile on Beam Axis (GPT). Max Bz = 2.2 T for 2.1 A*Turns/m

## Slide 7: 60 MeV e+: Time Evolution of Phase Space in 2.2 T Solenoid (max Bz(r = 0))

## Slide 8: 60 MeV e+: Example of 20 e+ Trajectories

## Slide 9: 60 MeV e+: Positron Losses and Beam Divergence
RMS vs Time
Number of e+ vs Time (107 primary e-)

## Slide 10: 60 MeV e+: Tranverse Beam Size and Normalized Emittance
Normalized Emittance vs Time
Beam Size vs Time

## Slide 11: 60 MeV e+: Longitudinal Beam Size
At target:
σt = 0.14 ps
σz = 0.042 mm

## Slide 12: 10±3 MeV e+: Time Evolution of Phase Space in 2.2 T Solenoid (max Bz(r = 0))

## Slide 13: “10 MeV” e+: Time Evolution of Phase Space in 0.34 T Solenoid (max Bz(r = 0))

## Slide 14: 10 MeV e+: Example of 20 e+ Trajectories

## Slide 15: 10 MeV e+: Positron Losses and Beam Divergence
RMS vs Time
Number of e+ vs Time (107 primary e-)

## Slide 16: 10 MeV e+: Beam Size and Normalized Emittance
Normalized Emittance vs Time
Beam Size vs Time

## Slide 17: 10 MeV e+: Longitudinal Beam Size
At target:
σt = 0.4 ps
σz = 0.12 mm

## Slide 18: Next Steps
Optimal target position relative to solenoid:
  Vary target-to-magnet distance
  Target in the middle of solenoid
  Target between 2 solenoids
Change/optimize dimensions of solenoid (inner radius, length)
Tapered solenoid with a high field near the target (Adiabatic Matching Device AMD)