## Slide 1: Wien filter: Bolts and washers
03/17/2020
Gabriel Palacios
gabrielp@jlab.org

## Slide 2: Three cases are presented:
Bolts and washers material:
  All metal (perfect electrical conductor PEC)
  Alumina washers (99.6% lossless), PEC bolts
  All alumina
All at 20 kV per plate, 15 mm plates gap.
All models simulated with the whole vacuum enclosure setup, but only show plates, mounting tabs, HV spring guide, mounting springs, and plate insulators.

## Slide 3: Bolts, washers, long insulators
1 cm radius washer
1 mm radius curvature blend at bolt head
0.5 cm radius washer
Insulator design comes from Danny’s 32893-0112
Now with venting holes!

## Slide 4: All metal bolts and washers
Defined as PEC in CST Microwave studio

## Slide 5: Lateral cross section of the plates
Voltage on plates ±20 kV
5.1 MV/m
4.6 MV/m
5.9 MV/m
15 mm gap
Bolts and washers metal
±20 kV

## Slide 6: Zoom to mounting tab
3.2 MV/m
0.7 MV/m
Zoom here
1.1 MV/m
Bolts and washers metal

## Slide 7: Transparent insulators
3.2 MV/m
Triple point: 11 MV/m
Grounded
Peek through the insulator venting hole: Possible plasma chamber?
Bolts and washers metal

## Slide 8: Lateral cross section insulators
E-field channels that might lead particles towards mounting tab surface
Bolts and washers metal

## Slide 9: Transversal cross section insulators
3.2 MV/m
Bolts and washers metal
This plane

## Slide 10: Metal bolts, alumina washers
The bolts are defined as PEC and “floating” potential in CST.

## Slide 11: Lateral cross section of the plates
Voltage on plates ±20 kV
5.3 MV/m
5.2 MV/m
5.9 MV/m
15 mm gap
Metal bolts, alumina washers
Floating

## Slide 12: Zoom to mounting tab
11 MV/m
1 MV/m
Zoom here
0.6 MV/m
Metal bolts, alumina washers

## Slide 13: Transparent insulators
Triple point: 25 MV/m
Grounded
Peek through the insulator venting hole: Possible plasma chamber?
Had to change the scale cuz the field was so high!
Metal bolts, alumina washers

## Slide 14: Lateral cross section insulators
E-field channels that might lead particles towards mounting tab surface
Metal bolts, alumina washers

## Slide 15: Transversal cross section insulators
3.2 MV/m
Metal bolts, alumina washers
This plane

## Slide 16: All alumina bolts and washers
Lossless

## Slide 17: Lateral cross section of the plates
Voltage on plates ±20 kV
5.3 MV/m
5.2 MV/m
5.9 MV/m
15 mm gap
Alumina bolts and washers

## Slide 18: Zoom to mounting tab
0.2 MV/m
0.2MV/m
Zoom here
0.2 MV/m
Alumina bolts and washers

## Slide 19: Transparent insulators
Triple point: 1.1 MV/m
Grounded
Peek through the insulator venting hole: fix!
Alumina bolts and washers

## Slide 20: Lateral cross section insulators
E-field channels that might lead particles towards mounting tab surface
Alumina bolts and washers

## Slide 21: Transversal cross section insulators
3.2 MV/m
This plane
Alumina bolts and washers

## Slide 22: Conclusion:
Use all alumina washers and bolts, man!