## Slide 1: Simulated and Measured Extreme High Vacuum in the Jefferson Lab Polarized Electron Source
Marcy Stutzman, Philip Adderley,
Veronica Over, Matt Poelker
Thomas Jefferson National Accelerator Facility
Newport News, VA 23601, USA

## Slide 2: Thomas Jefferson National Accelerator Facility
US Department of Energy, 12 GeV electrons, recirculating linear accelerator
Up to 90% polarization from DC photoemission source
Electron currents to 200μA beam (CW) to four experimental halls
Halls A, B, C
Hall D
Source
Polarized source

## Slide 3: DC Photoemission Source
Polished high voltage electrodes
Strained superlattice GaAs/GaAsP photocathode
Surface preparation: Cs, oxygen or fluorine
Polarized Photoemission
Residual gasses ionized, limit operational lifetime
Base pressure approaching XHV ≡ P < 1x10-10 Pa
0.36
GaAs
GaAsP
GaAs
Strained
Superlattice
Photocathode
14 layers
-100 to
-350 kV
cathode
electrode
anode (ground)
light in
electrons out

## Slide 4: Outline
Achieving and measuring pressure in JLab systems
Begin exploration of systems with Molflow+ modeling for static vacuum
  Pressure distribution with appendage vs. inboard pumping
  Pressure distribution due to electrodes
Can we do any better?
  Leybold commercial cryopump
  Novel Boron Nitride NanoTubes (BNNT)

## Slide 5: CEBAF Polarized Inverted Gun Vacuum
Installed pumping
SAES WP1250 modules x 10 (5600 l/s total)
Gamma SEM/XHV ion pump
(35 l/s for hydrogen)
~ 25 micron TiZrV coating
400°C heat treatment for outgassing
Measured pressure ~1-2x10-12 Torr
Charge Lifetime: ~200 Coulombs
- cathode maintenance ~monthly
System works for CEBAF
Future Proposed Polarized Sources
require current ~50x higher
M.A. Mamun, A.A. Elmustafa, M.L. Stutzman, P.Adderley, and M.Poelker JVSTA,32, 021604 (2014)

## Slide 6: XHV gauges
Extractor gauge
  x-ray limit reduced through geometry
Axtran gauge
  Bessel box energy discrimination
  electron multiplier for low current measurements
Watanabe 3BG (Bent Belt Beam) gauge
  230° deflector BeCu housing
  JVSTA 28, 486 (2010)
Extractor
BBB
Axtran

## Slide 7: Test Chamber Base Pressure
Getters
  4 x WP950 modules
  1 GP500 pump
Ion pump
  35 l/s SEM style Ti/Tan
Outgassing rate
  1x10-12 TorrLs-1cm-2
Volume: 40 l
Area: 8000 cm2
Simple calculations: expected pressure
4 x 10-13 Torr

## Slide 8: Measured Pressure: 3 XHV gauges
Pressure ~ 4x10-12 Torr
Minor differences between three gauges
  Rely on manufacturer sensitivity
  Should be sent for calibration
Measured pressure ~10 times pressure from simple calculation
Chart: Base pressures
| Extractor | 3BG | AxTran
 | 3.13e-12 | 3.93e-12 | 4.43e-12

## Slide 9: Vacuum System Modeling near XHV
Motivation:
Appended pumping?
Pressure gradients through chamber?
Molflow+ software
R. Kersevan and J.-L. Pons, JVSTA 27, 1017 (2009)
Input:
  3D CAD model
  Outgassing
  Pump speed, locations
Output:
  Pressure distribution
Test chamber with ion and NEG pumps

## Slide 10: Test Particle Monte Carlo
Tracks simulated particles
  Pump speeds defined by sticking coefficients
  Outgassing rates as measured previously
  Compare simulation with measured results
Ion
pump
XHV gauges
NEG GP500 pump
NEG Sorb-AC WP950 pumps

## Slide 11: Molflow+ simulated pressure:
P (simulated) = 1.6x10-12 mbar
P (measured) = 4-6 x10-12 mbar
Much better agreement than simple calculations
Simulated Gauge Position
mbar
Ion
pump
NEG GP500 pump
NEG Sorb-AC WP950 pumps

## Slide 12: Add XHV Cryopumping
Cryopumps typically not bakable
  Adhesives for charcoal cryosorption surface
  Mechanics of closed-cycle helium refrigerators
Leybold bakable cryopump
  LN2 chill circuit to keep charcoal, adhesive, mechanics cold during vacuum bakeout
Boron nitride nanomaterial as cryosorber material
  Mechanical attachment, no adhesive
  Thermally conductive, heat stable, inert, carbon free

## Slide 13: Appendage Pumping: Cryopump
P(simulated)= 2.7x10-12 mbar
P(simulated)= 1.6x10-12 mbar
gauge
position
Valve Closed
Valve Open
Simulations show outgassing from valve, conductance severely limit
cryo-pumping on chamber
mbar

## Slide 14: Measured Performance of Leybold cryopump
Chart: Equilibrium pressures
NEG, Ion only | 4.1629e-10 | 5.2269e-10 | 5.8919e-10
NEG, Ion and Cryopumps | 3.192e-10 | 3.9767e-10 | 4.3491e-10
Pressure with CP valve open = ~4x10-10 Pa
Simulation: 3x10-10 Pa
Preliminary studies using Molflow+ simulations
Useful tool
Emphasize conductance limitations

## Slide 15: Novel Cryopump: BNNT
Boron Nitride NanoTubes
  Freestanding adsorber, no adhesive
  1g = 300 m2 surface area
BNNT first prototype
  T ~ 15K
  Heat load due to copper mesh absorption
BNNT second prototype improvements
  Fine wire attachment, no copper mesh
  Total 4.4g BNNT, ~1000 m2
  Attachment on both sides of fins
US Patent 9463433 issued October 2016

## Slide 16: BNNT simulations
Simulated pressure profile: Upgraded BNNT cryopump |  | 
Sticking coefficient: top and bottom of fins | α =0.003 | α =0.012
Simulated Gauge Pressure | 6.2x10-9 Pa | 1.55x10-9 Pa
First BNNT prototype | 
Sticking coefficient calculated from measured pressure | α =0.003
Measured pressure | 6.2x10-9 Pa
mbar
as built
α = 0.003
α = 0.012
2nd Prototype model

## Slide 17: BNNT Cryopump: First and Second builds
Chart: Hours

## Slide 18: Chamber geometry: High Voltage
350 kV benefits
  Eliminate capture
  Smaller volume for highest ionization cross section
  Higher bunch charge
High voltage modeling determines geometry
  Cathode shape
  Cathode diameter determines wall distance
8 MV/m
11 MV/m

## Slide 19: Simulation: 350 kV Chamber

## Slide 20: Conclusions
Measured pressure in operational CEBAF photogun: ~1x10-12 Torr (extractor gauge, backgrounds subtracted)
Test chamber pressure measurements with three XHV gauges in reasonable agreement after background corrections
Modeling emphasizes conductance effects with appended cryopump
Modeling BNNT system: BNNT sticking coefficient?
Beginning modeling to determine conductance effects, pressure distribution near high voltage electrodes
Future higher voltage, higher current systems balance high voltage performance and requirements with vacuum conductance

## Slide 21: Acknowledgements
Matt Poelker, Joe Grames, Don (Bubba) Bullard,
Marcy Stutzman, John Hansknecht, Shukui Zhang,
Carlos Hernandez Garcia, Philip Adderley, Riad Suleiman
U.S. DOE Contract No. DE-AC05-06OR23177 and with funding from the
DOE R&D for Next Generation Nuclear Physics Accelerator
Facilities Funding Opportunity Number: DE-FOA-0000339
Jefferson Lab
Center for
Injectors and
Sources

## Slide 23: Polarized Source Variations
Vertical Gun (100 kV)
  SLAC design
  First polarized electron source
  No NEG pumping
  No heat treatment
  Poor electron optics

## Slide 24: Polarized Source Variations
Vertical orientation
Horizontal gun
  Improve electron optics
  Add NEG pumping
  Cylindrical symmetry
  No heat treatment
  Vent and bake to change photocathode
  Photocathode chemistry (Cs) contaminates electrode, vacuum

## Slide 25: Polarized Source Variations
Vertical orientation (100 kV)
Horizontal gun (100 kV)
Load Lock Gun (100 kV)
  Separate chemistry from high voltage
  Load-Lock for cathodes
  400ºC heat treatment
  NEG coating
  High field points
  Thick flange outgassing
  Cylindrical symmetry broken

## Slide 26: Polarized Source Variations
Vertical orientation (100 kV)
Horizontal gun (100 kV)
Load Lock Gun (100 kV)
Inverted Insulator Load Lock Gun (130-200 kV)
  Eliminate DN275 Conflat flanges
  Heat treated, NEG coated
  Cylindrical symmetry broken
  Line of sight: insulator charging

## Slide 27: Polarized Source Variations
Vertical gun (100 kV)
Horizontal gun (100 kV)
First Load Lock Gun (100 kV)
Inverted Insulator Load Lock Gun (130 kV)
350 kV Inverted Gun
  Heat treated
  NEG coated
  Larger diameter
  Doped ceramic
  Version 1: NEG strip
  Version 2: WP modules, rotated on side

## Slide 28: Polarized Source Evolution: 20 years
First JLab polarized gun
Add NEG pumping: high polarization cathodes
Load Lock: avoid electrode and vacuum contamination
NEG coating
Eliminate thick flanges
400 ºC heat treatment
Higher voltage: larger diameter

## Slide 29: NEG pumping configurations
Initial design
  360º array surrounding cathode – anode gap
Load Lock
  Hemisphere array
Inverted Gun
  Rotate modules: eliminate line of sight to walls
350 kV Inverted Gun
  Strips instead of modules
  Rotate back to open configuration

## Slide 30: Add XHV Cryopumping
Cryopumps typically not bakable
  Adhesives for charcoal cryosorption surface
  Mechanics of closed-cycle helium refrigerators
Solutions other places:
  KEK, Katrin: Silversolder or Thermoguss bakable adhesives
  KEK: 2K helium flow, no compressor
Our research
  Leybold bakable cryopump
    LN2 chill circuit to keep charcoal, adhesive, mechanics cold during vacuum bakeout
  Boron nitride nanomaterial as cryosorber material
    Mechanical attachment, no adhesive
    Thermally conductive, heat stable, inert, carbon free

## Slide 31: Leybold pump performance
Chart: Time (days)