## Slide 1: CEBAF Source and Injector Upgrade Status Moller Collaboration Meeting November 11-12, 2016
Joe Grames
Center for Injectors and Sources

## Slide 2: Topics
CEBAF
4-Hall Laser Upgrade
Gun2 Operation
Delivering Spin in 12 GeV era
UITF – CEBAF Injector Upgrade
Gun Status
200 keV Wien
Upgrade Cryounit
Photocathode R&D

## Slide 3
Experiment | Beam Energy (GeV) | Pol (%) | I (µA) | Target (Length) | Apv (ppb) | Charg Asym (ppb) | Position Diff (nm) | Angle Diff (nrad) | Size Diff (δσ/σ)
HAPPEx-I (Achieved) | 3.3 | 38.8 68.8 | 100 40 | 1H (15 cm) | 15,050 | 200 | 12 | 3 | 
G0-Forward (Achieved) | 3.0 | 73.7 | 40 | 1H (20 cm) | 3,000-40,000 | 300±300 | 7±4 | 3±1 | 
HAPPEx-II (Achieved) | 3.0 | 87.1 | 55 | 1H (20 cm) | 1,580 | 400 | 2 | 0.2 | 
HAPPEx-III (Achieved) | 3.484 | 89.4 | 100 | 1H (25 cm) | 23,800 | 200±10 | 3 | 0.5±0.1 | <10-3
PREx-I (Achieved) | 1.056 | 89.2 | 70 | 208Pb (0.5 mm) | 657±60 | 85±1 | 4 | 1 | <10-4
QWeak-I (Achieved) | 1.155 | 89.0 | 180 | 1H (35 cm) | 281±46 | 8±15 | 5±1 | 0.1±0.02 | <10-4
QWeak | 1.162 | 90 | 180 | 1H (35 cm) | 234±5 | <100±10 | <2±1 | <30±3 | <10-4
PREx-II | 1.0 | 90 | 70 | 208Pb (0.5mm) | 500±15 | <100±10 | <1±1 | <0.3±0.1 | <10-4
MOLLER | 11.0 | 90 | 85 | 1H (150 cm) | 35.6±0.74 | <10±10 | <0.5±0.5 | <0.05±0.05 | <10-4
CEBAF Polarized Electron Injector

## Slide 4
MOLLER Injector
Replace 130kV gun with 200kV gun
Replace ¼ CM with an improved ¼ CM having an SRF capture section
No prebuncher
Upgrade Wien to 200 keV and improve spin flipper layout
More attention paid to beamline vacuum
Our new “1/4 cryomodule”:
2 cell capture section + 7 cell cavity,
should provide 10 MeV beam and introduce no x/y coupling, allow better matching, more adiabatic damping

## Slide 5
4-Hall Laser Upgrade
Summer 2016

## Slide 6
4-Hall Laser Upgrade
Fall 2016
Each laser is manually configurable to a 249.5 or 499 MHz RF spigot
Ops can ‘assign’ any laser to any hall e.g. now : Laser C => Hall A
Only 3 RF spigots presently available

## Slide 7
4-Hall Laser Upgrade
January 2017
New LLRF system with 4-spigots, one per laser
Remote control to change laser rep rate (laser + RF)
Provide phase control at each frequency (now all done at 499 MHz)
Spring 2017
Planned simultaneous 4-Hall beam test (if all Halls ready)
We anticipate 3-beam chopper will be limiting factor
Injector group (Kazimi) is working on scheme for new 4-Hall chopper

## Slide 8
8
Gun2 Operation
Spring/Fall 2016
  SSL GaAs/GaAsP SVT #5756-4 (Polarization ~ 87%)
  No heat/activation over Summer SAD
Jun 2016
Sep 2016

## Slide 9
Gun2 Operation
Fall 2016
Gun2 operating at -130 kV without any problems
Charge lifetime >100C with average current 70-80 mA

## Slide 10
Gun2 Operation
Fall 2016
Gun HV power supply may now remain ON in Power Permit
May anticipate improved reliability, monitoring and charge lifetime
First 5 weeks of
Spring 2016 Run
First 5 weeks of
Fall 2016 Run

## Slide 11
Delivering Spin in 12 GeV era
Spring 2016
Elegant model w/ synchrotron radiation to predict energy @ dipoles
Hall A arc energy measurement (+0.23% above machine value)
Integrated spin precession from injector to Hall A

## Slide 12
Delivering Spin in 12 GeV era
Fall 2016
LINACS reduced 4% to 1050 MeV for gradient headroom
Hall A arc energy measurement (+0.19% above machine value)
Elegant model and spin precession for Hall A @ 4th pass
Without spin dance Moller measurement indicate high polarization
Investigation about discrepancy in LINAC/ARC energy calibration
Hall A Moller @ 4th pass 8516 MeV
(11/1/16)

## Slide 13
UITF – CEBAF Upgrade Testing
TESTING MORE ROBUST (>300KV) INVERTED GUN
COMMISSIONING NEW 2/7 CELL CRYOUNIT
TEST 200KV WIEN FILTER

## Slide 14
UITF - CEBAF/ILC 200 kV Inverted Gun
Developed and ready for installation
Commissioned at Test Cave to 225 kV w/o field emission
Large grain Niboium electrode
-200kV
light in
e- out
photocathode

## Slide 15
UITF - Higher Voltage Polarized Source
8 MV/m
11 MV/m
Benefits of higher gun voltage will be tested
Stiffer beam leads to less loss
Higher voltage reduces improves QE
Rapid energy gain reduces ionization
450kV HVPS
Tested
HV Chamber
Baked ~2E-12 T
Prep Chamber ready for activation

## Slide 16
UITF – 200 keV Wien upgrade
UITF will provide opportunity for 200 keV Wien characterization
  10A magnet limits 200 keV spin precession to ~65 deg
  Jay proposed (JLAB-TN-15-032) to retrofit new 20A magnet coils to extend capability to higher beam energy
  Successfully tested HV feed thru to 20kV and polished the electrodes
Wien Upgrade for 100 deg precession |  |  | 
Beam Voltage | keV | 200.00 | 350.00
Integrated BL | G-cm | 3993.86 | 6788.51
Magnet Current | A | 15.36 | 26.11
Electric Field | MV/m | 2.67 | 5.27
Electrode High Voltage | kV | 20.05 | 39.56

## Slide 17
UITF - New CEBAF Injector Cryounit
2016 Commissioning at Test Lab
  Summer – Cryostat assembled + cryo @ UITF
  Fall – SRF commissioned to 20 MV/m @ CMTF
  Winter – Install @ UITF, planned up to ~8 MeV (klystrons)
Installation timeline at CEBAF in advance of Moller TBD

## Slide 18
UITF – Photocathode R&D
Testing benefits of Standard vs. DBR GaAs/GaAsP SSL
Standard photocathode: absorption in the GaAs/GaAsP superlattice < 5%
DBR photocathode : absorption in the GaAs/GaAsP superlattice >20%
Non-DBR photocathode
DBR photocathode

## Slide 19
UITF – Photocathode R&D
High polarization photocathodes
Standard high QE photocathode w/ polarization > 90%
Test DBR photocathode for reliability and lifetime before CEBAF option
At 776 nm:
Standard
  QE = 0.89%
  Polarization = 92%
DBR
  QE = 6.4%
  Polarization = 84%

## Slide 20
Summary
CEBAF
  Source is operating reliability w/ high polarization and QE
  Charge lifetime is good at typical Moller current, possible gain from HVPS
  4-Laser upgrade went well, will complete LLRF this Winter, then test delivery
UITF Injector Upgrade Activities
  CEBAF Upgrade 200 kV “tee” inverted gun is ready
  Higher voltage polarized gun w/ spherical electrode soon tested
  200kV Wien filter modification in progress
  New cryounit assembled and SRF commissioning completed, install soon
Not to forget…
  Final pass of Mott calibration before publication early 2017
  Stewart platform development can proceed if test “owner” identified
  Maybe some interest to test a helicity quad for spot size sensitivity?
  PQB tests at UITF e.g. low-noise receiver may be considered