## Slide 1: WIEN-FILTER SPIN ROTATOR IN THE CONTEXT OF pEDM
G. Palacios-Serrano, C. Hernández-García,
Thomas Jefferson National Accelerator Facility, Newport News, VA 23606, USA

## Slide 2: Introduction
The proton-electron dipole moment (pEDM) experiment requires*:
  Study the optimum material, height, and shape of electric field plates with a field strength of 4.4 MV/m for 4 cm plate separation, in order to minimize the highest E-field value.
  Small surface area E-field plates made of aluminum and coated with TiN have been developed and used at JLab; rather cheap and robust. Need to expand this technology to large-area, about 20 cm high and 2m long.
Diagram of the storage ring EDM concept. Jim Alexander et al, 2022.
* The storage ring proton EDM experiment. J. Alexander et al, 2022.

## Slide 3: We have experience!
We have built four Wien filters at JLab:
  Two 200 keV at CEBAF
    In operation since February 2021
    32 cm electrode plate
    1.5 cm gap
    20 kV max achieved voltage per plate
    2.7 MV/m max gap electric field
    Undergoing optics matching studies.
  A shorter-gap 300 keV at UITF
    In operation since July 2022
    32 cm electrode plate
    1.3 cm gap
    26 kV max achieved voltage per plate
    3.9 MV/m max gap electric field
  One with integrated ion pump at test lab
    Patent!
    Still on the works

## Slide 4: Ok but, what have we actually done?
3D modeling
Simulations
  E and B field maps
  Particle tracking
  Optimization
Assembled
  Polished
  Surveyed
  HV tested

## Slide 5: Challenges for the pEDM electrodes
Significant engineering concept and design!
176 kV gap voltage (88 kV per plate)
TiN-coated aluminum electrodes
  JLab has done this before on a smaller scale.
Tolerances
R28 alumina insulators
  Structural
  HV
  Ripple
Field homogeneity
Fringe fields
Spin dynamics
The storage ring proton EDM experiment. J. Alexander et al, 2022

## Slide 6: A start:
4.4 MV/m

## Slide 7: Thanks!
Fin

## Slide 9
Extras
Modelling
  The Wien filter is composed of
    HV electrode plates with mounting tabs and Rogowski profile
    HV spring guide contacts with spring coils
    HV electrical feedthroughs with alumina insulators
    MACOR mounting insulators
    Vacuum chamber with electrode mounting springs
    Magnet coils
    Magnet mirrors, pole plates and return yokes
Isometric view of 3D model of the existing CEBAF 130 keV Wien filter based on SLAC’s original design.