## Slide 1: Vacuum Window Meeting
Caryn 2/19/2020

## Slide 2: ATLIS: End of Spring Run
Rot ~45
Baseline birefringence and birefringence gradient measurement on present window
~45 deg (could be 20 or 30, as long as we approx. know what it is)
Pcup 10/20uA
Spot moves with steering lens +-0.5mm/1mm
RHWP scans (IA unplugged)
== know gradients we started with
If repeat after new window installed, know what we ended up with
RHWP
Steering lens
Known bir. direction

## Slide 3: Air test
HWP
QWP
pol
pol
pd
Translation stages
Rot stage
Rot stage
Rot stage
-2 polarizers
-3 rotation stages
-2 translation stages
-1 photodiode+scope OR power meter
scope
-prepare initial state
-rotate analyzer to find direction and magnitude of bir.
-assume direction of dn is the same, translate window
-for a few positions, repeat rotation scan to verify direction of dn
Steering lens?

## Slide 4: Vac test
HWP
QWP
pol
pol
pd
Rot stage
Motorized Rot stage
Rot stage
-2 polarizers
-2 rotation stages
-1 motorized rot stage
-1 photodiode+scope OR power meter
-vac feedthroughs
-breadboard
scope
-prepare initial state
-before pumping down, rotate analyzer to find direction and magnitude of bir.
-pump down, monitoring transmission
-rot anal. to find new direction and mag of bir.
-assume direction of dn is the same, translate beam on cathode with laser
-for a few positions, repeat rotation scan to verify direction of dn
Bread board
jack?
Steering lens?

## Slide 5: Vac test
HWP
QWP
pol
pol
pd
Rot stage
Rot stage
Rot stage
-2 polarizers
-3 rotation stages
-1 photodiode+scope OR power meter
-vac feedthroughs
-chamber
-jack?
scope
-prepare initial state
-before pumping down, rotate analyzer to find direction and magnitude of bir. 1, then insert2, repeat
-pump down, monitoring transmission
-rot anal. to find new direction and mag of bir.
-assume direction of dn is the same, translate beam on cathode with laser
-for a few positions, repeat rotation scan to verify direction of dn
1
2
jack?
Steering lens?

## Slide 6: Vac test
HWP
QWP
pol
pd
Rot stage
Rot stage
-2 polarizers
-2 motorized rot stages
-1 photodiode+scope OR power meter
-vac feedthroughs
-breadboard
scope
-prepare initial state
-before pumping down, rotate analyzer to find direction and magnitude of bir.
-pump down, monitoring transmission
-rot anal. to find new direction and mag of bir.
-assume direction of dn is the same, translate beam on cathode with laser
-for a few positions, repeat rotation scan to verify direction of dn
Bread board
mirror
jack?
Steering lens?