## Slide 1
Detector Geometry: Envelope and Active Regions
50 cm external radius
45 cm of active area
considering a 5 cm outer ring for gas frames and services location.
Endcaps Envelope Dimensions -
Disks Outer Radius
MPGD Disk | Max Z Pos (cm) | Disk Outer Radius (cm) | Outer Active Reg. radius (cm) | Calculated Beam pipes radii (mm) | Offset (mm) | Disk Inner Radius (cm) | Inner Active Reg. radius (cm)
HD MPGD 2 | 163.5 | 50 | 45 | 55.8 | 22.5 | 9 | 10.5
HD MPGD 1 | 150.5 | 50 | 45 | 53.1 | 19.9 | 9 | 10.5
LD MPGD 1 | -112.5 | 50 | 45 | 37.7 | -3.1 | 4.5 | 6.0
LD MPGD 2 | -122.5 | 50 | 45 | 39.2 | -3.4 | 4.5 | 6.0
Calculated
Radii
Disks Inner Radius
different for the two HD and LD regions
HD: 9 cm inner radius
10.5 cm radius of active area
LD: 4.5 cm inner radius
6 cm radius of active area
considering 1.5 cm gas frame
Beam Pipes Envelope Radii and Offsets
The geometrical envelopes are available at: https://eic.jlab.org/Geometry/Detector/Detector-20240117135224.html

## Slide 2
-3.61
1.993.34
Pseudo-rapidity coverage: effective ranges
Component | Z (cm) | Inner Active Reg. Radius (cm) | min (deg) | max | Outer Active Reg. Radius (cm) | max | min
HD MPGD 2 | 162 | 10.5 | 3.35 | 3.43 | 45 | 15.52 | 1.99
HD MPGD 1 | 148 | 10.5 | 4.06 | 3.34 | 45 | 16.91 | 1.9
LD MPGD 1 | -111 | 6 | 3.09 | 3.61 | 45 | 22.07 | 1.63
LD MPGD 2 | -121 | 6 | 2.83 | 3.69 | 45 | 20.40 | 1.72
Component | Z (cm) | Inner Active Reg. Radius (cm) |  |  | Outer Active Reg. Radius (cm) |  | 
HD MPGD 2 | 162 | 10.5 | 3.35 | 3.43 | 45 | 15.52 | 1.99
HD MPGD 1 | 148 | 10.5 | 4.06 | 3.34 | 45 | 16.91 | 1.9
LD MPGD 1 | -111 | 6 | 3.09 | 3.61 | 45 | 22.07 | 1.63
LD MPGD 2 | -121 | 6 | 2.83 | 3.69 | 45 | 20.40 | 1.72
The range covered by the MPGD Endcap tracking disks is compliant with requirements.
The minimum value is not larger than 2
it is limited by the outer HD disk location/dimensions
The maximum value is not less than 3.34
it is limited by the inner HD disk location/dimensions

## Slide 3: Actions – To Do List – Hardware et al.
What | Who | When
Implement 500 pitch strip density in the endcap drawings 32 FEBs/disk |  | 
Define the dimensions of the outer “service” area (non active-area) |  | 
Define the frame dimensions |  | 
Study the strip routing to the connector identify connectors – ask Irakli Damien |  | 
Gap-size definition (3mm drift gap + 3 mm GEM foil gap) |  | 
Assessment of the spatial resolution requirements |  | 
Material budget assessment ( including GEM pre-amplifier) |  | 
Gap-size definition (3mm drift gap + 3 mm GEM foil gap) |  | 
GEM sectors studies and definition |  | 
LV needs |  | 
Services & Cooling |  | 
HV supply choice |  | 
Endcaps survey/photogrammetry plans /targets to be installed? |  | 
Mounting procedures and relative constraints |  | 
Humidity sensors |  | 
Gas distribution system |  | 
What | Who | When
Define the dimensions of the outer “service” area (non active-area) |  | 
Define the frame dimensions |  | 
Study the strip routing to the connector identify connectors – ask Irakli Damien |  | 
Gap-size definition (3mm drift gap + 3 mm GEM foil gap) |  | 
Assessment of the spatial resolution requirements |  | 
Material budget assessment ( including GEM pre-amplifier) |  | 
Gap-size definition (3mm drift gap + 3 mm GEM foil gap) |  | 
GEM sectors studies and definition |  | 
LV needs |  | 
Services & Cooling |  | 
HV supply choice |  | 
Endcaps survey/photogrammetry plans /targets to be installed? |  | 
Mounting procedures and relative constraints |  | 
Humidity sensors |  | 
Gas distribution system |  | 

## Slide 4: Actions – To Do List - Software
What | Who | When
Detector geometry simulation (Matt supervision&support) |  | 
Detector response simulation (Matt supervision&support) |  | 
Implementation of MPGD endcaps in the Tracking |  | 
Ghost hits and disks orientation | Mariangela, Lucilla | 
On-Line Calibration |  | 
Alignment procedure |  | 
Slow controls |  | 
On-line monitoring |  | 

## Slide 5: Actions – To Do List - Plans
What | Who | When
Financial plan: - ask Rui for disks uRwell and GEM foils costs |  | 
Financial plan: - FEB costs (including cables) |  | 
Financial plan: - HV costs (including cables) |  | 
Financial plan: - LV distribution costs (including cables) |  | 
Financial plan: - Cathods |  | 
Financial plan: - Peek Frames |  | 
Financial plan: - Connectors |  | 
Financial plan: - Mechanical support |  | 
Overall time plan and costs |  | 
Understanding the assembly needs (clean room, instrumentation, materials) |  |