## Slide 1: DSG NPS Collaborators’ Meeting Update
Aaron Brown and the Detector Support Group
02/25/2021

## Slide 2: Contents
Radiall-to-SAMTEC High Voltage (HV) Cables
  Fabrication
  Testing
HV Schematic
Hardware Interlock System Development
  Tentative signal list
  Dew point interlock
CSS-BOY Screen Development
Conclusion

## Slide 3: Radiall-to-SAMTEC HV Cables: Fabrication
Cables being fabricated by Mindy Leffel – five of 40 complete
Grounding wire connected to each braided shield at Radiall connector end
SAMTEC connectors (labeled 1,2, and 3) have 15, 15, and 6 HV channels, respectively

## Slide 4: HV Schematic
Mindy Leffel is fabricating the high voltage cables

## Slide 5: Radiall-to-SAMTEC HV Cables: Testing
Testing goals
  Observe cables’ SAMTEC connectors at 1100 V
  Verify neighboring channels don’t change voltage or current if a channel, or adjacent channel, is turned off
Marc McMullen is developing the Test Chassis
Test chassis internal schematic developed in AutoCAD

## Slide 6: Hardware Interlock System Development
Tentative signal list: ~180 monitored signals
Signal readout from sensors
  To Keysight → cRIO → EPICS
  To cRIO → EPICS

## Slide 7: Hardware Interlock System Development
Minimum coolant temperature of chiller is 5°C
→ Dew point should be interlocked at ≤ 4°C
→ For operational temperature of 18oC, max RH ≤ 40%
  Providing margins for humidity and temperature sensors accuracies

## Slide 8: CSS-BOY Screens Development
Screen enables user to turn off channels individually
Buttons to be added:
  Turn off slot
  Turn off crate
  Turn off both crates
Snippet of Module/Channel Power CSS-BOY screen

## Slide 9: Conclusion
Work is progressing smoothly

## Slide 10
Thank You