## Slide 1: NPS Calorimeter
ERR, May 15 (2019)
Carlos Munoz Camacho, IPN-Orsay
for the NPS Collaboration
IPN-Orsay NPS group:
E. Rindel, T. Nguyen Trung, G. Hull, J. Bettane
C. Domingues, M. Imre, B. Mathon, L. Seminor, L. Vatrinet, B. Geoffroy
H. S. Ko, C. Munoz

## Slide 2
Overview: conceptual design
Back view
Design 100% completed
30x36 (1080) PbWO4 crystals (2x2x20 cm3)
Hamamatsu R4125 PMTs JLAB, YEREVAN
Custom-made active bases
Crystals placed in a 0.5 mm-thick carbon frame to ensure good positioning
PMTs accessible from the back side to allow maintenance
Calibration and radiation curing with blue LED light though quartz optical fiber
JLAB, CUA
OHIO, YEREVAN
ORSAY
Calorimeter frame:
Survey & alignment requirements: ~1mm
Back view
Front view

## Slide 3
Crystals status
Quality analysis:

## Slide 4
Crystals status
Crystal procurement:
SICCAS
CRYTUR
160 rejected crystals
SICCAS:
460 (2017-18) onsite
CRYTUR:
100 (2018) onsite
250 (ordered 2019)
300 (ordered 2019 - replacing an order to SICCAS)
=======
650
All crystals will be onsite by Summer 2020

## Slide 5
PMT and voltage dividers
PMT (Hamamatsu R4125 ):
340 onsite, 1000 more ordered (delivery by Summer 2019)
Voltage dividers:
80% of them (865) assembled. Completion expected by Summer 2019
Voltage dividers tested in the Hall D ComCal prototype:
5
FADC amplitude (count)
FADC amplitude as a function of the beam energy
10 GeV : 3200 FADC channels
FADC range: 2 V (maximum range)
Typical HV: 700 – 750 V
Array of 12x12 PbWO4 crystals

## Slide 6
Linearity of the FADC peak amplitude
750 V
2 V FADC range
850 V
2 V FADC range
Original PMT base, gain 25
Modified base, gain 3
Some non-linearities on the level of 2 – 3 % were observed for the original PMT base
(PMT was operated at relatively small HV, recommended HV is about 1 kV)
The linearity can be improved by reducing the amplifier gain and increasing HV:
change of 1 resistor in the base needed
Anode current will be evaluated and gain adjusted as needed

## Slide 7
Energy resolution of prototype
More details can be found in GlueX-doc-3590, GlueX-doc-3998, V. Berdnikov, A.Somov, J. Crafts



NPS prototype
HyCal (Hall B)
NPS Prototype
3x3 array
bypassed amplifier
Relatively good energy resolution.
Consistent with Hall B HyCal, constructed with SICCAS crystals
HyCal

## Slide 8
Calorimeter carbon frame
PMT assembly
m-metal shield
PMT
HV divider
2-cm of C (0.5 mm thick) at the front and
back of the crystals
Easy disassembly of PMT block
with one long single captive screw

## Slide 9
Carbon frame: impact on energy resolution & efficiency
1.2% (ideal case) to 1.6% at 10 GeV
with 1mm of air between crystals
More than 97% of energy collected after 22 X0

## Slide 10
Carbon frame: mechanical simulations and tests
Simulations:
Less than 0.2 mm deformation at the center
0.4 mm deformation on external layer
Very resistant structure
Real tests on the bench ongoing:
Effect of 1 crystal
in each cell

## Slide 11
Cables and fibers
180mm

## Slide 12
PCB design (HV, signal, LED)
Routing of the board completed
SMA connectors (signal)
PMT
Ficher conector for HV (smaller than regular SHV)
LEDs
LED control
HV input
Signal outputs
Slots for rails
Design 100% completed
1st board being manufactured (delivery by end of May)

## Slide 13
Calibration and curing
glue
grease
1 blue LED per channel (onto the PCB board)
Pulsed mode for calibration
Continuous mode for curing
Light through 800 mm diameter silicate fiber (radiation hard)
TO DO:
LED control board (JLAB)

## Slide 14
Radiation environment
1 mA, 15 cm LH2
Geant4 simulation, cross-checked with RadCon estimates
30 Gy/h
Curing expected to be needed
every few days or few weeks, depending on the kinematics setting
Irradiation and curing tests made with 30 Gy at 1Gy/min rate

## Slide 15
Irradiation and curing tests
Strong 60Co source (3000 Cu)
Radiation hardness measurements

## Slide 16
Irradiation and curing tests
Blue LED optical bleaching
30 Gy
(at ~1Gy/min)
Radiation damage recovered with a few hours of blue light curing

## Slide 17
Full scale mock-up of NPS frame
Cable lengths defined:
32 cm PMT->PCB (HV+signal)
Signal PCB-> top of box: 0.5-1.5 m

## Slide 18
Full scale mock-up of NPS frame
18 cm
Human sized detector
Easy PMT maintenance
Fiber
HV+signal

## Slide 19
Temperature zones
Heating Zone : 500mW/channel = 540 W
Crystals Zone : @ 18°+/-0,1°
External Zone : T° = 22°c

## Slide 20
Temperature control: back side
Heating electronic Zone : 500mW/channel = 540 W
Heating zone cooled with 2 heat exchangers 6320G3SB (Lytron)
+ funs + 1 chiller Kodiac RC006G03BG3
Crystals Zone : @ 18°+/-0,1°
Heat exchangers & chiller procured
Same manufacturer than the ones used for HyCal
Higher heat load specification

## Slide 21
Temperature control: crystals
Crystals Zone : @ 18°+/-0,1°
Foam : thermal insulator
4 copper plates around + 1 intermediate copper plate + 1 other chiller ( cooling separated from backward zone)

## Slide 22
Summary
NPS calorimeter construction in progress:
  All crystals and PMT/bases will be onsite by Summer 2020
  Calorimeter frame components will be shipped (from Orsay) early 2020
  Assembly (+tests) at JLab can start from September 2020
No show-stoppers anticipated

## Slide 23
Back-up

## Slide 24
1% constant term added to
simulation (miscalibration, etc)

## Slide 25
Beam Test of the Calorimeter Prototype
Array of 12x12 PbWO4 crystals
Beam hole: 2 x 2 crystals
Tungsten absorber covers the inner
most layer (taken from HyCal)
Water cooling (minimum 5 C),
nitrogen purge
LED-based gain monitoring system
Positioned on X-Y movable platform
Installed in the experimental Hall D. Used to detect Compton events in the PrimEx D experiment
- successfully operated during PrimEx D production run in the Spring of 2019

## Slide 26: Calibration
Move each calorimeter module to the photon beam
- Calibration runs at small luminosity (rate in the module 30 kHz at 30 MeV threshold)
Use beam energy provided by the Hall D tagger counters to equalize gains
10 GeV : 3200 FADC channels
FADC range: 2 V (maximum range)
Typical HV: 700 – 750 V
FADC amplitude (count)
FADC amplitude as a function of the beam energy

## Slide 27
Linearity
750 V
2 V FADC range
850 V
2 V FADC range
Original PMT base, gain 25
Modified base, gain 3
Some non-linearities on the level of 2 – 3 % in the calorimeter response were observed for the original
PMT base for both the peak amplitude and pulse integral
- PMT was operated at relatively small HV, recommended HV is about 1 kV
The linearity can be improved by reducing the amplifier gain and increasing HV. Some tuning of the
PMT base may be required
Linearity of the FADC peak amplitude

## Slide 28
Energy Resolution



NPS prototype
HyCal (Hall B)
NPS Prototype
3x3 array
bypassed amplifier
Relatively good energy resolution, which is consistent with the resolution of the
Hall B HyCal calorimeter (which was constructed using SICCAS crystals)
This plot will be updated
More details can be found in
GlueX-doc-3590, GlueX-doc-3998, V. Berdnikov, A.Somov, J. Crafts

## Slide 29
Energy Resolution
3x3 SICCAS crystals
3x3 CRYTUR crystals