## Slide 1
NPS mechanical design
11/13/2018 Jlab meeting

## Slide 2
General view
Mike Fowler structure design
Lifting frame
Base with rails
Black box

## Slide 3
General view
structure design + calorimeter
Calorimeter

## Slide 4
General view
structure design + calorimeter
+ connectic
PCB cards and cables

## Slide 5
Calorimeter
36 raws of 30 crystals =1080 crystals 0,5 x 20,5 x 200 mm
Cooling copper plates around the calorimeter + insulation with Depron in order to maintain the T° @ 18°=/- 0,1 °(Study in progress)
Pitch between 2 crystals = 21,35 mm in each direction (gap between 2 crystals = 0,8mm
Each crystal is wrapped of reflective sheet on each side except the back side toward the PMt (Reflecteurs, Enhanced Specular Reflector 3M S+ESR 65µ thickness)

## Slide 6
Calorimeter support
Front side alveoles (20 mm width)
Back side alveoles (20 mm width)
Aluminum frame (20 mm width)
Spacers and threaded rods between the 2 frames

## Slide 7
Calorimeter support: Back side alveoles details
Carbon plates glued on the ref. plate
Reference Aluminum plate
(on which are fixed the PMts)
Carbon plates 0,5 mm thickness crossed

## Slide 8
Calorimeter support: Front side alveoles details
Insert plastic part inside each alveole
(after insertion of the crystal)
Blocking plastic parts for an axial maintain of the crystals
Carbon plates 0,5 mm thickness crossed

## Slide 9
PMt assembly
Mu metal shielding
Copper plate for cooling
PMt
PCB
Optic fiber for monitoring and curing

## Slide 10
PMt and crystal assembly cut view
PMt
Optic fiber for monitoring and curing

## Slide 11
Cables , PCB cards and connectors
5 Cables for HT ,signal and ground
Optic fiber for monitoring and curing
1 Pcb card per column
800 x 230 x1,6 mm

## Slide 12
Cables , PCB cards and connectors
5 Cables for HT ,signal and ground /chanel
Optic fiber for monitoring and curing
Sma connector
Detail : 1 LED/channel connected to optic fiber
Translation system
3 HV connectors
LED connector

## Slide 13
Cables , PCB cards Translation
Slide the PCB in order to permit the acces to the PMTs
25 cm seems ok : test in orsay with a moke up

## Slide 14
Thermical aspect
Heating Zone : 500mW/channel = 540 W
Crystals Zone : @ 18°+/-0,1°
External Zone : T°?
Intermediate Zone : Thermical Resistance
Intermediate Zone : Made of Glass , Vacuum (PMt)
Depron (Thermal insulator)

## Slide 15
Thermical aspect: Crystal zone
Crystals Zone : @ 18°+/-0,1°
Copper plate with cooling system
Depron: thermal insulator

## Slide 16
Thermical aspect: Heating zone
Copper plate with cooling system
Copper for Heating conduction (via gap pad)

## Slide 17
Thermical aspect: Heating zone

## Slide 18
500mWatts sur une plaque en cuivre
Refroidissement interne 18°
Plaque froide à 18°
Thermical aspect: Heating zone

## Slide 19
500mWatts applied on each PMt zone
Cooling 18°
This approximative calculation show the difficulty to cool the plate in the center
Thermical aspect: Copper plate 10 mm thickness cooling

## Slide 20
This model show an improvement for T° but difficulty to cool the center
Thermical aspect: Copper plate 20 mm thickness cooling
500mWatts applied on each PMt zone
Cooling 18°