## Slide 1: Hall C’s CPS Magnet
Steven Lassiter Sept 19,2022

## Slide 2
Magnet steel is 1006 Poles are Permendur-V2 Water cooling of poles Water cooled coils Luvata #6801 conductor
Internal Shielding is Heavy Met Tungsten (90W,7Ni,3Fe)
CPS Magnet Steel : Width = 75cm
Height = 77.8cm
Length = 79cm

## Slide 3: Coils, Absorber & Pole Cooling Plates
Coils 55 turns/pole
Cu Absorber Center Channel 3mm x 3mm
Poles and embedded Cooling Plate

## Slide 4: CPS Tosca model updated to include bolts holes, cutouts and pole cooling plate J=500A/cm^2, Yoke = 1010*, Pole= Supermendur Max Pole field 3.89T, tracks: electrons 11 Gev @ 2.7uA
*Yoke has been upgraded to 1006

## Slide 5
30 electrons tracks shown at the front of the magnet and at the center.

## Slide 6: Yoke and Pole Magnetization Coils suppressed for visual clarity Peak field is 3.8T

## Slide 7: Stray Fields 10 Gauss fields extends out to ~80cm from ends
10 Gauss lines

## Slide 8: Coils : Based on Vendors Coil Length & Turns
Plenty of overhead – We spec’d a 12.5kW heat load to the coil

## Slide 9: High Radiation considerations (~20 MRad)
Use OFHC copper to minimize radiation swelling of copper.
Use BT Polyimide resin with Boron free glass tape insulation for coil fabrication. Good for GRad.
Design for all LCW, Power and I/O connections to be outside the shielding box.

## Slide 10: CPS Copper Absorber To minimized Thermal expansion effects along the z axis, center sections was sliced into 3mm thick blocks with a 1mm gap between them

## Slide 11: Heating Profile Along Absorber Heat Flux is applied uniformly over the surface area of each block Group of 4 blocks have the same heat flux
Chart: Rastered Beam Deposited
| 1.6 | 3.2 | 4.8000000000000007 | 6.4 | 8 | 9.6 | 11.2 | 12.799999999999999 | 14.399999999999999 | 15.999999999999998 | 17.599999999999998 | 19.2 | 20.8 | 22.400000000000002 | 24.000000000000004 | 25.600000000000005
 | 6637411.4601 | 8235266.6895 | 10324796.3171 | 12783075.9724 | 15241358.9254 | 18682984.0794 | 22370441.486 | 26303737.7406 | 30974537.3482 | 36137011.3541 | 41176564.2872 | 46093202.7428 | 50272334.5477 | 53591038.6289 | 55188897.1559 | 55311739.0837
 | 55311739.0837 | 53590820.98 | 50640715.2317 | 45723931.6768 | 41052980.3745 | 35767446.7919 | 30113156.5862 | 24458863.0828 | 19173326.2025 | 14502374.9001 | 10323097.996 | 7250077.7704 | 4545814.1678 | 2701971.6935 | 1595642.4654 | 980981.0401 | 612151.8673 | 366240.4697 | 366167.9201 | 243174.2976
Fitted
30kW of Heat applied as surface flux to bottom surface of the channel

## Slide 12: Stress and Thermal Expansion BC: Bottom Surface fixed, Top surface is free
Yield Stress: C10200 OFHC 4.3E3 psi C11000 ETP 1.04E4 psi
Highest stresses are due meshing size and sharp corners Still stresses in main body are above yielding for the majority of absorber
Tmax = 720°C Stress (vm) = 118 ksi (814MPa)
Deflection (in) = 0.025 (0.64mm)

## Slide 13: Close up of Highest Temperature Region Tmax = 720C
Thermal expansion of bottom aperture is of the order of 0.4mm or 13% of the opening. Does not impinge upon beam acceptance.
If a gap forms between top and bottom half of the absorber, then Tmax climbs to 1,140C
Top Half
Bottom Half

## Slide 14: Initial Fluent modeling Uniform heat deposit along inner channel just bottom half of absorber modeled
Total amount of heat source applied to the copper absorber was 30kW.
There are 58 individual heat source blocks.
Therefore 30kW/58 = 0.5172 kW was applied for each block.
Volume of each block is 29.1 mm3 or 2.91 x 10-8 m3 [3mm x 1.0mm x 9.7mm]
Energy source for each block was then 517.2 W/2.91 x 10-8 m3 = 1.78 x 1010 W/m3
Boundary Conditions for the inlet were the following:
Velocity of fluid 1.8 m/s (6 ft/s) in order to prevent corrosion
Temperature of the fluid at the inlet 303.2K (300 C)
Boundary Conditions for the outlet were the following:
Gauge pressure 206,843 pascals (30psig)
Backflow total temperature 303.2K (300 C)

## Slide 15: Solution converged and results look physically ok Max Temp of 617°C .

## Slide 16
LCW Temperature profile Temp rise ~28°C
LCW Pressure Profile Delta P <1psig
Cooling of LCW at the closed ends has since been resolved in Model

## Slide 17: CPS Energy Deposition Plots

## Slide 18: Fluka Data: grid overlaid on cross section of Absorber Spacing is 1mm x 1mm in XY plane XY planes are spaced 10mm apart in Z
Fluka data: heat load sum was only 25kW. Each data point was scaled by 30/25 to reach a sum total heat load of 30kW

## Slide 19: Bottom half of the absorber with the Grid map overlaid

## Slide 20: Grid Points vs Absorber Geometry
X= -0.5mm
X= +0.5mm
Data points are at the center of 1mm x1mm x10mm long volume
Each plane is 1mm spaced in X and Y
X= +1.5mm
X= +2.5mm

## Slide 21: YZ Plane cuts of Heat deposited [W] at x=0.5mm
Top of absorber
Bottom of absorber
Center section of absorber
Z Axis
Y axis
Max Q=203W Sum of heat in this plane 4.90kW
X= +0.5mm

## Slide 22: YZ Plane cuts of Heat deposited [W] at x=1.5mm
Max Q=38.3W Sum of heat in this plane 2.61kW
X= +1.5mm

## Slide 23: YZ Plane cuts of Heat deposited [W] at x=2.5mm
Max Q=16W Sum of heat in this plane 1.82kW
X= +2.5mm

## Slide 24: CPS Prototype
Central section of the lower absorber, where beam heating will be at the maximum, is prototype for testing of:
A: fabrication of cutting slits and brazing of copper sections.
B: test various cooling channels options and to verify against Fluent modeling.
C: Temperature and thermal expansion verification to test FEA modeling.

## Slide 25: Temperature Profile with two 1.2kW heaters
Tmax=893°C of Heating rods holder
T(absorber)=212°C at base of cooling channel

## Slide 26: Displacement and Stresses for two 1.2kW heaters 0.26mm and 515MPa (75.ksi) Temperature along top Absorber is 212°C.

## Slide 27: CPS Prototype
Testing hardware is being acquired.
Power connections and components have been requested from Spectrometer support group.
Testing will hopefully begin in the late fall.

## Slide 28: Prototype Cooling Circuit Design 1

## Slide 29: Conclusion
CPS magnet and coils are a straight forward & basic design but uses expensive high mu material. Procurements are under way.
Estimates of the Absorber heating and cooling have been used in the design of the magnet – addition of pole cooling plates, providing clearances between coil/pole and the Absorber.
A complete 3D thermal modeling of the Absorber and the magnet, using Fluent, is ongoing. The 3D heating profile data from Fluka is being read directly into Fluent.
Prototype of the Absorber has been built and is being prepared for testing to validate FEA models and options for the LCW cooling profile.