## Slide 1
FPGA
FPGA_DAC
500 MSPS
ADCs
monitor
Switch ADG1611
LDOs
Vout adj.
CH180
Switch ADG1611
CH108
Switch ADG1611
CH3
Switch ADG1611
CH2
Switch ADG1611
CH1
Amplifier AD8021
Switch ADG1611
CHmonitor
Bleach_En(6:1) /(10:1)
Channel_En(108:1) /(180:1)
VME_64
JTAG
engine
Config
memory
Trigger
Clock
In/Out
VME +5V
DAC_D(5:0)
2x80ft ribbon cable
VME LED Driver (VLD) design
Bleaching current limit
‘Serial termination’,
Cable reflection suppression
AC or DC coupling
To be determined
1080 (30x36) LEDs, through long ribbon cables.
Calibration: individually controllable, up to 110 mA, ~ns pulses
Bleaching: All ON, 35 mA, many hours
Design in progress
William GU
No protection

## Slide 2
VLD design
FPGA_DAC
6-bit
500 MSPS
DAC_D(5)
DAC_D(4)
DAC_D(3)
DAC_D(2)
DAC_D(0)
DAC_D(1)
DAC_OUT
FPGA
1, 0, Z
FPGA_enable(1)
FPGA_enable(180)
FPGA_enable(…)
FPGA_enable(2)
LED Cal pulse
LED(1)
LED(180)
LED(…)
LED(2)
DAC_D: width adjustable with steps of 2ns
Amplitude: 3.3V, 0V, or high impedance (each bit)
ADG1611:
1 Ohm typical on resistance
+3.3V enable control
+12V single supply.
William GU

## Slide 3
VLD PCB
80-pin 3M P5E
36-LEDs #3
80-pin 3M P5E
36-LEDs #2
80-pin 3M P5E
36-LEDs #1
LEMO I/O
Trigger Clock
XC7A200T
FPGA
On-board (?)
80-pin 3M P5E
36-LEDs
On-board (?)
80-pin 3M P5E
36-LEDs
VME64x
1080 channels:
* 10 VLDs: the front panel
* 6 VLDs: the front panel and on-board

## Slide 4
Trigger Interface for NPS
Existing trigger/Clock/Sync distribution system
(SHMS/HMS)
TI_master
NPS#1
TI_DC
Fiber
#1
Fiber
#5
#6
#7
#8
NPS#2
TI
NPS#3
TI
NPS#4
TI
NPS#5
TI
TI_DC: TI New mode of operations:
When the TI_DC is set to master mode, these five crates behaves like an independent (DAQ) system.
When the TI_DC is set to Daisy Chain mode, it receives Trigger/Sync/Clock from, and sends BUSY to the SHMS/HMS master TI via fiber#1 (as a salve TI); fans out the Trigger/Sync/Clock to, and accepts BUSY from fiber#5, #6, #7, and #8 as a TD (or master TI).
TI_DC FPGA firmware is being developed/tested
Long fiber from CH to HUT
Short fibers inside HUT
Minimum fiber route (addition), minimum existing (SHMS/HMS) trigger interface change.