## Slide 1: NPS Calorimeter
ERR, May 15 (2019)
Carlos Munoz Camacho, IPN-Orsay
for the NPS Collaboration
IPN-Orsay NPS group:
E. Rindel, T. Nguyen Trung, G. Hull, J. Bettane
M. Imre, B. Mathon, L. Seminor, L. Vatrinet, B. Geoffroy
H. S. Ko, C. Munoz

## Slide 2
Conceptual design
Front view
Back view
100% completed
30x36 (1080) PbWO4 crystals (2x2x20 cm3)
Hamamatsu R4125 PMTs
Custom-made active bases (covered in some other talk?)
Crystals placed in a 0.5 mm-thick carbon frame to ensure good positioning
PMTs accessible from the back side to allow maintenance
Calibration and radiation curing with blue LED light though quartz optical fiber

## Slide 3
Crystals status
?% crystals onsite
Procurement timeline…
Quality analysis:
SICCAS
CRYTUR
160 rejected crystals
will request update from Vladimir/Tanja

## Slide 4
PMT and voltage dividers
PMT: all ordered (?% onsite) ?
Bases: % produced? (Details on potential modifications, etc) ?
will request update from Julie

## Slide 5
Calorimeter carbon frame
PMT assembly
m-metal shield
PMT
HV divider
2-cm of C (0.5 mm thick) at the front and
back of the crystals
Easy disassembly of PMT block
with one single captive screw

## Slide 6
Carbon frame: impact on energy resolution & efficiency
1.2% (ideal case) to 1.6% at 10 GeV
with 1mm of air between crystals
More than 97% of energy collected after 22 X0

## Slide 7
Carbon frame: mechanical simulations and tests
Simulations:
Less than 0.2 mm deformation at the center
0.4 mm deformation on external layer
Very resistant structure
Real tests on the bench ongoing:

## Slide 8
Cables and fibers
180mm

## Slide 9
PCB design (HV, signal, LED)
Routing of the board completed
SMA connectors (signal)
PMT
Ficher conector for HV (smaller than regular SHV)
LEDs
LED control
HV input
Signal outputs
Slots for rails
Design 100% completed
1st board being manufactured (delivery by end of May)

## Slide 10
Full scale mock-up of NPS frame
Cable lengths defined:
32 cm PMT->PCB (HV+signal)
Signal PCB-> top of box: 0.5-1.5 m

## Slide 11
Temperature zones
Heating Zone : 500mW/channel = 540 W
Crystals Zone : @ 18°+/-0,1°
External Zone : T° = 22°c

## Slide 12
Temperature control: back side
Heating electronic Zone : 500mW/channel = 540 W
Heating zone cooled with 2 heat exchangers 6320G3SB (Lytron)
+ funs + 1 chiller Kodiac RC006G03BG3
Crystals Zone : @ 18°+/-0,1°
Heat exchangers & chiller procured
Same manufacturer than the ones used for HyCal
Higher heat load specification

## Slide 13
Temperature control: crystals
Crystals Zone : @ 18°+/-0,1°
Foam : thermal insulator
4 copper plates around + 1 intermediate copper plate + 1 other chiller ( cooling separated from backward zone)

## Slide 14
Calibration and curing
glue
grease
1 blue LED per channel (onto the PCB board)
Pulsed mode for calibration
Continuous mode for curing
Light through 800 mm diameter silicate fiber (radiation hard)

## Slide 15
Irradiation and curing tests

## Slide 16
Summary and outlook

## Slide 17
Back-up

## Slide 18
1% constant term added to
simulation (miscalibration, etc)