## Slide 1
Field Programmable Gate Array
Michael S. Goodrich, Ph.D.
Staff Scientist
Experimental Physics Scientific Compute Infrastructure
November 5, 2021
(FPGA)

## Slide 2
What’s an FPGA?
Under The Hood
Programming an FPGA
What’s an FPGA Good For?
Overview

## Slide 3
Field → In-Service; “Fielded”
Programmable → Configurable Digital Circuit
Gates
  Configurable Logic Blocks (CLBs)
    AND, OR, LATCHs, FlipFlops, etc
    Memories, DSPs, CPUs, AI/ML, …
  Programmable Switch Matrices (PSMs)
Array→ Regular Arrangement of Logic Gates
What’s an FPGA?

## Slide 4
→
What’s an FPGA?
FPGA = CLBs + PSMs

## Slide 5
Programmable Switch Matrices (PSMs):
Dynamic Configurations – special memory loaded with bit patterns that control inputs to CLBs via PSMs.

## Slide 6
FPGA Architecture
I/O Cont
RAMs: Multiported, FIFOs,
DMA
PUs: ARM, DSP, NPU, ALUs
Clocks: PLLs
AI/ML

## Slide 7
Programming (RTL)
Verilog module:
Module smpl_crct(A,B,C,x,y);
input A,B,C;
output x,y;
wire e;
and g1(e,A,B);
not g2(y,C);
or g3(x,e,Y);
Endmodule;
Design Circuit
Verilog Simulation – validate logic design
Synthesis – Translate design to bit patterns that program PSMs for connections to CLBs in a Resource Efficient Manner.

## Slide 8
High Level Synthesis (HLS):
C like syntax:
A[i] = B[i] * C[i];
D[i] = B[i] * E[i];
F[i] = A[i] + D[i];
Pipelining
Parallelization
Interval
Latency
Parallelization
Interval
Latency
Pipelining?
Interval, Latency
Parallelization

## Slide 9
High Level Synthesis (HLS):
Verilog Design:
HLS Design:

## Slide 10
FPGA Use Cases

## Slide 11
Current Project
Experiment Edge Compute
Data Center
FPGA
Data
Center
Traffic
Shaper
Edge
Data
Source
AI
Steering
System
FPGA
Edge
Data
Shaper
Telemetry
Telemetry
Steering

## Slide 12
Questions?

## Slide 13
Current Project

## Slide 14
FPGA Architecture
I/O Cont
RAMs: Multiported, FIFOs,
DMA
PUs: ARM, DSP, NPU, ALUs
Clocks: PLLs
AI/ML

## Slide 15
100 GBS streaming UDP data from Accelerator
Destination = FPGA
Current Project

## Slide 16
Integration: I/O, Proc, Rams, DSPs, ARMs, ...
Flexibility: Digital Chameleon
Time To Market: COTS
Low Obsolescence: Components
Less Power Than CPU based Solution
Parallel Execution at Hardware Speeds
FPGA Benefits

## Slide 17
Excel at Simple Data Intensive Problems
Move Compute to Data
Flexibility > Custom Circuit or ASIC
No Economies of Scale (otherwise ASIC)
FPGA Use Cases

## Slide 18
Engineering Costs < Custom Circuit
Flexibility > Custom Circuit or ASIC
No Economies of Scale (otherwise ASIC)
Less Power Than CPU
FPGA Pro / Con

## Slide 19
FPGA Architecture

## Slide 20
Dynamic Configuration
Programming – special memory loaded with bit patterns that control inputs to CLBs via PSMs.

## Slide 21
More on Programming

## Slide 22
More on CLBs

## Slide 23
• Real 6-input look-up table (LUT)
• Dual LUT5 (5-input LUT) option
• Distributed Memory and Shift Registers
• carry logic for arithmetic functions
• Wide multiplexers for efficient utilization
  Configurable Logic Blocks (CLBs)

## Slide 24
Logic → MUXs, LUTs
Static Memory → Flip-Flops (D-FF)
‘Wires’ → Gates Connecting Logic/Memories
Programming→ bit patterns that setup inputs to LUTs and ‘wire’ connections
Under the Hood

## Slide 25
Cost
Energy
Data Base Accelerator
Generic Device
FPGA Use Cases

## Slide 26
Custom H/W (Versus S/W) → FW
Network Accelerator
Data Base Accelerator
Generic Device
FPGA Use Cases

## Slide 27
Compute Accelerator
Network Accelerator
Data Base Accelerator
Generic Device
FPGA Use Cases

## Slide 28
More on ‘Wires’
Programming – special memory loaded with bit patterns that construct and control inputs to CLBs via ‘Wires’.

## Slide 29
More on CLBs

## Slide 30
Module1 → Read Inputs (Parallel)
Module2 → Buffer Inputs (Parallel)
Module3 → Process Inputs (Parallel)
Module4 → Format Display Inputs (Parallel)
The only delay comes from the switching delays of the transistors in the chip, which are incredibly small
Parallel / Pipelined Design

## Slide 31
Gates → Combined Transistors (N/P Types)
“Wires” →
Primitive → AND, OR, XOR, NAND, NOR, XNOR, Latch
Mid → FF, LUT, MUX
High→ LUT
More on Gates

## Slide 32
COTS: more flexible than legacy hardware
data processing now on commodity servers
common Sub system for FE electronics
meets ATLAS requirements with margin
performance tests show ready for deployment
Summary