## Slide 1: Introduction to the tritium target design Roy J. Holt
Tritium Target Review
Jefferson Lab, Newport News
15 September 2015

## Slide 2: JLab 3He & 3H Measurements
E12-06-118: Marathon d/u ratios from 3H(e,e’)/3He(e,e’) DIS measurements
E12-11-112: x>1 measurements of correlations
E12-14-009: elastic: 3H – 3He charge radius difference [3H “neutron skin”]
E12-14-011: Nucleon Momentum Distributions in A = 3 Asymmetric Nuclei
Thermo-mechanical design of a static gas target for electron accelerators
B. Brajuskovic et al., NIM A 729 (2013) 469

## Slide 3: Tritium Gas Targets at Electron Accelerators
Lab | Year | Quantity (kCi) | Thickness (g/cm2) | Current (mA) | Current x thickness (mA-g/cm2)
Stanford | 1963 | 25 | 0.8 | 0.5 | 0.4
MIT-Bates | 1982 | 180 | 0.3 | 20 | 6.0
Saskatoon | 1985 | 3 | 0.02 | 30 | 0.6
JLab | (2016) | 1 | 0.08 | 20 | 1.6
JLab Luminosity ~ 2.0 x 1036 tritons/cm2/s
Large acceptance spectrometers at JLab

## Slide 4: Design Criteria
Gas targets for accurate comparison of 3He and 3H
Minimize risk in terms of pressure, Curies, beam current, days of operation, on/off cycles ( 0.9-2.0 kCi and 15-24 mA)
Detailed thermo-mechanical design of the target cell including FEA
3He, 2H2 and H2 targets at more than twice the pressure of the 3H2 target (500 psi/200 psi)
Minimize tritium handling at JLab – fill/decommission offsite
Completely sealed cell design
Secondary containment – isolated scattering chamber
Handling hut and ventilation system
Tritium, vacuum, temperature, raster, coolant monitors/interlocks
The target cell can be safely used with all required target gases:
3H2, 3He, 2H2, H2 and Ar

## Slide 5: Tritium Gas Target Safety Algorithm for JLab
Risk = Sp RiskP
RiskP = (1 – exp(-P/CP))exp(P/CP),

## Slide 6: Risk vs. Beam current
Relative risk vs. beam current when target is 1000 Ci. The optimum current is 21 mA. This assumes that the high risk value for time is 365 days.

## Slide 7: Tritium target technical reports
Hall A Tritium Target System, D. Meekins et al, September, 2015
A Tritium Gas Target for Jefferson Lab, R. J. Holt et al, July 13, 2015.
Jefferson Lab Tritium Target Cell, D. Meekins, November 28, 2014
Activation of a Tritium Target Cell, G. Kharashvili , June 25, 2014
Thermomechanical Design of a Static Gas Target for Electron Accelerators, B. Brajuskovic et al., NIM A 729 (2013) 469.
Absorption Risks for a Tritium Gas Target at Jefferson Lab, R. J. Holt, August 13, 2013.
Beam-Induced and Tritium-Assisted Embrittlement of the Target Cell at JLab, R. E. Ricker (NIST), R. J. Holt, D. Meekins, B. Somerday (Sandia), March 4, 2013.
Activation Analysis of a Tritium Target Cell for Jefferson Lab, R. J. Holt, D. Meekins, Oct. 23, 2012.
Tritium Inhalation Risks for a Tritium Gas Target at Jefferson Lab, R. J. Holt, October 10, 2012.
Tritium Permeability of the Al Target Cell, R. J. Holt, R. E. Ricker (NIST), D. Meekins, July 10, 2012.
Scattering Chamber Isolation for the JLab Tritium Target, T. O’Connor, March 29, 2012.
Hydrogen Getter System for the JLab Tritium Target, T. O’Connor, W. Korsch, February 16, 2012.
Tritium Gas Target Safety Operations Algorithm for Jefferson Lab, R. J. Holt, February 2, 2012.
Tritium Gas Target Hazard Analysis for Jefferson Lab, E. Beise et al, January 18, 2012.
Analysis of a Tritium Target Release at Jefferson Lab, B. Napier (PNNL), R. J. Holt, January 10, 2012.
Estimating the X-ray Dose Rate from the MARATHON Tritium Target, J. Singh, February 22, 2011.
Task force: R. J. Holt, A. Katramatou, W. Korsch, D. Meekins, T. O’Connor, G. Petratos, R. Ransome,
J. Singh, P. Solvignon, B. Wojtsekhowki

## Slide 8: Static gas target density and energy loss
J. Gorres et al, NIM 177 (1980) 177
H. Yamaguchi et al, NIM A589(2008) 150
Threshold for density fluctuations
10 mW/mm
Lab | Year | Quantity (kCi) | Thickness (g/cm2) | Current (mA) | Power loss (mW/mm)
Stanford HEPL | 1963 | 25 | 0.8 | 0.5 | 3.2
MIT-Bates | 1982 | 180 | 0.3 | 20 | 47.7
SAL | 1985 | 3 | 0.02 | 30 | 4.8
JLab | (2016) | 1 | 0.08 | 20 | 12.7
Density vs. current scan will be performed for the targets.

## Slide 9: JLab Tritium Target
Thin Al windows
  Beam entrance: 0.010”
  Beam exit: 0.011”
  Side windows: 0.018”
  25 cm long cell at ~200 psi T2 gas
Tritium cell filled and sealed at Savannah River (SRTE)
  Pressure: accuracy to <1%,
  Purity: 99.8% T2 gas, main contaminants are 3He and D2
  12.32 y half-life: after 1 year ~5% of 3H decayed to 3He
Administrative current limit: 20 mA
Design Authority and Project Manager: Dave Meekins

## Slide 10: Summary
Experiments with 3H at JLab can safely provide:
  First DIS measurements
  First x > 1 measurements
  First (e,e’p) measurements
  First precision charge radius measurements
  First …..
Textbook physics experiments – benchmark data

## Slide 11: Extra slides

## Slide 12: E12-10-103: DIS kinematics with an HRS (simulation)
P. Solvignon
11 GeV, 23.4 deg.
10 atm 3H, 20 atm 3He
0.018” Al windows
Present design:
13.6 atm 3H, 30 atm 3He
0.010” upstream window
0.011” downstream window
Target luminosity comparable
to window luminosity
BB at larger angles
BB comparable z_targ resolution
Al windows
3He
3H
Target_z (m)

## Slide 13: E12-11-112: x>1 kinematics with an HRS (simulation)
P. Solvignon
Worst case- other cases are:
  larger angles (larger
  window separation)
  higher energies (better
  resolution)
  Lower x (larger cross section)
4.4 GeV, 17.0 deg, p=3.98 GeV
13.6 atm 3H
0.010” Al upstream window
0.011” downstream window
Al windows
3H
Target_z (m)

## Slide 14: E12-14-009: Elastic scattering from A=3 nuclei

## Slide 15: Beam and Tritium-assisted Embrittlement
Beam-induced corrosion of Al, threshold at 180 K
  Beam dissociates hydrogen molecules into atoms – atomic fraction = 10 ppm
  Cryo-cool target when beam is on – keep windows below 180 K.
  H. M. Flower, “Electron Irradiation Induced Aqueous Corrosion of Aluminum and Magnesium,” Radiation Effects 33 (1977) 173; G. Bond et al., Scripta Metallurgica 20 (1986) 653.
Tritium-assisted embrittlement of Al
  Swelling threshold = 0.0045 He/Al
  Tritium diffusion into cell for one year -> 3He/Al = 1.8E-10
  M. R. Louthan, “Aluminum-Lithium Technology and Savannah River’s Contribution to Understanding Hydrogen Effects in Metals,” WSRC-2000-00061

## Slide 16: Special issues for tritium
Tritium permeation through Al (J. Scully et al, Mat. Sci. For. 331-337 (2000) 1583)
  nAl = 6E22 cm-3, CH=1.6E-11, D=2.3E-7 cm2/s, J=nAlCHD/d
  Ambient temperature -> 142 mCi in one year, diffusion; 371mCi/y for seals and valve
X-rays from the target cell (J. Singh)
  18.6 keV beta endpoint -> < 3.6 mrem/hr/cm2 at window surfaces
Radiation damage of target cell
  105-106 orders of magnitude – Al cells routinely used for target cells
Hydrogen embrittlement of the target cell
  7000 series Al tested at Sandia up to 15000 psi, target at 200 psi (B. Somerday)
Energy stored in pressurized gas cell (JLab ESH 6151 Appendix T4)
  125 and 250 J ~ to polarized 3He target
Chemical energy in the gas cell
  ~0.4 liters STP, 17 kJ, strongly diluted in scatt. chamber or Hall, 10 ppb
  ~1E-4 of hydrogen gas in standard cryotargets
Activation of the Al target cell (7075)
  Target windows: 1.7 mR/hr; after 2 days: 0.07mR/hr @ 1 m
Full tritium release in Hall A
  0.2 mrem/hour for a worker

## Slide 17: Secondary Containment – scattering chamber
May 30, 2012 meeting -> Use BB scattering chamber
Completely isolated from beam line
  Water cooled isolation windows
  Rad-hard RGA’s to detect tritium
  Activated getter pump
  Ventilation system with stack (design?)
T. O’Connor

## Slide 18: Contamination of scattering chamber?
10,000 dpm actionable limit not exceeded if 250 l/s speed is available within 1 second of losing the primary containment.
Two 1000 l/s turbos on chamber,
vented to stack
>100 l/s NEG pump available
Ai = ApolyTi
where Apoly is the absorption rate in CH2, and Ti is the time at step i. The pump with speed, S,
is turned on after delay Td, the absorption rate is given by:
Ai = Ai-1 + Apolyexp(-(Ti-Td)/(VC/S))

## Slide 19: Stack height and maximum dose
Stack height (m) | Dose at 300 m 600 Ci (mrem) | Distance at max dose (m) | Max dose 600 Ci (mrem) | Max dose 1000 Ci (mrem)
0 | 160 | <100 | 890 | 1483
5 | 54 | 200 | 67 | 112
10 | 6.5 | 500 | 9.7 | 16
15 | 0.28 | 750 | 3.2 | 5.3
20 | 0.0036 | 1000 | 1.4 | 2.3
HotSpot calculations by
Bruce Napier, Pacific Northwest National Lab
Assumptions: 100% HTO, 60 minute sampling time, class F weather (minimal dispersion)

## Slide 20: Dose vs. distance for a 20 m stack (600 Ci, 100% HTO, class F weather, 60 min sampling time)

## Slide 21: Algorithm for number of days and beam trips
The total number of days for experiments is 61 at 1000 Ci and 25 mA:
ndays = (61 days)(1000 Ci)(25 mA)/((nci)(ib))
where nci = no. of Ci and ib = beam current.
Cycling risk (beam trips):
Riskcyc = (1 – exp(-ncyc/cychi))exp(ncyc/cychi)exp(press/presshi)exp(ib/ibhi),
Where ncyc = no. of cycles and press = gas pressure.

## Slide 22: Risk vs. Target Activity
Relative risk vs. curies when the beam current is 21 mA. The optimum target activity is 1350 Ci. This assumes that the high risk time is 365 days.

## Slide 23: F2n/F2p, d/u ratios and A1 for x→1
 | F2n/F2p | d/u | A1n | A1p
SU(6) | 2/3 | 1/2 | 0 | 5/9
Diquark/Feynman | 1/4 | 0 | 1 | 1
Quark Model/Isgur | 1/4 | 0 | 1 | 1
Perturbative QCD | 3/7 | 1/5 | 1 | 1
Dyson-Schwinger | 0.49 | 0.28 | 0.17 | 0.59
C. D. Roberts, RJH, S. Schmidt, PLB 727 (2014) 249

## Slide 24: Present status: Neutron to proton structure function ratio
C. D. Roberts, RJH, S. Schmidt, PLB 727(2013) 249;
RJH, C. D. Roberts, RMP 82 (2010) 2991

## Slide 25: High x impacts high energy physics
Accardi, Mod. Phys. Lett. A28 (2013) 35; arXiv 1308.2906v2
W charge asymmetry vs. W rapidity
High x and low Q2 evolves to low x and high Q2

## Slide 26: From three-body nuclei to the quarks
Parton model ->
Mirror symmetry of A=3 nuclei
  Extract F2n/F2p from ratio of measured 3He/3H structure functions
R = Ratio of “EMC ratios” for 3He and 3H
Relies only on difference in nuclear effects
Calculated to within 1.5%
Most systematic, theory uncertainties cancel
  JLab E12-06-118: Marathon
G. Petratos, RJH, R. Ransome, J. Gomez

## Slide 27: A look at quarks in the nucleus: the EMC effect
EMC effect discovered 1982 (H. Montgomery et al.), remains a mystery today
Scattering from quarks in a nucleus is not just a superposition of scattering from quarks in nucleons
  Dependence on nuclear density, short range correlations, flavor, spin, isospin?
SLAC E-139, 1984, J. Gomez et al.
J. Seeley et al, PRL 103 (2009)

## Slide 28: Isospin structure of 2N-SRCs (JLab E12-11-112)
3He/3H is simplest asymmetric case:
Simple estimates for 2N-SRC
Isospin independent
Full n-p dominance (no T=1)
40% difference between full isosinglet dominance and isospin independent
Few body calculations [M. Sargisan, Wiringa/Peiper (GFMC)] predict n-p dominance, but with sizeable contribution from T=1 pairs
Goal is to measure 3He/3H ratio in 2N-SRC region with 1.5% precision
   Extract R(T=1/T=0) with uncertainty of 3.8%
Extract R(T=1/T=0) with factor of two improvement over previous triple-coincidence, smaller FSI
P. Solvignon, J. Arrington, D. Day, D. Higinbotham

## Slide 29: 3He(e,e’p)/3H(e,e’p)
arXiv:1409.1717
JLab E12-14-011 Proton and Neutron Momentum Distributions in A = 3 Asymmetric Nuclei
3He/3H ratio for proton knockout yields n/p ratio in 3H
np-dominance at high-Pm implies n/p ratio  1
n/p at low Pm enhanced
No neutron detection required
L. Weinstein, O.Hen,
W. Boeglin, S. Gilad

## Slide 30: Charge radii: 3He and 3H
With new tritium target -> improve precision on DRRMS by factor 3-5 over SACLAY results
First opportunity for 3H at JLab (E12-14-009)
Precise theoretical calculations of <r2rms>3H, <r2rms>3He
Experimental results: large uncertainties, discrepancies
 | <r2rms>3H | <r2rms>3He
GFMC | 1.77(1) | 1.97(1)
EFT | 1.756(6) | 1.962(4)
SACLAY | 1.76(9) | 1.96(3)
BATES | 1.68(3) | 1.87(3)
Atomic | -------- | 1.959(4)
DRRMS = 0.20(10)
DRRMS = 0.19(04)
L. Meyers, J. Arrington, D. Higinbotham