## Slide 1
Hall A coordinators system
Offset from detector misspoint, beam, and target
Bulleyes scan for beam convention
Angle and vertex calibration Gmp optics data Oct, 2016
Tritium Weekly meeting Nov/28/2016
Dien Nguyen

## Slide 2
1.1 Hall Coordinators system: (HCS)
Zlab
Xlab
Beam
Ylab:
X: positive : Left
X: negative : right
Z: positive: Downstream
Z: Negative: upstream
Y: positive: up
Y: negative: Down

## Slide 3
1.2 Target coordinators system for Both arms Ideal case
Zlab
Xlab
Floor marks
HC
LHRS
Ztg
Ytg
Zlab
Xlab
HC
Ytg
Ztg
RHRS
LHRS: Convention
Ztg: positive: Downstream
Ztg: negative : Upstream
Ytg: positive: Upstream
Ytg: Negative: Downstream
Xtg: positive: pointing down
RHRS : Convention
Ztg : positive: Downstream
Ztg: negative: upstream
Ytg: positive: Downstream
Ytg: negative: upstream
Xtg: positive: pointing down

## Slide 4
2. Offset in Ytg from spectromispoint, beam offset, target offset LHRS
a. Spectromisspoint
Zlab
Xlab
Floor marks
Specoff
HC
ytg
b. Beam offset
Ytg
Zlab
Xlab
Floor marks
HC
xbeam
Ytg
c. Target offset
Ytg
Zlab
Xlab
Floor marks
HC
Ytg
Tg_off
Offset convention:
Specoff: + : upstream - : downstream
Xbeam: + :Left - : Right (HCS)
Tg_off: + : downstream - : upstream (HCS)
Ytg = - specoff - Tg_off *sin + xbeam* cos
=> Expected value for Ytg :

## Slide 5
3. Bulleyes Scan for beam convention
Run3882 Nominal beam
BPMA: X = 0.689 mm
BPMB: X = -1.5 mm
Ytg ~ -0.9 mm
Run3880: Xbeam +1mm
BPMA: X = 1.48 mm
BPMB: X = -0.57 mm
Ytg ~ -1.8 mm
Run3881: Xbeam -1mm
BPMA: X = -0.12 mm
BPMB: X = -2.49 mm
Ytg ~ 0
We keep everything the same accept Xbeam changed : if follow hall convention for beam:
Ytg(3880) = Ytg(3882) +Delta_X *cos (theta) here theta = 25
=>Delta_X ~ -1 mm This is opposite to BPM convention

## Slide 6
3. GMP optics data Oct 2016 for RHRS
Run Number for angle and vertex calibration:
22828, 22829, 22830, 22831, 22832, 22833, 22834.
2. Kinematic setting:
Angle : 48.75 , Ebeam = 2.217 GeV, P0 = 1 GeV, Sieve in
3. Target: Multiple carbon foils:
9 foils cover 20 cm along the beam -10cm ->10cm
4. Sieve:
New Sieve 26 rows, 7 columns
5. Optics matrix:
Initial optics data base: GmP spring 2016

## Slide 7
Sieve plots Using the Initial optics matrix

## Slide 8
Vertex plot using initial optics Matrix

## Slide 9
Angle Calibration: after optimization

## Slide 10
Vertex calibration: After optimization

## Slide 11
Discussion:
Next step: finish Dp calibration in RHRS
Take a look at the LHRS optics as well
Testing the optics: ->Need some suggestion about what can be test to make sure the optics is good