Tritium Elastic Sieve Energy Loss
Scott Barcus
4/25/17

---
Introduction
- Experiment E12-14-009 requires a special sieve to be constructed to keep rates acceptable.
- Goal is to knock electrons incident on plate out of momentum acceptance.
- HRS momentum acceptance is -4.5% < δp/p < 4.5%.
  - Elhrs=1070 MeV → Emin=1021.85 MeV
  - E0=1100MeV → 7.1% energy loss.

---
Theory
- At energies above a few tens of MeV Bethe-Bloch collisional losses are minimal and Bremsstrahlung dominates.
- Bremsstrahlung loss depends of E0 and electric field the electron experiences.
  - Cross section: E0, impact parameter and Z.
- Screening of the nucleus by electrons:
  - If mec2 << E0 << 137mec2Z-1/3 →ζ>>1→ no screening.
  - If E0 >> 137mec2Z-1/3 →ζ~0 → complete screening.
  - Al = 29.77 and W = 16.67 → complete screening.

---
Energy Loss Calculation
- Cross section for complete screening (Leo):
- Radiative energy loss can be found by integrating the cross section times the photon energy over the allowable energy range of the emitted photons.

---
Energy Loss Calculation Cont.
- This can be rewritten as:
- In the case of complete screening we have:
- Here f(Z) is a Coulomb correction with a=Z/137:

---
Calculation Check
- Plot (1/ρ)(dE/dx) from Bremsstrahlung for Cu.
  - Good agreement (low energy has no screening).

---
Results
- Proposed materials for sieve plate are Al and W.
- Фrad depends only on material.
- Must also multiply dE/dx by material thickness (length*density).

---
Energy Loss of Al and W dE/dx

---
Energy Loss Radiation Length Al and W
- Collisional losses dominate as energy is lost.
- 1 radiation length leave 1/e energy.

---
Conclusion/Future Work
- As expected tungsten depletes the electrons of energy faster than aluminum.
- Current proposal calls for a 0.5 cm thick tungsten plate which seems reasonable.
- Need to determine standard stock thicknesses to minimize machining costs.
- Need to determine plate size for current holder.

---
References
- Alcorn, J et al. (2004). Basic Instrumentation for Hall A at Jefferson Lab. Nuclear Instruments and Methods A522: 294-346.
- Groom, Don. "Atomic and Nuclear Properties of Materials for More than 300 Materials." AtomicNuclearProperties. Particle Data Group, 23 Sept. 2016. Web. 20 Apr. 2017. <http://pdg.lbl.gov/2016/AtomicNuclearProperties/>.
- Leo, William R. “2.4 Energy Loss of Electrons and Positrons.” Techniques for Nuclear and Particle Physics Experiments: A How-to Approach. 2nd ed. Berlin: Springer, 1992. N. pag. Print.
- L S Myers, D. W. Higinbotham, J. R. Arrington. (Aug. 22, 2014). E12-14-009: Ratio of the electric form factor in the mirror nuclei 3He and 3H http://arxiv.org/pdf/1408.5283.pdf